## Slide 1: MRAD 251: CT Theory 1
Outcome 3:
Analyze components of image formation and appearances

## Slide 2: Objectives
1.
2.
Apply terminology specific to CT
Summarize the parameters that operators have at their disposal
when manipulating image appearance
3.
4.
5.
Summarize the use of windowing in CT image display Describe CT image post-processing tools
Describe the different types of image reconstruction used in CT
3.6 Explain the concepts of maximum intensity
projection (MIP),
multiplanar reconstruction (MPR) and three dimensional (3D) imaging
3.7 Identify common CT image artifacts

## Slide 3: Recap: CT Image Display
Image acquisition, and image reconstruction affect image display.
Displayed images are assessed based on the concept of image quality
  An images diagnostic capability
  Aka. Image fidelity/image accuracy
Images should be free of unnecessary artifacts and distortion
Images with poor image quality should be repeated, and omitted from image archiving

## Slide 4: Objectives 3.1 & 3.2
The ability to accurately depict a scanned object can be organized into three main categories:
Temporal resolution
Spatial/Detail resolution
Contrast resolution
Image resolution is affected by a variety of factors, organized into two general sub-categories:
  Controlled
    Example: Scan parameters
  Uncontrolled
    Example: Involuntary movement

## Slide 5: Temporal Resolution
The speed at which data can be acquired. Controlled by:
Gantry rotation speed
  Length of time required for the x-ray tube to complete one full rotation
    Aka. ; typical scan times:
      0.5→2 seconds for routine imaging
0.35→0.45 seconds for cardiac imaging
Number of detectors
DAS speed
Improves image quality when imaging moving structures

## Slide 6: Spatial Resolution
Ability of a scanner to display two objects that are close together, as separate objects.
Inferior to conventional radiography
Measured in lp/mm or lp/cm
  Measurement values must be consistent
Note: an objects spatial frequency affects its image quality
Determined by:
  Direct measure
  MTF calculations

## Slide 7: Modulation Transfer Function
A ratio of image accuracy in comparison to the actual object scanned.
Measured using a scale of 0→1
  Objective evaluation
A graphical representation, depicting a CT scanners resolution capabilities
  Spatial frequency & image quality have a non-linear relationship
•
  Used for equipment comparisons

## Slide 8: Contrast Resolution
Differentiating structures that vary only slightly in density.
CT has superior low-contrast resolution
  0.5% contrast variation detectability
    1% variation = 10HU difference
Subjective evaluation
  Windowing can improve low-contrast visibility
Affected by Image Noise

## Slide 9: Image Noise
Quantum Mottle results from underexposures and affects image contrast
Burnout is caused by extreme over-exposures, decreasing image contrast
Factors that affect mAs in CT are similar to general radiography:
  Reciprocity Law
    mA x s (time, in seconds) = mAs
  Tissue thickness & Density
  mAs is easier to manipulate & predict vs kVp

## Slide 10: mAs/Dose
CT systems typically possess two filaments (that produce electrons), which are used to create photons.
Small filament = small focal spot size
  Increases spatial resolution
Large filament = large focal spot size
  Used for higher mA settings (˃350)
Typical range = 20→800mA

## Slide 11: mAs/Dose Considerations
Dose and image quality are not directly related in CT, due to the digital nature of the imaging process.
Aka. The Uncoupling Effect
  Similar to automatic rescaling
    Computer processes images to improve image quality (example: unable to visually
detect over-exposures)
  *Quantum Mottle is unaffected by this effect
Automatic Tube Current Modulation (ATCM)
  Balances dose & image quality
  Can reduce patient dose by 15→40%
  Uses a fixed kVp
    mAs automatically adjusts for patient size and weight

## Slide 12: Scan Parameters
Tube Voltage
Typical settings:
  120→140kVp for adult patients (selection dependent on patient body habitus)
    Most common = 120kVp
  80kVp for pediatric patients
General Rules:
  Higher kVp settings increase photon penetrability
  kVp affects contrast, due to its relationship with scatter production

## Slide 13: Scan Parameters
Pitch
Affects:
  Effective slice thickness
    More pronounced in SDCT
  Image Quality (due to interpolation)
(Acquisition) Slice Thickness
↑ slice thickness = ↓image quality
  Primarily caused by: Partial Volume Averaging
Affects:
  SNR
  Contrast & Detail

## Slide 14: Scan Parameters
DFOV
Determines amount of raw data used for reformatting
  Affects Spatial resolution
Pixel size determines accuracy of objects imaged
  Affects Contrast & Detail
Matrix size controls pixel size
  512x512 common in CT
Pixel Size =
DFOV
Matrix Size

## Slide 15: Scan Parameters
Reconstruction algorithms
Raw data manipulation
Improves image quality
  Algorithms that ↑spatial resolution ↓contrast
    Example: Bone/Edge enhancement
  Algorithms that ↑contrast resolution ↓detail
    Example: Smoothing/Soft-tissue enhancement

## Slide 16: Objective 3.3
Windowing
Manipulates contrast resolution
  Wide WW = ↓low-contrast detectability
    Example: bone
  Narrow WW = ↑low-contrast detectability
    Example: brain tissue

## Slide 17: Objective 3.4
CT Post-processing can be divided into three main categories:
Basic Functions
*Retrospective Reconstruction
Reformatting

## Slide 18: 1. Basic Functions
Windowing:
Most common
Distance Measurements:
Determine size of pathology
Grids are also used:
  For distance
  Act as guides for needle placement/treatment
Image Annotation:
Words, arrows etc.
(Image display) Communication
Multiple Image Display:
Viewing more than one image simultaneously

## Slide 19: 1. Basic Functions
Reference Image:
Used for anatomical reference
Image Magnification:
≠ DFOV
Applies to Image data
Helps with accuracy of pathology measurements
Histogram Display:
Graph demonstrating how often (in the image) CT numbers occur, within a specified ROI

## Slide 20: 2. Retrospective Reconstruction
Uses RAW data to create new images
  Same plane as acquisition images
The following parameters can be changed:
  DFOV
  Image Center
  Reconstruction Algorithms
Changing the parameters retrospectively, can enable/improve image reformatting

## Slide 21: Objective 3.5
Retrospective Slice Thickness
MDCT
  Techs can retrospectively combine slices in different ways to create thicker image slices
    Thicker slices for reformatting:
      Require less computer storage space
Overlapping Reconstructions
  Improves 2D & 3D reformatted image quality
    Creates “thinner” image slices to ↓reformatting artifacts
  Not required if the voxel is at/near isotropic
    When DFOV & slice thickness are small

## Slide 22: 3. Reformatting
Uses IMAGE data
  Improves display of anatomic relationships
Reformats require an identical:
  DFOV
  Image Center
  Gantry Tilt
  Contiguous slices
Motion degrades quality of reformat

## Slide 23: Objective 3.6
Reformats are either:
2D
  Example: MPR
3D
  Examples:
    MIP
    MinIP
    SR
    VR

## Slide 24: Multiplanar Reformation (MPR)
Displays anatomy in various planes
  Transverse
  Coronal
  Sagittal
Oblique
Curved
Can be programmed for automatic generation
No additional dose to the patient required
Reformatted images maintain the original HU values as the acquisition images
Manual

## Slide 25: Maximum Intensity Projections (MIP)
Maximum Intensity Projections:
Voxel with the highest value is displayed
  Creates a high contrast image
High-attenuation structures
  Examples:
    Contrast filled vessels
    Bone

## Slide 26: Minimum Intensity Projections (MinIP)
Minimum Intensity Projections:
Lowest value is displayed
  Creating a high contrast image
Low-attenuation structures
  Example:
    Bronchial tree

## Slide 27: MIP & MinIP
Can be created using entire dataset or a select portion.
Sliding slab method:
  “Deletes” structures that are not of clinical interest
  Minimizes superimposition

## Slide 28: 3D Image Reformatting
Rendering adds lighting, texture & color to the 3D image
Original HU values not retained
Images can be rotated/tilted

## Slide 29: Surface Rendering
Aka. Shaded Surface Display
Mostly replaced with VR
Images are created using threshold CT values
  Voxels are excluded or included based on the threshold level
  Threshold value determines image accuracy
    Anatomy can be concealed
Uses 10% of data
  Displays the contour of an object
  All other voxels are excluded
Useful for surfaces of airways, colon & blood vessels

## Slide 30: Volume Rendering
3D semi-transparent image.
All voxels are used
  Examines internal & external structures
Displays multiple tissues & anatomical relationships
Used for Endoluminal Imaging
Pixels can be assigned a color, brightness, and an amount of transparency
  Attenuation based classification of structures

## Slide 31: Improving 3D Imaging
Segmentation
Aka. ROI Editing
  Removal of unwanted data for display purposes
    Manual or Automatic
  Improves visualization of area of interest
Errors
  Manual & Automatic
  Anatomy of interest is not displayed
    Can be impossible to identify
      Can exclude stenosis
      Can create false positives (mimic stenosis)

## Slide 32: Reformatting & Artifacts
Artifacts degrade reformatted images.
Most common:
  Motion
  Metal
  Asymmetrical Voxels
    Causing a “Stair-step” appearance

## Slide 33: Objective 3.7
Definition(s):
Appearance that is unrelated to the subject being studied
Any discrepancy between the HU values in the image & the true attenuation coefficients of the object
More likely to occur in CT imaging
3 general appearances:
•
•
•

## Slide 34: Things to Take Away
MTF
Uncoupling effect
Artifacts
Calculating Pixel Size
  Romans Clinical Application Box 6-1 pg. 67
Post-processing
  Main categories
    Including 2D & 3D reformats
  Overlapping reconstruction
    Romans Clinical Application Box 8-2 pg. 85
Segmentation