## Slide 1: MRAD 204:
Radiographic Technique 1
Outcome 1-5:
Positioning – Scapula & AC Joints
MRT Program
Anderson College

## Slide 2: Affiliated Readings
Module 5
Bontrager
Pg: 205
Pgs: 207→209

## Slide 3: Overview
Guidelines/Considerations
Protocol
Positioning
Evaluation Criteria

## Slide 4: Guidelines/Considerations – AC & Scapula
Identify required anatomy
  Note: scapula images do not require entire clavicle
Gowning instructions/Artifact removal
  Same as shoulder imaging
Select appropriate equipment/technical factors
Breathing instructions
Use external landmarks
  Same as shoulder and clavicle imaging

## Slide 5: Protocol – AC Joints
Routine:
AP without weights
AP with weights
Note: Both AC Joints must be imaged, however they are typically performed “one side at a time” using a 110cm SID

## Slide 6: Positioning –AP AC Joints w/o weights
Shoulders Relaxed, with arm in
neutral rotation
Image one AC joint at a time – centering one joint over the middle of the IR for each image
Collimate tightly (as per yellow outline)
Note: suspend respiration
Bontrager pg. 206 Fig. 5.90

## Slide 7
w/o weight
Evaluation criteria: “anatomy demonstrated”
Anatomical marker + w/o weight marker
One AC Joint per image
Acromion
Lateral End of Clavicle
Bontrager pg. 206 Fig. 5.90

## Slide 8: Positioning – AP AC Joints w/ weights Same position as AP w/o weights, except:
Place a weight on the patients wrist, keeping their shoulder relaxed
  *Tell patient to drop weights when
done
Image each AC joint separately
Collimate tightly (as per yellow outline)
Note: suspend respiration

## Slide 9
Evaluation criteria: “anatomy demonstrated”
Bontrager pg. 205 Fig. 5.88
w/ weight
Anatomical marker + w/ weight marker
One AC Joint per image
Acromion
Lateral End of Clavicle
w/ weight

## Slide 10: Protocol - Scapula
Routine:
AP
Lateral

## Slide 11: Positioning – AP Scapula
Bontrager pg. 207 Fig. 5.95
Abduct arm to 90o and extend
above head
Position top of collimated light
field 1” above top of the shoulder
CR to midscapular region
Place an anatomical marker (using
Anderson Marker Rules)
Note: suspend respiration

## Slide 12
Evaluation criteria: “anatomy demonstrated”
Bontrager pg. 207 Fig. 5.97
SAIT image library
Entire Scapula
AC Joint
~½ the Clavicle
Scapula
Shoulder

## Slide 13: Evaluation Criteria: “Position”
Lateral portion of scapula free of superimposition (from the ribs)
Optimal density and contrast
Bontrager pg. 207 Fig. 5.97

## Slide 14: Positioning – Lateral Scapula
Bontrager pg. 208 Fig. 5.99
Have patient reach across chest
and hold opposite shoulder
Same rotation as PA Scap Y
Place an anatomical marker (using Anderson Marker Rules), and make final adjustments
Note: suspend respiration

## Slide 15: Evaluation criteria: “anatomy demonstrated”
Bontrager pg. 208 Fig. 5.100
VS.
SAIT image library
Shoulder

## Slide 16: Evaluation Criteria: “Position”
As much as possible, the humerus should not superimpose the scapula
Optimal density and contrast
Bontrager pg. 208 Fig. 5.100