## Slide 1: MRAD 204: Radiographic Technique 1
Outcome 6-10:
Image Critique – Femur and Knee

## Slide 2: Affiliated Readings
Bontrager
Pgs: 246→250
Pgs: 278→280
Emphasis on the “pink box” Evaluation Criteria

## Slide 3: Overview
Image Critique – Femur
Image Critique – Knee
Tips & Tricks

## Slide 4: Image Critique – Femur
Anatomy
Ideally, routine Femur radiographs should display:
Entire Femur
Entire Hip & Knee joint
McQuillen Martensen 5th Ed. Pg.415 Fig. 6.256
At least 1-inch of proximal tib/fib
R
SAIT Image Critique Handbook
McQuillen Martensen 5th Ed. Pg.423 Fig. 6.270
R
R

## Slide 5: Image Critique – Femur
Routine AP Pelvic radiographs should display:
kVp range of 75→85
Optimal density and contrast:
  no motion (i.e. blur)
  soft tissue margins visible
  clear bony trabecular markings
Exposure & Technique
R
R

## Slide 6: Image Critique – Femur
Marker Placement &/or artifacts
No removable artifacts are visible
Marker placement: in the same anatomical location on both images in each projection, not obscuring bony anatomy
R
If unmoved between the two images of the AP projection:
Marker will display in the: superior lateral edge of the proximal image & inferior lateral edge of the distal image
If unmoved between the two images of the Lateral projection:
Marker will display in the: superior anterior edge of the proximal image & inferior anterior edge of the distal image

## Slide 7: Image Critique – AP Distal Femur
CR & Collimation
Four sided collimation with lengthwise crosshair centered over the femoral body
Notes:
Soft-tissues not required in their entirety; only bony anatomy is of interest

## Slide 8: Image Critique – AP Distal Femur
Position
@ 75 kVp
Femoral & tibial condyles symmetric in size and shape
Patella slightly closer to medial side of femur
Medial half of fibular head superimposed by tibia
Femur parallel to collimated light-field
*Knee joint not fully opened due to beam divergence
Bontrager pg. 278 Fig. 7.37

## Slide 9: Image Critique – AP Proximal Femur
R
CR & Collimation
Four sided collimation with lengthwise crosshair centered around the femoral body
SAIT Image Library & SAIT Campus 2021
Notes:
symphysis pubis not required
CR centering (proximal/distal) is dependent on the field size used
When only 1/3rd of the proximal femur is included, the CR should be near the femoral neck

## Slide 10: Image Critique – AP Proximal Femur
Position
@ 75 kVp
SAIT Image Library
Femoral head seen through the acetabulum
Femoral neck in profile
Greater trochanter in profile
Lesser trochanters barely seen (or not seen at all) on the medial side
Femur parallel to collimated light-field

## Slide 11: Image Critique – Lateral Distal Femur
R
CR & Collimation
Four sided collimation with lengthwise crosshair centered over the medial epicondyle of the femur
Notes:
Soft-tissues not required in their entirety; only bony anatomy is of interest
Bontrager pg. 279 Fig. 7.38

## Slide 12: Image Critique – Lateral Distal Femur
Position
@ 75 kVp
Aka. Inferior margins of femur not superimposed
Open patellofemoral joint space
Anterior margins of condyles superimposed
Distal margins of condyles not superimposed
*Closed knee joint, due to beam divergence

## Slide 13: Image Critique - Lateral Proximal Femur
R
CR & Collimation
Four sided collimation with lengthwise crosshair centered around the femoral body
McQuillen Martensen 5th Ed. Pg.423 Fig. 6.270
Notes:
CR centering (proximal/distal) is dependent on the field size used
When only 1/3rd of the proximal femur is included, the CR should be near the femoral neck

## Slide 14: Image Critique - Lateral Proximal Femur
Position
@ 75 kVp
Head of femur in the acetabulum
Femoral neck foreshortened and superimposed by the greater trochanter
Only a small part of lesser trochanter visible on the medial side
Femur parallel to collimated light-field
McQuillen Martensen 5th Ed. Pg.423 Fig. 6.270

## Slide 15: Image Critique – Routine Knee
Anatomy
Ideally, all routine Knee radiographs should display:
1/4 of proximal tib/fib
R
Distal femur
Entire patella

## Slide 16: Image Critique – Routine Knee
ALL routine hip radiographs should display:
kVp range of 65→80
Optimal density and contrast:
  no motion (i.e. blur)
  soft tissue margins visible
  clear bony trabecular markings
Exposure & Technique

## Slide 17: Image Critique – Routine Knee
Marker Placement &/or artifacts
No removable artifacts are visible
Marker placement, not obscuring soft-tissue:
AP, & Oblique projections: lateral edge of light-field
Lateral projection: anterior, inferior edge of light field

## Slide 18: Image Critique – Routine Knee
CR & Collimation
Four sided collimation centered to mid-knee joint
McQuillen Martensen 5th Ed. Pg.385 Fig. 6.187

## Slide 19: Image Critique – AP Knee
Position
@ 65 kVp
Open femorotibial joint space
Tibial plateaus seen with only minimal surface area
Intercondylar eminence centered at mid-femur (“side-side”)
Symmetric femoral and tibial condyles
~ ½ fibular head superimposed by tibia
Bontrager pg. 246 Fig. 6.101
R

## Slide 20: Image Critique: AP Internal Oblique Knee
Position
@ 65 kVp
R
~½ patella superimposing medial condyle of femur, and ~½ free of superimposition
Open proximal tibiofibular joint
  Aka. head and neck of fibula free of superimposition
Lateral condyle of femur & tibia in profile

## Slide 21: Image Critique: AP External Oblique Knee
Position
@ 65 kVp
R
SAIT MRT Image Critique Handbook
~½ patella superimposing lateral condyle of femur, and ~½ free of superimposition
Proximal fibula superimposing lateral half of tibia
  Fibular head aligned with “anterior edge” of tibia
Medial condyle of femur & tibia in profile

## Slide 22: Image Critique – Lateral Knee
Position
@ 65 kVp
R
Patella in profile
Posterior and distal margins of femoral condyles directly superimposed
Open Patellofemoral joint
Proximal tibiofibular joint slightly superimposed by posterior half of proximal tibia
SAIT MRT Image Critique Handbook
Note: Femur should be parallel to collimated light-field
Note: This image used to demonstrate all other “ideal” positioning criteria
McQuillen Martensen 5th Ed. pg. 385 Fig. 6.187

## Slide 23: Tips & Tricks – Femur Projections
Critique same way you would critique AP Hip, EXCEPT:
  “Symph” not required
  Femur requires a lower technique
  *If proximal femur is site of injury, the CR will not be centered over femoral neck
Proximal AP Femur Image:
@ 80 kVp
AP Proximal Femur
AP Hip
Bontrager pg. 288 Fig. 7.67
SAIT Image Library

## Slide 24: Tips & Tricks – Femur Projections
Critique same way you would critique Lateral Hip, EXCEPT:
  Only a small part of the lesser trochanter will be visible medially
  Femur requires a lower technique
  Femur must be parallel to edge of IR (i.e. no collimator tilt)
  *If proximal femur is site of injury, the CR will not be centered over femoral neck
Proximal Lateral Femur Image:
@ 80 kVp
Lateral Proximal Femur
Lateral Hip

## Slide 25: Tips & Tricks – Femur Projections
Critique same way you would critique AP & Lateral Knee projections EXCEPT:
  Femur requires a higher technique
  Knee joint will be superimposed in femur projections
  Lateral distal Femur: Femoral condyles will not be superimposed
Distal Femur Images:
@ 65 kVp
AP distal Femur
AP Knee
@ 65 kVp
Lateral Knee
Lateral distal Femur

## Slide 26: Tips & Tricks: Lateral Knee Projections
Adductor tubercle (yellow arrow): is it superimposed (on top of another structure)
Superimposition of fibula = under-rotation
Superimposition of fibula = over-rotation
https://i.pinimg.com/736x/3b/d5/83/3bd5833938cc85d55028ec1dbb9fb27e.jpg
Evaluate the Fibula & Adductor tubercle:

## Slide 27: Tips & Tricks: Lateral Knee Projections
NOT Superimposed inferiorly
NOT Superimposed anteriorly
If CR centering is accurate, but femoral condyles are:

## Slide 28: Tips & Tricks: External Oblique Knee
Internal rotation will demonstrate head of fibula closer to the lateral side of the tibia
Look at the overall appearance of the femoral condyles, patella, & the position of the fibular head in relation to the tibia:

## Slide 29: Tips & Tricks: Internal Oblique Knee
External rotation will demonstrate superimposition of the fibular head
Look at the overall appearance of the femoral condyles, patella, & the position of the fibular head in relation to the tibia:
SAIT MRT Image Critique Handbook
McQuillen Martensen 5th Ed. Fig. 6.162