## Slide 1: MRAD 204: Radiographic Technique 1
Outcome 6-10:
Image Critique – Ankle, Calcaneus, & Foot

## Slide 2: Affiliated Readings
Bontrager Reading
Pgs: 232→242
Emphasis on the “pink box” Evaluation Criteria

## Slide 3: Overview
Image Critique – Ankle
Image Critique – Calcaneus
Image Critique – Foot
Tips & Tricks

## Slide 4: Image Critique – Routine Ankle
Anatomy
Ideally, routine Ankle radiographs should display:
Entire Ankle Joint
Distal 1/3rd of tibia & fibula
Talus
Lateral & medial malleoli
Lateral projection must also display the entire calcaneus, navicular and base of 5th metatarsal

## Slide 5: Image Critique – Routine Ankle
All Routine Ankle radiographs should display:
kVp range of 60→75
Optimal density and contrast:
  no motion (i.e. blur)
  soft tissue margins visible
  clear bony trabecular markings
Exposure & Technique
R
R

## Slide 6: Image Critique – Routine Ankle
Marker Placement &/or artifacts
No removable artifacts are visible
Marker placement: not obscuring soft-tissue anatomy
AP & Mortise = Lateral side
Lateral = Anterior side (“walking” on the foot)
R

## Slide 7: Image Critique – Routine Ankle
CR & Collimation
Four sided collimation centered over the Tibiotalar joint (aka. ankle joint)
Note: Ankle joint is NOT the center of required anatomy
Bontrager pg. 239 & 240 Fig. 6.78 & 6.81

## Slide 8: Image Critique – AP Ankle
Position
@ 60 kVp
Bontrager pg. 239 Fig. 6.79
Distal Tib/Fib parallel to length of IR
Open tibiotalar joint
Open medial mortise joint
Closed lateral mortise joint
  Slight superimposition of distal tibia, fibula, and talus

## Slide 9: Image Critique – AP Mortise Ankle
Position
@ 60 kVp
Bontrager pg. 240 Fig. 6.82
Open medial mortise joint
Open lateral mortise joint
Malleoli in profile
Slight superimposition of distal tibiofibular joint

## Slide 10: Image Critique – Lateral Ankle
Position
@ 60 kVp
Talus and calcaneus in profile
Distal fibula superimposed over posterior ½ of tibia
Open tibiotalar joint
  Superimposed talar domes

## Slide 11: Image Critique – Routine Calcaneus
Anatomy
Ideally, routine Os Calcis radiographs should display:
Entire Calcaneus
Base of 5th metatarsal
Talocalcaneal joint
Lateral projection must also display ~1 inch of distal Tib/fib, and navicular
Soft-tissues
McQuillen Martensen 5th Ed. pg. 334 Fig. 6.68

## Slide 12: Image Critique – Routine Calcaneus
BOTH routine Os Calcis radiographs should display:
kVp range of 60→75 (Axial = 65-75; Lateral = 60-75)
Optimal density and contrast:
  no motion (i.e. blur)
  soft tissue margins visible
  clear bony trabecular markings
Exposure & Technique

## Slide 13: Image Critique – Routine Calcaneus
Marker Placement &/or artifacts
No removable artifacts are visible
Marker placement, not obscuring soft-tissue:
Plantodorsal (axial) projection: lateral edge of light-field
Lateral projection: anterior, “inferior” edge of light field

## Slide 14: Image Critique – Routine Calcaneus
CR & Collimation
Four sided collimation
Note: CR is centered around subtalar joint (~1 inch distal to medial malleolus)
Note: when viewing the plantar surface, the CR is centered around the level of the 5th metatarsal base

## Slide 15: Image Critique – Axial Calcaneus
Position
@ 65 kVp
R
Sustentaculum tali in profile
Open subtalar (aka. talocalcaneal) joint space
No distortion of the calcaneal tuberosity

## Slide 16: Image Critique – Lateral Calcaneus
Position
@ 60 kVp
R
Calcaneus in profile
Open tibiotalar, talocalcaneal, calcaneal cuboid, and talonavicular joint
Superimposed talar domes

## Slide 17: Image Critique – Routine Foot
Anatomy
Ideally, routine Foot radiographs should display:
Entire Foot
Soft-tissues
Lateral projection must also display ~1 inch of distal tib/fib
AP (axial) projection is only required to display all anatomy anterior to the talus

## Slide 18: Image Critique – Routine Foot
ALL routine Foot radiographs should display:
kVp range of 55→70 (AP = 55-65; Oblique & Lateral = 60-70)
Optimal density and contrast:
  no motion (i.e. blur)
  soft tissue margins visible
  clear bony trabecular markings
Exposure & Technique

## Slide 19: Image Critique – Routine Foot
Marker Placement &/or artifacts
No removable artifacts are visible
Marker placement, not obscuring soft-tissue:
AP & Oblique projections: lateral “superior” edge of light-field
Lateral projection: anterior, “superior” edge of light field

## Slide 20: Image Critique – Routine Foot
CR & Collimation
Four sided collimation, centered around base of 3rd metatarsal
Note: CR is centered more distally as less anatomy is included radiographically

## Slide 21: Image Critique – AP Foot
Position
@ 55 kVp
R
Bontrager pg. 232 Fig. 6.57
Equal distance between 2nd→5th metatarsal bodies
  *Overlap of bases
1st & 2nd metatarsal bases generally separated
Intertarsal joint space between 1st & 2nd cuneiforms

## Slide 22: Image Critique – AP Oblique Foot
Position
@ 60 kVp
SAIT MRT Image Critique Handbook
3rd→5th metatarsals free of superimposition
  No overlap of bases
1st & 2nd metatarsal bases overlapped
Base of 5th metatarsal in profile
Open joint spaces around cuboid and sinus tarsi

## Slide 23: Image Critique – Lateral Foot
Position
@ 60 kVp
R
SAIT MRT Image Critique Handbook
Metatarsal heads superimposed
Open tibiotalar joint
Distal fibula superimposed by posterior ½ of tibia

## Slide 24: Tips & Tricks – Lateral Projections
Anterior/posterior misalignment and superior/inferior misalignment
Assess the level of superimposition of the talar domes:
McQuillen Martensen 5th Ed. pg. 340 Fig. 6.85
McQuillen Martensen 5th Ed. pg. 340 Fig. 6.82

## Slide 25: Tips & Tricks – Lateral Projections
Fibula should be aligned to the posterior ½ of the Tibia
Check if the fibula is more anterior or posterior
Assess the position of the fibula in relation to the tibia:
Ideal
McQuillen Martensen 5th Ed. pg. 340 Fig. 6.85
McQuillen Martensen 5th Ed. pg. 340 Fig. 6.84

## Slide 26: Tips & Tricks – Lateral Projections
Fibula should be ~½ inch inferior to the Tibia
Check if the fibula is more inferior or superior
McQuillen Martensen 5th Ed. pg. 340 Fig. 6.82
McQuillen Martensen 5th Ed. pg. 340 Fig. 6.83
Assess the position of the fibula in relation to the tibia:

## Slide 27: Tips & Tricks – Lateral Projections
About ½ of the cuboid should be free of superimposition:
  Check if the cuboid is superimposed
McQuillen Martensen 5th Ed. pg. 340 Fig. 6.82
McQuillen Martensen 5th Ed. pg. 340 Fig. 6.83