## Slide 1: MRAD 204: Radiographic Technique 1
Outcome 6-10:
Positioning – IC fossa, Patella, & Tib/fib

## Slide 2: Affiliated Readings
Module Reading
Bontrager
Pgs: 244→245
Pgs: 253→255
Pgs: 256→261

## Slide 3: Overview
Guidelines/Considerations
Protocol
Positioning

## Slide 4: Guidelines/Considerations – IC Fossa
Identify required anatomy
Intercondylar Fossa projections require visualization of the fibular head distally, the femoral condyles medial/laterally, and the femoral epicondyles proximally
R
https://radiopaedia.org/articles/knee-beclere-method-intercondylar-view-1?lang=us

## Slide 5: Guidelines/Considerations – IC Fossa
2. Select appropriate equipment/technical factors
110cm SID, measured electronically using détentes (i.e. blue lock must be engaged)
IC Fossa technique = 70→80 kVp
On the console, select:
  “Table IR”
  *your method of choice
*Using the smallest field size possible, collimation

## Slide 6: Guidelines/Considerations – IC Fossa
Setup room before bringing the patient in
Tube and IR aligned @ 110cm SID (*set the tube angle first, then measure for SID)
  Lock: centers tube to IR laterally/medially
  Laser light: centers tube to IR superiorly/inferiorly
Correct anatomical marker selected
Ensure IR is covered completely prior to patient mount/dismount
For table imaging: All locks must be “on” except yellow & green
*lock engaged

## Slide 7: Guidelines/Considerations – IC Fossa
3. Artifact Removal
Any clothing or objects between the mid-femur to the “mid-calf”
Notes: when the patient is in the room:
Use external landmarks when positioning
  Femoral epicondyles determine correct patient position
    *when centering: remember the IC Fossa is part of the femur
  CR must be parallel to the Tib/Fib
*can be easier to ask your patient to remove their pants and provide them with a gown & housecoat
  Marker likely under soft-tissue anatomy shadow

## Slide 8: Intercondylar (IC) Fossa Protocol
Routine:
PA axial
OR
AP axial

## Slide 9: Positioning – PA axial (Camp Coventry Method)
Patient prone, knee flexed ~450 with support under affected leg
Femur parallel to edge of IR
Knee must be positioned in true PA (aka. Femoral epicondyles parallel to IR)
CR angle matches knee flexion
Place an anatomical marker (using Anderson Marker Rules), at the inferior lateral edge of the light field, and make final adjustments
L
Bontrager pg. 253 Fig. 6.118
CR perpendicular to tib/fib

## Slide 10: Positioning – PA axial (Camp Coventry Method)
Note: When using “large” angles, check for CR crosshair in relation to anatomy as the light field will be distorted (i.e. crosshair should “hit” the lateral femoral epicondyle)
Crosswise crosshair should be located around knee joint
Lengthwise crosshair centered between femoral epicondyles
“Bottom” of light field on pt. ~2.5-inches below knee joint (to include head of fibula)
“Top” of light field on IR at least ½ inch proximal to femoral epicondyles
CR & Knee flexion = ~450 (i.e. CR perpendicular to tib/fib)
Femur parallel to longitudinal edge of IR
Lateral-medial collimation: @ least ½ inch beyond femoral epicondyles
Marker on lateral edge of light-field “femur-up”

## Slide 11: Positioning – PA (Holmblad Method)
Bontrager pg. 253 Fig. 6.119
Patient kneeling, and leaning forward ~200 to remove soft-tissue superimposition
Femur parallel to edge of IR
Knee must be positioned in true PA (aka. Femoral epicondyles parallel to IR)
CR angle matches lower leg
Place an anatomical marker (using Anderson Marker Rules), at the inferior lateral edge of the light field, and make final adjustments
CR perpendicular to tib/fib

## Slide 12: Positioning – PA (Holmblad Method)
Crosswise crosshair should be located around knee joint
Lengthwise crosshair centered between femoral epicondyles
“Bottom” of light field on IR ~2.5-inches below knee joint (to include head of fibula)
“Top” of light field on IR at least ½ inch proximal to femoral epicondyles
CR perpendicular to tib/fib
Femur parallel to longitudinal edge of IR
Lateral-medial collimation: @ least ½ inch beyond femoral epicondyles
Marker on lateral edge of light-field “femur-up”
Patient weight placed on unaffected knee

## Slide 13: Positioning – AP axial (Béclere Method)
Bontrager pg. 255 Fig. 6.124-6.126
Worst method (due to distortion caused by OID)

## Slide 14: Guidelines/Considerations – Patella
Tangential patella projections require visualization of the entire patella, patellofemoral joint space, intercondylar sulcus of the femur, and the femoral condyles
1, 2 & 3. Same as IC Fossa EXCEPT:
CR cassette must be used for tangential patella projections
SID 100cm

## Slide 15: Patella Protocol
Routine:
PA
Lateral
Tangential

## Slide 16: Positioning – PA & Lateral Patella
Bontrager pg. 256-257 Fig. 6.127-6.130
L
Only 5-100 knee flexion
Small field size, centered to patella
L

## Slide 17: Positioning – Seated Settegast Method
Patient seated with feet at bottom edge of table
Femoral epicondyles parallel to IR)
Palpate borders of patella to determine specific CR angle required to pass through patellofemoral joint space
Pt. to hold IR perpendicular to CR
Place an anatomical marker, (using Anderson Marker Rules), and make final adjustments
R

## Slide 18: Positioning – Seated Settegast Method
Crosswise crosshair should appear to “wrap around” the patella
Lengthwise crosshair centered between femoral epicondyles
“Bottom” of light field on IR @ level of femoral epicondyles
“Top” of light field on IR at least ½ inch beyond the patella shadow
CR parallel to patellofemoral joint space
Lateral-medial collimation: @ least ½ inch beyond femoral epicondyles
Marker on lateral superior edge
R
IR held perpendicular to CR
Knee flexed 900

## Slide 19: Positioning – 90/20 Settegast Method
Patient prone, knee flexed 900 with support for affected leg as needed
Femur parallel to edge of IR
Femoral epicondyles parallel to IR)
CR angle matches angle of patella (~200)
Place an anatomical marker, distal to the femur (using Anderson Marker Rules), and make final adjustments
Bontrager pg. 260 Fig. 6.137
R

## Slide 20: Positioning – 90/20 Settegast Method
Crosswise crosshair should appear to “wrap around” the patella
Lengthwise crosshair centered between femoral epicondyles
“Bottom” of light field on IR @ level of femoral epicondyles
“Top” of light field on IR at least ½ inch beyond the patella shadow
CR parallel to patellofemoral joint space
Femur parallel to longitudinal edge of IR
Lateral-medial collimation: @ least ½ inch beyond femoral epicondyles
Marker on lateral edge of light-field “patella-up”
Knee flexed 900

## Slide 21: Positioning – Hughston Method
Crosswise crosshair should appear to “wrap around” the patella
Lengthwise crosshair centered between femoral epicondyles
“Bottom” of light field on IR @ level of femoral epicondyles
“Top” of light field on IR at least ½ inch beyond the patella shadow
CR parallel to patellofemoral joint space
Femur parallel to longitudinal edge of IR
Lateral-medial collimation: @ least ½ inch beyond femoral epicondyles
Marker on lateral edge of light-field “patella-up”
Knee flexed 50-600

## Slide 22: Guidelines/Considerations – Tib/Fib
Identify required anatomy
AP& lateral tib/fib radiographs require the knee joint, ankle joint, entire tibia and fibula, & surrounding soft-tissues
R
SAIT MRT Image Critique Handbook

## Slide 23: Guidelines/Considerations – Tib/Fib
2 & 3. Same as IC Fossa except:
Patient must also be instructed to remove their socks
Wireless digital IR can be used to ensure entire tib/fib is imaged in one radiograph
  If this option is selected, SID must begin at 100cm, then increased (as needed) to ensure all required anatomy “fits” lengthwise into the maximum permissible light-field

## Slide 24: Tibia/Fibula Protocol
Routine:
AP
Lateral

## Slide 25: Positioning – AP Tibia/Fibula
Knee must be positioned in true AP
  Aka. Femoral epicondyles parallel to IR
Dorsiflex foot (if possible)
Place an anatomical marker (using Anderson Marker Rules), proving overlap as needed, and make final adjustments
Note: the longer field size should include site of injury, and the marker is used to prove overlap
Place leg diagonally across wireless IR (heel and knee in opposite corners) or take two portrait table IR images

## Slide 26: Positioning – AP Tibia/Fibula
“Bottom” of light field on IR ~½ inch inferior to lateral malleolus
Lengthwise crosshair ½ between femoral epicondyles
Marker on lateral side, not under anatomy shadow
Remember: wireless IR/cassette should be diagonal
CR should be located around mid-tibia
“Top” of light field on IR @ level of femoral epicondyles
Lateral-medial collimation: @ least ½ inch beyond soft-tissue
Foot dorsiflexed 900

## Slide 27: Positioning – Lateral Tibia/Fibula
Knee must be positioned in true Lateral
  Aka. Femoral epicondyles perpendicular to IR
Partially flex knee of affected side
Dorsiflex foot (if possible)
Place an anatomical marker (using Anderson Marker Rules), proving overlap as needed, and make final adjustments
Place leg diagonally across wireless IR (heel and knee in opposite corners) or take two portrait table IR images
Note: must have @ least ½-inch of light posterior to the soft-tissue of the calf muscle (not shown in this image)

## Slide 28: Positioning – Lateral Tibia/Fibula
“Bottom” of light field on IR ~½ inch inferior to lateral malleolus (must check inferior/posteriorly)
Lengthwise crosshair ½ between femoral epicondyles
Marker on anterior side, not under anatomy shadow
Remember: wireless IR/cassette should be diagonal
CR should be located around mid-tibia
“Top” of light field on IR @ level of femoral epicondyles
Anterior/posterior collimation: @ least ½ inch beyond patella
& soft-tissue
Foot dorsiflexed 900
Ensure unaffected leg is removed from ROI
Knee partially flexed