## Slide 1
Workplace Electrical Safety

## Slide 2
Worst Case Scenario
Crane was being moved backwards while the crane boom was raised. Boom of the crane contacted a 44 kV line running across the highway. One worker, acting as a signaler for the driver. When the boom made contact . . .
The worker touching the body of crane while standing on the ground died. The crane driver jumped from the crane’s truck cab to see what happened to the first worker, made contact with the crane and the ground. This worker also died.
This was a father and son.

## Slide 3: This applies at home as well
Three times as many people die from electrical contact in their home as all of general industry combined.
Knowing what
to do and then…
doing it !

## Slide 4: What do you do at work or home?
What’s wrong with this picture?
How can you eliminate the hazard?

## Slide 5: What is Electricity?
Electricity is an invisible, silent form of tremendous energy that can kill and disfigure.
It is a transfer of energy in a flow of electrons from one place to another.
Lightning is electricity and kills more people than all other natural disasters combined.
It is an important source of power, to produce heat, light, and motion.

## Slide 6
The work electricity does is measured in “WATTS”. A 40-Watt light bulb uses less power or energy than a 100-Watt light bulb.
40 W 100 W

## Slide 7
The pressure or potential for work is the Voltage, measured in VOLTS.
This pressure, voltage, is like psi (pounds per square inch).

## Slide 8
The flow, or current of Electricity is measured in AMPERES or AMPS.
Current is the Killer.
It takes very little current.

## Slide 9: How fast is it?
Electricity travels at the speed of light.
The speed of light is 300,000 kilometers per second or 186,000 miles per second.
Electricity could travel around the world over 7 times in one second

## Slide 10: How does it kill people ? Current is the Killer - Amps Current’s Effect On The Body.

## Slide 11
How does it kill people ?
One outlet can feed 45 x 40-Watt Bulbs and have a surge current even higher.

## Slide 12: It goes through your nervous system, blood, muscles, organs, and bones. You cook and your cells die, even after the electricity stops flowing.
Current is the Killer

## Slide 13: How does it kill people? Electricity has to have … a path to flow.

## Slide 14: The path can be through the ground.

## Slide 15: The path can be through you to the ground. Touch potential. What about birds?

## Slide 16: The path can be through you on the ground. Step potential.

## Slide 17: Duties of Employers
Section 25. (1) An employer shall ensure that,
the equipment, materials and protective devices as prescribed are provided
the equipment, materials and protective devices provided by the employer are maintained in good condition
the measures and procedures prescribed are carried out in the workplace
the equipment, materials and protective devices provided by the employer are used as prescribed

## Slide 18: Duties of Employers
Section 25. (2) Without limiting the strict duties imposed by subsection (1), an employer shall,
(a) provide information, instruction and supervision to a worker to protect the health or safety of the worker;
(c) when appointing a supervisor, appoint a competent person;
(d) Acquaint a worker or a person in authority over a worker with any hazard in the work and in the handling, storage, use, disposal and transport of any article, device, equipment or a biological, chemical or physical agent;
(h) Take every precaution reasonable in the circumstances for the protection of a worker;

## Slide 19: Supervisor Responsibilities
Section 27 (1) A supervisor shall ensure that a worker,
Works in the manner and with the protective devices, measures and procedures required by this Act and the regulations; and
Uses or wears the equipment, protective devices or clothing that the worker’s employer requires to be used or worn R.S.O. 1990, c. 0.1, s. 27 (1)
Advise a worker of the existence of any potential or actual danger to the health or safety of the worker of which the supervisor is aware;
Where so prescribed, provide a worker with written instructions as to the measures and procedures to be taken for protection of the worker; and
take every precaution reasonable in the circumstances for the protection of a worker, R.S.O. 1990, c. 0.1, s.27 (2).

## Slide 20: Worker Responsibilities
Section 28 (1) A worker shall,
Work in compliance with the provisions of this Act and the Regulations
Use or wear equipment and/or PPE required by Employer
Report, to his or her employer or supervisor the absence of or defect in any equipment or protective device of which the worker is aware and which may endanger himself, herself or another worker; and
Report to his or her employer or supervisor any contravention of the Act or the regulations or the existence of any hazard of which he or she knows. R.S.O. 1990, c. 0.1, s. 28 (1).

## Slide 21: Worker Responsibilities
Section 28 (2) No worker shall,
Remove or make ineffective any protective device required by the regulations or by his or her employer, without providing an adequate temporary protective device and when the need for removing or making ineffective the protective device shall be replaced immediately;
Use or operate any equipment, machine, device or thing or work in a manner that may endanger himself, herself or any other worker; or
Engage in any prank, contest, feat of strength, unnecessary running or rough and boisterous conduct. R.S.O. 1990, c. 0.1, s. 28 (2).

## Slide 22: Electrical Hazards
Electrical Shock
Electrocution (loss of life)
Arc Flash
Arc Blast

## Slide 23: Electrical Shock
Received when current passes through the body
Severity of the shock depends on:
  Path of current through the body
  Amount of current flowing through the body
  Length of time the body is in the circuit

## Slide 24: Electrical Current On the Human Body
Current in milli-amperes Effects
1 or less No sensation; probably not noticed
1 to 3 Mild sensation not painful
3 to 10 Painful shock.
10 to 30 Muscular control could be lost or muscle clamping
30 to 75 Respiratory paralysis
75mA to 4 amps Ventricular Fibrillation
Over 4 amps Tissue begins to burns. Heart muscles clamp and heart stops beating
1/10 ampere is 100 milliamperes

## Slide 25
Electrical Shock Injury
Most common shock-related, nonfatal injury
Occurs when you touch electrical wiring or equipment that is improperly used or maintained
Typically occurs on the hands
Very serious injury that needs immediate attention

## Slide 26
Electrical Shock Injury
There must be a current flow from one point of the body to another point of the body, i.e., not an open circuit.
Most of the current flows through the inside of the body rather than through the body surface which is skin.
In this picture it exited the foot

## Slide 27
Arc Flash
The light and heat released from an electrical breakdown that is due to electrical current ionizing gases in the air.

## Slide 28
Temperatures can reach 20,000 F
Burns the skin directly
Can ignite clothing immediately
Arc flash majority of electrical accidents
Can kill at a distance of 3 meters
Arc Flash

## Slide 29
Arc Blast
An explosive or rapid expansion of air with tremendous pressure and temperature, which is caused by arcs sometimes.
This wave can cause physical injuries, collapse your lungs, or create noise that can damage hearing.

## Slide 30
Noise exposure of up to 140 dBA
Molten metal created
Shrapnel can penetrate the body
Arc Blast

## Slide 31: Arc Flash

## Slide 32: Electric Arc
An electric arc may be started in one of the following ways:
An improvised test probe (possibly a screwdriver blade or bare alligator clips) with more than the necessary exposed metal may create a phase-to-phase or phase-to-ground short-circuit on the closely spaced fuse clips or bus bars of a 600 V panel.

## Slide 33: Electric Arc
A screwdriver that is being used on energized equipment may slip and ground out the live parts.
A multimeter that is not switched from the ammeter or ohmmeter mode may create a short-circuit across phases when the probes are placed on the conductors to measure voltage. The multimeter may disintegrate because the internal fuse may not be designed to protect against this kind of misuse. The arcing caused at the test probes can ionize the air, resulting in a fire ball.

## Slide 34: Electrical Hazard
Two factors can make energized low-voltage equipment extremely hazardous. The first is that the small working clearances between low-voltage components leave little room for error when using tools.
low-voltage equipment in some industrial services may be supplied by an electrical system that can feed incredible amounts of energy into a fault (caused by a short-circuit, for example).

## Slide 35: Electrical Hazards
In such cases, a fault can cause an intense, persistent, and rapidly expanding arc of electrical energy to build in a split second. This energy is released suddenly in a restricted space.
The flames can result in terrible burns on anyone within the arc’s range, which may reach up to 3 m (10 ft.). Arcs of this kind often leave the electrical structure a charred and melted wreck — stark evidence of the intense heat generated (several thousands of degrees).

## Slide 36: Risk Assessment
Personal Protective Equipment
Administrative
Substitution
Elimination
Engineering Controls
{
Prevention
Personal Protective Equipment
Isolation

## Slide 37: Risk Assessment
Required to reduce the likelihood of injury to the worker or damage to equipment
To ensure that hazards are properly identified with regard to their severity and the likelihood of their occurrence.
Once the hazards have been identified, the risk can be identified
Control measures are then implemented

## Slide 38: Elimination
Elimination
- The total removal of hazards
- Makes all identified possible injury or health affects impossible
- All other controls no longer required

## Slide 39: Substitution
Substitution
- Replaces one hazard with one that is a lessor risk
- Work scheduling considerations- Achieves same objective

## Slide 40: Isolation
Isolation
- Keep hazard separated from the people at risk

## Slide 41: Engineering
Engineering Controls
- Physical changes that limit the hazard
- Include structural changes to work environment, redesign or adding of safeguards - erection of barriers to prevent workers from hazard exposure

## Slide 42: Administration
Administrative
- Controls include work systems/procedures/training
- Help reduce exposure to the risks
- May be used in conjunction with other controls
- Should involve people who regularly perform tasks like contractors / workers due to risks knowledge
- Requires effective communications to workers

## Slide 43: Safe Electrical Procedures Include:
Identified electrical hazards
Identifying tasks to be performed
Documenting hazards for each tasks
Eliminating the risk for each hazard
PPE requirement

## Slide 44: Responsibilities for Controlling the Risks
Suppliers
Electrical Engineers (designers)
Electricians
Supervisors
Management

## Slide 45: Electrical Safety Program
Evaluating electrical equipment
Documenting first time procedures
De-energizing
Identifying unexpecting events
Identifying electrical hazards
Reducing the risks to electrical hazards

## Slide 46: Electrical Safety Program
Protecting the worker from shock, burns or blasts
Using the right tools for the job
Peoples abilities to perform the job
Auditing the program

## Slide 47: Electrical Safety Program Controls
Training and the worker applies
Procedures to identify the hazard and develop plans to eliminate or control the hazard
Circuit is considered live until proven
Circuit is made safe to work on (lockout)
Limited approach boundary
Determine the potential hazard of a task

## Slide 48: Electrical Safety Program Procedures
Purpose of the task
Number of workers to be involved
Identification of hazards and risk of each task
Safe work practices to be used
PPE to be involved
Tools involved
Sketches, reference data and equipment detail

## Slide 49: Hazard Alert
Two workers were attempting to add a new 400 A switch to the energized 600 V section of a 1,500 kVA power centre. A number of important loads were fed from the low-voltage busbars where the workers were going to install a new fused switch. They didn’t want to inconvenience other operations by de-energizing the other loads connected to the busbars. Instead of planning a shutdown, they decided that they could install the switch live because it was “only” low voltage. The workers were severely burned during the installation

## Slide 50: Industrial Regulations
42. (1) The power supply to electrical installations, equipment or conductors shall be disconnected, locked out of service and tagged before any work is done, and while it is being done, on or near live exposed parts of the installations, equipment or conductors.
(2) Before beginning the work, each worker shall determine if the requirements of subsection (1) have been complied with.
(3) Locking out is not required,
(a) if the conductors are adequately grounded with a visible grounding mechanism; or
(b) if the voltage is less than 300 volts and there is no locking device for the circuit breakers or fuses and procedures are in place adequate to ensure that the circuit is not inadvertently energized.
(4) If locking out is not required for the reason set out in clause (3)
(b), the employer shall ensure that the procedures required by that clause are carried out

## Slide 51: Industrial Regulations
(5) If more than one worker is involved in the work referred to in subsection (1), the worker who disconnected and locked out the power supply shall communicate the purpose and status of the disconnecting and locking out. O. Reg. 630/94, s. 1.
(6) If a tag is used as a means of communication, the tag,
(a) shall be made of non-conducting material;
(b) shall be secured to prevent its inadvertent removal;
(c) shall be placed in a conspicuous location;
(d) shall state the reason the switch is disconnected and locked out;
(e) shall show the name of the worker who disconnected and locked out the switch; and
(f) shall show the date on which the switch was disconnected and locked out.
(7) The employer shall establish and implement written procedures for compliance with this section.

## Slide 52: Industrial Regulations
42.1 (1) This section applies and section 42 does not apply if it is not practical to disconnect electrical installations, equipment or conductors from the power supply before working on, or near, live exposed parts of the installations, equipment or conductors.
(2) The worker shall use rubber gloves, mats, shields and other protective equipment and procedures adequate to ensure protection from electrical shock and burns while performing the work.
(3) If the installation, equipment or conductor is operating at a nominal voltage of 300 volts or more, a suitably equipped competent person who is able to recognize the hazards and perform rescue operations, including artificial respiration, shall be available and able to see the worker who is performing the work. (4) Subsection (3) does not apply to equipment testing and trouble-shooting operations.
43. Tools and other equipment that are capable of conducting electricity and endangering the safety of any worker shall not be used in such proximity to any live electrical installation or equipment that they might make electrical contact with the live conductor.

## Slide 53: Industrial Regulations
44. (1) Cord-connected electrical equipment and tools shall have a casing that is adequately grounded. (2) Subsection (1) does not apply to cord-connected electrical equipment or tools that are adequately double-insulated and whose insulated casing shows no evidence of cracks or defects
(3) Subsection (1) does not apply to a portable electrical generator in which the electrical equipment or tools are not exposed to an external electric power source if the casing of portable electrical equipment or tools connected to the generator is bonded to a non-current-carrying part of the generator.
44.1 When used outdoors or in wet locations, portable electrical tools shall be protected by a ground fault circuit interrupter installed at the receptacle or on the circuit at the panel.
44.2 A ground fault that may pose a hazard shall be investigated and removed without delay.

## Slide 54: Lock Out
Placement of a lockout device on an energy isolating device in accordance with established procedures to ensure the equipment being controlled cannot be operated until the lockout device is removed.

## Slide 55: Lockout/Tag Out
To ensure that the machine or piece of equipment is de-energized from all potentially hazardous energy sources; and,
Locked out to prevent any chance of it being inadvertently started up while the equipment is being maintained.
Achieving zero energy state
Always be aware if a secondary power source

## Slide 56: PPE Category
Category 1
  Arc rated long sleeve shirt and pants or arc rated coverall
  Arc rated faceshield or arc flash suit hood
  Arc rated jacket, parka, rainwear, or hard hat liner
  Category 2
    Arc rated long sleeve shirt and pants or arc rated coverall
    Arc rated arc flash suit hood or arc rated faceshield and arc rated balaclava
    Arc rated jacket, parka, rainwear, or hard hat liner

## Slide 57: Personal Protective Equipment

## Slide 58: Personal Protective Equipment

## Slide 59: Electrical Safety Hazard Alert
A journeyman electrician was burned when there was an explosion caused by an electric arc. He was installing a 600 V temporary service to a construction site. The high-visibility vest he was wearing caught fire, and the plastic on the vest melted, increasing the severity of his burns.
Although flame-resistant vests are available, most high- visibility vests are not flame-resistant. If there is any danger of a fire or explosion when working with energized equipment, the worker should remove clothing that isn't flame-resistant.

## Slide 60: Electrical Safety Checklist
Electrical hazards
Voltage level
Number of workers required
Electrical safety person required
Lockout required
Secondary electrical source
Schematics available
Safety procedures
First aid / CPR
What is the job
Emergency equipment available
Equipment emergency shut off

## Slide 61: Electrical Accident Factors
In a hurry
Lack of unclear standards
Distractions
Changes from routine
Changes in equipment conditions
Personality conflicts
First time performing activity
Lack of knowledge or training
Job stress
Complacency
Awkward positions

## Slide 62: General Electrical Safety Precautions
Think ahead. Assess all of the risks associated with the task. Plan the whole job in advance so that you can take every precaution, including arranging for help in case of paralyzing shock. Consider the use of a pre-job safety meeting to discuss the job with all workers before starting the work.

## Slide 63: General Electrical Safety Precautions
Remove metal rings, bracelets, and wristwatch bands. These could cause a short-circuit where small clearances are involved. (If it is necessary to wear medic-alert bracelets, secure them with transparent surgical or adhesive tape or rubber bands
Use one hand with your face and body turned to the side when operating a safety switch. Limit possible injuries by not placing body parts directly in front of energized equipment when there is danger of an arc flash.
Use left hand, body standing to the right and face turned to the right

## Slide 64: General Electrical Safety Precautions
Use the correct equipment and clothing Cover-up blankets to avoid accidental contact with live equipment
Shock-resistant safety boots or shoes (with appropriate CSA symbol)
Safety glasses, goggles, or a face shield to protect the worker from molten metal or ultraviolet light
Flame-resistant clothing if there is a risk of an electric arc that could cause a fire

## Slide 65: General Electrical Safety Precautions
Insulated tools and equipment:
Insulated tools will be used when working inside the boundary of exposed energized conductors or circuit parts
Insulated tools will be rated for voltage to be used
Will be inspected before and after each use for damage to the insulation.

## Slide 66: General Electrical Safety Precautions
Examples of Warning Signs

## Slide 67: General Electrical Safety Precautions
Working alone:
The employer must develop and implement a written procedure for checking the well-being of someone doing electrical work alone or in isolation.
The procedure must include the time interval between checks and the procedure to follow in case the worker cannot be contacted (including provisions for emergency rescue).
Someone must be designated to establish contact with the worker at predetermined intervals and at the end of the work shift.
The time intervals must be determined in consultation with the worker assigned to work alone or in isolation.

## Slide 68: QUESTIONS?