## Slide 1: RADP 215: Radiation Protection
Best Practices for Minimizing Dose to Imaging and Support Personnel
RADP 215: Radiation Protection
Best Practices for Minimizing Dose to Imaging and Support Personnel

## Slide 2: Radiation Safety Roles in DI
All Medical Imaging staff are responsible for radiation safety
Governing Bodies
  Health Canada
    Safety Code 35
  The College of Physicians and Surgeons
  Canadian Association of Medical Radiation Technologists (CAMRT) and provincial colleges

## Slide 3: Fundamental Rules of Protection
Rules for staff protection:
  TIME: Decrease time in room
  DISTANCE: Increase distance from tube and patient
  SHIELDING: Always use protective shielding
  ALARA also applies to our exposure

## Slide 4: Protection from Radiation
Three types of radiation that may be in an X-ray room:
  Primary
  Scatter
  Leakage
Protection of staff from radiation must be considered if patients need to be restrained or assisted during a procedure
Where you stand is very important!
As beam energy increases, forward scatter also increases

## Slide 5: Scatter and Leakage
Patients are the greatest radiation hazard to the technologist!
Most scatter is produced by the patient
Important to reduce exposure to that scatter
During an exposure, individuals in the room should be:
  Positioned at 90° to primary beam
Scatter intensity is _________ of the primary beam

## Slide 6: Scatter and Leakage
Occupational exposure is greatest in fluoroscopy and interventional procedures for all staff
Table head and foot have the most scatter in fluoroscopy and CT
Several means to protect staff from scatter radiation:
  Protective equipment
    Image intensifier curtain
    Bucky slot shielding device
    Operator shield
      Mobile walls

## Slide 7: Tech Protection and Patient Safety
When restraining or supporting a patient during an exposure:
  No one other than the patient should be exposed to the primary beam
  Technologists should never stand in the primary beam
  Other support personnel should always be positioned with awareness of location of hands and arms in regard to the primary beam

## Slide 8: Protection and Safety
If the patient cannot follow instructions:
  Immobilization of a patient is preferred over exposing staff
  Mechanical restraints explained well and correctly used may be successful
Human restraints are a last resort
When human restraints are required:
  Non-occupationally exposed individuals can be asked to hold
  Some individuals are a better choice than others for radiation safety

## Slide 9: Protection and Safety
Technologist is responsible for positioning the individual holding the patient.
Ensure the individual is not in the primary beam and is protected from scatter and leakage.
Individual must wear all the appropriate lead protection.
No individual should routinely hold patients (including male RNs, radiation aides, security staff or caregivers).

## Slide 10: Protection and Safety
Pregnant women are never permitted to hold a patient!
Best options for asking an individual to help restrain a patient:
  Male or female past reproductive age
    1st choice: family member, friend or personal caregiver
    2nd choice: non-radiology hospital staff
Any one of these individuals has the right to refuse the request.

## Slide 11: Protection and Safety
Best practice suggests radiology staff is the last resort, but sometimes:
  There are time constraints
  Non-occupational individuals not available
  More efficient for a tech to hold
Techs must wear all the lead protection available, including gloves and collar monitor
Holding of the patient by a tech should always be reported and documented (as per best practices)

## Slide 12: Protective Equipment
Protection from secondary radiation
Lead (Pb) aprons (full and ½)
  Minimum is ______mm Pb where peak kVp is between 100-150kVp
Shielded barriers
  Wall: 0.3–2.0 mm Pb
  Hanging: 0.5 mm Pb

## Slide 13: Protective Equipment (cont’d)
Gloves
  ____________mm Pb
Glasses
  ____________mm Pb
Thyroid Collars
  ____________mm Pb

## Slide 14: Conclusion
Basic rules prevail:
  Never be in the primary beam
  If you don’t need to be there, don’t be there
  Stay as far away as you can
Use all the protective lead provided:
  Aprons, thyroid collars, gloves and glasses
  Protective curtains and mobile walls