## Slide 1: MRAD 204: Radiographic Technique 1
Introduction to Positioning

## Slide 2: Affiliated Readings
Bontrager
Pgs: 15→16
Pgs: 23 →24
Pgs: 26 →30

## Slide 3: Overview
Body Habitus
General Terms
“Special” Projections
Terms Related to Movement

## Slide 4: Body Habitus
Bushong 10th Ed. Fig. 13-03
“Average” Size
“Thin”
“Broad Frame”
Very Thin
Collimation should be adjusted according to body habitus

## Slide 5: General Terms
Radiograph
Bontrager pg 16 Fig. 1.39
Bontrager pg. 16 Fig. 1.38
Radiography
The steps required to create a radiograph
Include patient positioning, IR selection & placement
Aka. the x-ray image
Display as the patient facing the viewer, in anatomic position

## Slide 6: General Terms
View is used to identify which image (from a routine) is displayed
Common to take at least 2 radiographs (at different angles) of the same body part
  Taking images at different angles can improve: localization of foreign bodies, and determining alignment of fractures etc.
AP Knee
Lateral Knee
3 views of the wrist
PA
Oblique
Lateral
Bontrager pg. 34 Fig. 1-109
Bontrager pg. 35 Fig. 1-112

## Slide 7: General Terms
Position relates to the patient; describes how they are posed in relation to the IR
Imagine you could not see this patient. How should you describe their position, to someone else?
Standing with their right side against the IR
Erect Right Lateral
Right Lateral
Standing straight, with arms elevated
Bontrager pg. 21 Fig. 1.61

## Slide 8: General Terms
Projection relates to the x-ray tube and IR; describes how the x-ray beam is moving through the patient’s body
Lateral projections of the axial skeleton are typically defined more simply as “lateral”
Lateral projections of the appendicular skeleton: path of the CR must be defined as medial→lateral or lateral→medial
Bontrager pg. 19 Fig. 1.53 & 1.54
Mediolateral
Lateromedial
Bontrager pg. 24 Fig. 1.77

## Slide 9: Image Receptor (IR): aka. Detector
SAIT Campus 2021
DR or CR:
CR Cassettes have 3 sizes
  Small (8x10in or 20x25cm)
  Medium (10x12in or 24x30cm)
  Large (14x17in or 35x43cm)
For CR, must be placed in a CR reader to view a radiograph
Can be moved more freely
Active surface is “black”
Table & Wall IR

## Slide 10: Central Ray (CR)
Bontrager pg 19 Fig. 1.49
Indicates the middle of the x-ray beam
When turned on, the collimator light displays dark crosshairs. The middle of the x-ray beam (Central Ray) is located where the dark crosshairs intersect
Note: Your textbook uses a metal rod to demonstrate the Central Ray (CR)
SAIT Campus 2021

## Slide 11: Markers
Bontrager pg.32 & 164 Fig. 1.108 & 4.121
Can be added electronically, or directly using radiopaque lead
  Use of lead is best practice
  When used, radiopaque lead markers, appear white on a radiograph
Most commonly used to identify the anatomic side that was radiographed
Is this a Right or Left elbow? (right)

## Slide 12: “Special” Projections
Axial projections refer to radiographs that are taken using an x-ray tube angle
Projection rules apply: must describe how the Central Ray (CR) moves through the patients body to the IR
Exception: AP Foot Projection
  Axial is not used as a descriptor, despite the tube angle
Inferosuperior axial
axial Plantodorsal
Dorsoplantar

## Slide 13: “Special” Projections
Tangential projections use either an exaggerated patient position, and/or tube angle (that follows a body part of interest) to remove superimposition
Example: Tangential patella (aka. knee cap) projections
  CR matches angle of the patella (adapted to patient position)
  Radiographically will display the patella “away” from other bones

## Slide 14: Terms Related to Movement
Bontrager pg. 27 Fig. 1.95
Medial = towards the midline of the body
Lateral = away from the midline of the body
Bontrager pg. 28 Fig. 1.96

## Slide 15: Terms Related to Movement
Bontrager pg. 26 & 27 Fig. 1.88, 1.90 & 1.92
Flexion moves body parts, above and below a joint, closer together
Extension refers to straightening a joint (into a neutral position)
Acute flexion = 90o wrist “bend”
Hyperextension = movement past neutral
Exception = Foot movements are considered flexion
Defined by direction of flexion

## Slide 16: Terms Related to Movement
Bontrager pg. 26, 27 & 28 Fig. 1.91, 1.93, 1.94, & 1.97
Movement of the wrist (from neutral) towards the ulna
Palm is “face-up”
Palm is “face-down”
A “twisting” motion of the foot only (ankle remains in a neutral/straight position)
Eversion
Inversion

## Slide 17: Terms Related to Movement
Bontrager pg. 29 Fig. 1.100
https://www.slideshare.net/KRUPARAITHATHA/hip-joint-80278864
Circumduction = Circular motion
Reaching towards the toes
Shrugging shoulders “up”
Tilt occurs when the body part is not parallel to the long edge of the IR
Rotation occurs when the body part is not flat against the surface of the IR (one part is elevated off the IR surface)
Bontrager pg. 29 Fig. 1.99