## Slide 1: MRAD 204: Radiographic Technique 1
Outcome 1-5:
Positioning – Shoulder & Clavicle

## Slide 2: Affiliated Readings
Module 5
Bontrager
Pgs: 183, 191→193, 196, 199 & 201
Pg: 204

## Slide 3: Overview
Guidelines/Considerations
Protocol
Positioning

## Slide 4: Guidelines/Considerations - Clavicle
Identify required anatomy
Bontrager 9th Ed. pg. 204 Fig. 5.87A
To ensure entire clavicle is visualized, radiographs require SC joint & Acromion
Bontrager pg. 182 Fig. 5.14

## Slide 5: Guidelines/Considerations - Clavicle
*Clavicle technique = *70→85 kVp
On the console, select:
  “Wall IR”
  the projection you will begin positioning
2. Select appropriate equipment/technical factors
*Using the smallest field size possible, collimate
110cm SID, measured electronically using détentes (i.e. green lock must be engaged)
Wall IR

## Slide 6: Guidelines/Considerations - Clavicle
Setup room before bringing the patient in
Tube and IR aligned @ 110cm SID
  Lock and set SID
  Center tube to IR laterally/medially
  Laser light: centers tube to IR superiorly/inferiorly
Correct anatomical marker selected
Ensure the correct “green” détente is used

## Slide 7: Guidelines/Considerations - Humerus
3. Artifact Removal
“Everything from the waist up”
  Tops (i.e. shirt/sweaters), bra, necklace(s), long earrings, wet or braided hair
Ensure the marker is NOT placed under “anatomy shadow”
Notes:
Upright or seated position is best
SC, AC joints, & entire Clavicle can be used as external landmarks
Expose, when patient has suspended respiration on full inspiration
    *Patient must be given gowning instructions*

## Slide 8: Protocol - Clavicle
Routine:
AP
AP Axial
  Note: a 15→300 tube angle can be used
    Tube angle required is dependent on body habitus
      Example: less tube angle is required for “larger” hypersthenic patients

## Slide 9: Positioning – AP Clavicle
CR is ~mid clavicle
*check centering with patient inhalation*
Marker on lateral side
Shoulder “relaxed” (not depressed or elevated)
Horizontal x-ray beam
Light-field extends:
Superiorly: ~ ½ inch “above” AC joint
Inferiorly: ~ ½ inch “below” SC joint
Medially: jugular notch
Laterally: ~ ½ inch beyond AC joint
R
Note: suspend respiration @ end of inhalation

## Slide 10: Positioning – AP Axial Clavicle
Marker on lateral side
& “up” arrow used
Shoulder “relaxed” (not depressed or elevated)
Tube angled 150 cephalad
Light-field extends:
Superiorly: ~ ½ inch “above” AC joint
Inferiorly: ~ ½ inch “below” SC joint
Medially: jugular notch
Laterally: ~ ½ inch beyond Acromion
Note: suspend respiration @ end of inhalation
CR is ~mid clavicle
*check centering with patient inhalation*

## Slide 11: Guidelines/Considerations
Identify required anatomy- each projection requires visualization of different amounts of anatomy
Select appropriate equipment/technical factors
  Wall IR (for CR, 8x10 Cassette will be needed)
Use external landmarks
Gowning instructions – with artifact removal
Breathing instructions
  All images require suspended respiration
Patient care
  *People with shoulder injuries are susceptible to fainting – seated position may be best

## Slide 12: Shoulder Girdle – External Landmarks
Inferior angle of scapula
Scapulohumeral joint
AC joint
SC joint
Superior angle of scapula
Medial border of scapula

## Slide 13: Protocol
Routine:
AP shoulder with external rotation
AP Oblique for glenoid cavity
PA Scapular Y (lateral)
Superoinferior axial
Non-Routine:
AP shoulder with neutral rotation
AP shoulder with internal rotation
Adaptive Projections:
Inferosuperior axial
AP Scapular Y (lateral)

## Slide 14: AP Shoulder - Considerations
Identify required anatomy
AP Shoulder radiographs require ½ the sternum, entire scapula, entire clavicle, & the proximal humerus
Bontrager pg. 179 Fig. 5.4

## Slide 15: Positioning – AP (external rotation)
Align collimator light to the length of required anatomy (i.e. crosswise field size)
Center the anatomy on the IR and/or in the light field
“Externally rotate” epicondyles of humerus until they are parallel to the IR
Place an anatomical marker (using Anderson Marker Rules), and make final adjustments, as needed
Note: suspend respiration
R

## Slide 16: Positioning – AP Shoulder (external rotation)
CR is ~1 inch (2.5cm) inferior to coracoid process
*aka. ~ mid clavicle (side-side) & ~2 inches inferior to clavicle
Marker on lateral side
Humeral epicondyles parallel to IR
Light-field extends:
Superiorly: ~ ½ inch “above” AC joint
Inferiorly: ~ ½ inch “below” inferior angle
Medially: ~ mid sternum
Laterally: ~ ½ inch beyond soft-tissue margins of “superior-portion” of humeral head
Note: ensure inferior angle of scapula is included by comparing palpated anatomy height to level of light on the IR

## Slide 17: AP Oblique (aka. Glenoid) - Considerations
Identify required anatomy
Glenoid Shoulder radiographs require coracoid process, acromion, & humeral head with surrounding soft-tissues

## Slide 18: Positioning – Glenoid Cavity (45o RPO or LPO)
Rotate hips & shoulders 45o toward affected side
(placing body of scapula parallel to IR)
Ensure neutral rotation of arm
Center over the scapulohumeral joint
Follow Marker Rules
Note: suspend respiration
Bontrager pg. 196 Fig., 5.55

## Slide 19: Positioning – Glenoid Cavity
CR is ~mid scapulohumeral joint
Marker on lateral side
Light-field extends:
Superiorly: ~ ½ inch “above” AC joint
Inferiorly: ~ level of axilla
Laterally: ~ ½ inch beyond soft-tissue margins
Medially: “whatever you get” = ~ mid clavicle
Note: light-field on the patient appears distorted; radiograph will only include ~½ clavicle, but the light will appear to “cover” entire clavicle
Hips & Shoulders rotated 450 towards IR
R
Arm in “neutral” rotation

## Slide 20: PA Oblique (Scap Y Lateral) - Considerations
Identify required anatomy
Scap Y Shoulder radiographs require entire scapula
Note: this projection is used to demonstrate dislocations
Anterior: humeral head beneath coracoid process
Posterior: humeral head beneath acromion

## Slide 21: Positioning – PA Scap Y(RAO or LAO position)
Face patient towards IR, with arm flexed 900
Rotate patient posteriorly until the AC joint AND superior angle are perpendicular to IR
Align collimator light to the length of required anatomy (i.e. tilt as required)
Center the anatomy on the IR and/or in the light field
Follow Anderson’s Marker Rules
Note: suspend respiration
R

## Slide 22: Positioning – PA Scap Y
CR is mid scapula; parallel to medial border
Marker on lateral side
Light-field extends:
Superiorly: ~ ½ inch “above” AC joint
Inferiorly: ~ ½ inch “below” inferior angle of scapula
Laterally: ~ ½ inch beyond lateral edge of acromion
Medially: “whatever you get”
Note: light-field on the patient appears distorted (medial border of light will “look” larger than it really is)
AC joint AND superior angle perpendicular to IR
Arm flexed 900
Collimator light matches angle of medial border

## Slide 23: Superoinferior “Axial” - Considerations
Identify required anatomy
Superoinferior Shoulder radiographs require ~¼ of the proximal humerus, entire coracoid process, and anterior/posterior soft-tissue margins

## Slide 24: Positioning – Superoinferior (0-15o) Axial
Seat patient at end of table on a stool/chair
Flex patient’s elbow 90o
Get patient to lean laterally, to place shoulder joint over a small cassette
  Notes: lowering the table helps place the joint “on top” of the IR
  If shoulder joint does not extend over the IR, angle the x-ray tube (not to exceed 150) towards the elbow, until the joint “lands on top” of the IR
*CR over shoulder joint – use “laser light” to help center
Note: suspend respiration

## Slide 25: Positioning – Superoinferior (0-15o) Axial
Locating the shoulder joint:
  Gently palpate contour of humeral head anteriorly
  Move your fingers medially, until humerus ‘ends’
Collimate to include anterior and posterior soft tissue, coracoid and entire humeral head
Place anatomical marker in the light-field, to “walk-along” the humerus (anteriorly)
Ask patient to rotate and tilt their head towards their unaffected shoulder

## Slide 26: Positioning – Superoinferior (0-15o) Axial
CR over shoulder joint
Marker on anterior side “walking-along” humerus
Light-field extends:
Anteriorly & Posteriorly: ~ ½ inch beyond soft tissue margins
Distally: ~ ¼ proximal humerus
Medially: “whatever you get”
Elbow & Shoulder parallel to length of IR
Note: cannot center anatomy on IR:
*ensure shoulder joint is at least 1-inch beyond medial edge of IR*
If shoulder joint is less than 1-inch beyond medial edge of IR: Add a tube angle (towards the elbow)
Head & Neck rotated and tilted towards opposite shoulder

## Slide 27: Adaptive Projection – Inferosuperior Axial
Bontrager pg. 193 Fig. 5.46 & 5.49
Typically performed when the patient cannot sufficiently extend their arm causing excessive OID
More abduction requires greater CR angles

## Slide 28: Adaptive Projection – AP Scap Y(RPO or LPO position)
Alternate to PA Scap Y
Performed on trauma patients
Notes:
IR behind patient
Reverse position from PA
http://www.wikiradiography.net/page/Lateral%20Scapula%20Radiography

## Slide 29: Non-Routine: AP Shoulder Neutral Rotation
Bontrager pg. 183 & 199 Fig. 5.19 & 5.68
Performed when trauma (i.e. fracture or dislocation are suspected) OR when dictated by site protocol
hand pronated on thigh

## Slide 30
Bontrager pg. 183 & 192 Fig. 5.17 & 5.44
Performed when dictated by site protocol
Non-Routine: AP Shoulder Internal Rotation
hand supinated on thigh