## Slide 1: MRAD 251: CT Theory
1
Outcome 6:
Summarize considerations for patient care
related to computed tomography (CT)

## Slide 2: Objectives
Describe the role and responsibilities of a technologist related to patient screening for CT scans
Identify important elements of a patient requisition and consent form
List the lab work and medications that need to be considered prior to scanning
Describe patient education in regard to administering contrast media
Describe how to effectively counsel a patient with respect to post-procedural care

## Slide 3: General Considerations
CT is minimally invasive however, there are a few considerations that make patient care in CT unique from other modalities.
CT Specific considerations:
  Use of IV contrast = ↑patient risk
  Gantry aperture may contribute to patient anxiety
    ↑anxiety = ↓patient cooperation

## Slide 4: Objective 6.1
Technologist responsibilities include:
Properly informing the patient
  Example: Communicating instructions for patient preparation, & post- procedure care
Preparing the exam room
  Example: Ensuring the room is clean, equipment is prepared for use, and functioning properly
    Accessibility considerations (in case a medical emergency occurs)
Documentation
  Conduct an effective patient history
    Example: Check for contraindications

## Slide 5: Tech Responsibilities Cont’d
Factors a technologist should consider, prior to performing a requested CT exam:
Patient factors:
  Age, Medical Condition, Ability to cooperate, body habitus, Risk vs Benefit, etc.
Requisition factors:
  What structure needs to be visualized?
    Is CT the best modality to visualize the anatomy of interest?
  Reason for the exam
    Pathology, Trauma, Vascular abnormalities, etc.
Protocol selected
Equipment factors:
  Scan acquisition/scheduling/sequencing

## Slide 6: Tech Responsibilities Cont’d
Knowing correct indications for performing a CT exam can be accomplished by:
Reading the requisition and clinical history prior to the exam
Obtain relevant information from the patient
Get informed consent
Check for relevant:
  Lab results
  Prior DI (aka. diagnostic imaging) exams
Identifying any possible contraindications
Consulting a radiologist if there are any outstanding questions or concerns

## Slide 7: Tech Responsibilities Cont’d
Information about a procedure must be presented to a patient
prior to image acquisition.
Patient understanding improves:
Cooperation
Anxiety levels
Image quality
Patient safety

## Slide 8: Considerations
Patient preparation includes:
Explaining the procedure
  Side effects/what can be expected?
    Normal side effects of IV contrast media (such as nausea/vomiting)
    Equipment is loud
    Breathing instructions
  How long will the procedure take?
Proper artifact removal/gowning instructions
Positioning to ensure optimal image acquisition and patient comfort
  Using appropriate anatomical reference points

## Slide 9: Patient Based Considerations
Additional considerations when positioning:
Patients eyes should be closed when using the laser lights to position for head scans
Donning PPE as required
Combative/Uncooperative patient considerations:
Avoid personal injury
Adjust scan acquisition time
Immobilization devices
Restraints
Sedation

## Slide 10: Sedation Considerations
Exams that are more susceptible to motion artifacts (which would degrade image quality) may require sedation
  3D reformats are susceptible to motion artifacts
Conscious sedation should be considered prior to deep sedation
  Deep sedation requires an anesthesiologist or specialized sedation
team
Should only be considered when all other methods have been unsuccessful

## Slide 11: Patient Screening
Patients should be assessed as soon as they arrive in the CT department:
Breathing patterns
Skin coloration
Overall health
Require a baseline for evaluation to prevent/treat possible adverse effects
Vital signs are the best early physiologic indicators:
  Body temperature
  Pulse
  Respirations
  Blood pressure

## Slide 12: Pediatric Considerations
CT scans of pediatric patients require a few additional considerations in comparison to adult patients.
Preparation prior to patient arrival is more important
  More monitoring and care is required
    ↑likelihood of requiring sedation
    Neonatal patients require specific room temperatures
    ↑immobilization requirements
Family members must be included in the exam procedure
  Required to obtain consent
  Parents may remain in the room during scan acquisition
    May help ↓ patient anxiety & ↑ cooperation

## Slide 13: Pediatric Considerations Cont’d
Equipment speed affects:
Scan times
Need for sedation
Patient dose
Technologists can minimize the risk of infection to neonatal patients by:
Removing jewellery (rings & watches)
Performing aseptic handwashing
Donning PPE (gloves, masks etc.)
Maintaining the patients body temperature
Ensuring a nurse monitors vital signs

## Slide 14: Objective 6.2
CT scans should not be performed without a requisition.
The radiologist must review the requisition
  Determines the appropriate Protocol
CT scans require appointment bookings for scheduling purposes:
  Scan times vary
  Workflow efficiency
    ↑patient throughput
    ↓department downtime

## Slide 15: Requisitions
Each requisition should be protocolled. Protocols should answer the clinical question(s) being asked.
The selected protocol should pose the least risk to the patient
  Accomplished with special attention to:
    Radiation exposure
      ALARA
    Reaction to contrast media
    Complications from more invasive procedures (such as biopsies or
fluid drainage)
      Example: Bleeding or infection

## Slide 16: Requisitions
Requisitions should include:
Clinical history and the presumptive diagnosis or the diagnostic question to be answered by the CT scan
Allergies
Medical history
  Example: diabetes, heart disease, etc.
Recent lab results (as required)

## Slide 17: Requisitions
Technologists should check the patients clinical history with the exam ordered.
Verify Protocol selection
Discrepancies require radiologist consult
Confirm with the patient:
Information on the requisition must be accurate
  Confirmation can be achieved using:
    Focused questions
    Reflective speech

## Slide 18: Objective 6.3
Most frequently reviewed lab values prior to performing a CT exam are:
For kidney assessment:
  SeCR
  GFR
**The specific levels and limits of these values may vary from site to site**
For blood coagulation abilities:
  PT
  PTT
  Platelet count

## Slide 19: Relevant Lab Work/Medication
Considerations:
CT exams performed for fluid drainage, and biopsies, may result in excess bleeding
Patients who are taking anticoagulants/blood thinners may be directed to temporarily discontinue these medications prior to their procedure
  Reduces risk of excessive bleeding

## Slide 20: Objective 6.4
Obtaining an appropriate medical history is vital to the CT exam.
Includes:
  Double identification
Helps ensure:
  Patient safety
    Example: contraindications, premedication's, pregnancy
  Proper protocol selection
    Example: contrast type & administration method(s)
  The radiologist has all relevant information required to interpret & report the study images

## Slide 21: How to Question a Patient
Address the patient by name
Ask focused, open-ended questions
Listen to the patient
  Encourage patients to tell you about their condition & symptoms
  Allow the patient enough time to respond &/or ask questions
Acknowledge patient responses
  Use Non-verbal
    Tactile
  &/or verbal communication techniques
    Reflective speech
Record all pertinent information

## Slide 22: Patient Consent
Any form of consent must be acquired before scan acquisition.
Basic consent is required for all routine exams
All CT scans performed with the use of IV contrast require informed/written consent
  All invasive procedures require signed consent
    Due to the possibility of adverse reactions
Consent is only valid when the patient is considered competent to make the decision
  Consent must be voluntary
    Patients cannot be under the influence of substances

## Slide 23: Consent Considerations
Immobilization devices require basic consent.
The reason for using the device must be explained to the patient
Used for:
  Patient safety
  Reminders to hold still throughout the procedure
    Improves the quality of the exam

## Slide 24: Informed Consent Considerations
Before obtaining informed/written patient consent:
Verify appropriateness of protocol selection
Identify any possible contraindications
  Information that may suggest a change of protocol or an alternate exam modality, such as:
    Previous contrast reaction or other allergies
    Asthma
    Kidney disease
    Diabetes
    Medications
      Example: Blood thinners, Metformin, Interleukin-2
    Patient Condition

## Slide 25: Objective 6.5
Patients should be instructed to remain in the imaging department (waiting area) for a minimum of 10 minutes following an IV contrast media procedure.
Technologists should assess the patient prior to dismissing them from their care
  In-Patients should be directed to their next exam/appointment or transported back to the appropriate unit
Remind patients to hydrate for a 24 hour period, post exam
If medication was restricted (ex. Metformin), remind the patient not to resume consumption until the appropriate lab work has been completed, and they confirm with their referring physician

## Slide 26: Summary
For every CT examination you should do the following:
Room prep
Verify order
Verify patient id.
Obtain medical history
Explain the exam & obtain consent
Continually assess the patient

## Slide 27: Things To Take Away
Know your role:
  Consent
  Post-procedure care
Requisitions:
  Protocol selection
    Check relevance/appropriateness
    Relevant lab work
How to question a patient:
  Focused questions
  Reflective speech
  Tactile