## Slide 1: MRAD 204: Radiographic Technique 1
Outcome 1-5:
Positioning –Wrist & Scaphoid

## Slide 2: Affiliated Readings
Module 3
Bontrager
Pgs: 153→156
Pgs: 162→163

## Slide 3: Overview
Guidelines/Considerations
Protocols
Positioning

## Slide 4: Guidelines/Considerations
Identify required anatomy
Scaphoid radiographs require metacarpal bases, and distal radius
SAIT Image Critique Handbook
R
Wrist radiographs require 2’ of distal forearm AND ½ of the metacarpals

## Slide 5: Guidelines/Considerations
2. Select appropriate equipment/technical factors
*For CR, always use the smallest cassette size
100cm SID, measured manually
On the console, select:
  “free cassette”
  the projection you will begin positioning
*Wrist technique = *55→70 kVp (PA = 55-65; Obl. & Lat. = 60-70)
*Scaphoid technique = 55→65 kVp

## Slide 6: Guidelines/Considerations
Setup room before bringing the patient in
  Note: can be done at either end of table
Ensure the table IR is not directly under the cassette
Tube and IR aligned using 100cm SID
Field size matches size of IR
Correct anatomical marker selected

## Slide 7: Guidelines/Considerations
3. Artifact Removal
Only anatomy of interest should appear in the light field & over the active surface of the image receptor
Ensure the marker is NOT placed under “anatomy shadow”
Notes: when the patient is in the room:
Best practice to have patient facing you
Do NOT let their legs go under the x-ray table/IR
Use external landmarks when positioning

## Slide 8: Wrist Protocol
Routine:
PA
PA Oblique (45o anterior oblique)
Lateral

## Slide 9: Positioning – PA Wrist
Center the anatomy on the IR
Align the length of anatomy with the length of IR
Position the forearm on the same horizontal plane & ensure the elbow and wrist are aligned
“Arch” hand slightly (make an arch)
Use external landmarks to set an appropriate field size
Place an anatomical marker (using Anderson Marker Rules), & adjust collimation as needed

## Slide 10: Positioning – PA Wrist
*At least 1½ inches of anatomy proximal to the ulnar styloid process must be over the active surface of the IR
(ensures 2 inches of distal forearm included)
CR is over the “bend” in the wrist (aka. halfway between the ulnar styloid process and base of 1st metacarpal)
Hand & Wrist parallel to length of IR
Fingers flexed to place entire wrist flat against IR
*At least 1/2inch of light beyond required anatomy*
Radiograph must include @ least ½ metacarpals & 2 inches of distal forearm
Marker on lateral side

## Slide 11: Positioning – PA Oblique Wrist
Center the anatomy on the IR
Align the length of anatomy with the length of IR
Position the forearm on the same horizontal plane & ensure the elbow and wrist are aligned
Rotate wrist laterally 450
Use external landmarks to set an appropriate field size
Place an anatomical marker (using Anderson Marker Rules), & adjust collimation as needed
Remember to change cassettes

## Slide 12: Positioning – PA Oblique Wrist
*At least 1½ inches of anatomy proximal to the ulnar styloid process must be over the active surface of the IR
(ensures 2 inches of distal forearm included)
CR is over the wrist joint
(aka. halfway between the ulnar styloid process and base of 1st metacarpal)
Hand & Wrist parallel to length of IR
*At least 1/2inch of light beyond required anatomy*
Radiograph must include @ least ½ metacarpals & 2 inches of distal forearm
Marker on lateral side
Styloid processes (of radius & ulna) form a 450 angle to the anterior surface of the IR

## Slide 13: Positioning – Lateral (lateromedial) Wrist
Center the anatomy on the IR
Align the length of anatomy with the length of IR
Position the forearm on the same horizontal plane & ensure the elbow and wrist are aligned
Position styloid processes perpendicular to IR
Use external landmarks to set an appropriate field size
Place an anatomical marker (using Anderson Marker Rules), & adjust collimation as needed
Remember to change cassettes

## Slide 14: Positioning – Lateral Wrist
*At least 1½ inches of anatomy proximal to the ulnar styloid process must be over the active surface of the IR
(ensures 2 inches of distal forearm included)
CR is over the wrist joint
(aka. halfway between the ulnar styloid process and base of 1st metacarpal)
Hand & Wrist parallel to length of IR
*At least 1/2inch of light beyond required anatomy*
Radiograph must include @ least ½ metacarpals & 2 inches of distal forearm
Marker on anterior side
Styloid processes (of radius & ulna) perpendicular to the anterior surface of the IR
*Thumb in a PA position* (not superimposing metacarpals)

## Slide 15: Scaphoid Protocol
Routine:
PA with ulnar deviation
150 PA Axial
Note: number of views/projections (and angles used) is work-site dependent

## Slide 16: Positioning – PA Scaphoid
Set a field size (just large enough for a “clear” anatomical marker to fit into each square of light)
Center the anatomy on the IR
Ensure the elbow and wrist are aligned, and on the same horizontal plane
Have the patient apply ulnar deviation
Place an anatomical marker (using Anderson Marker Rules), & adjust collimation as needed

## Slide 17: Positioning – PA Scaphoid
CR is over the scaphoid
(aka. halfway between the ulnar styloid process and base of 1st metacarpal)
Marker on lateral side
Wrist ulnar deviated
(until 1st metacarpal aligned with distal radius)
Light-field extends:
Distally: to ~½ of 1st metacarpal
Proximally: to ~ level of ulnar styloid process
Light-field extends:
Laterally: to include entire marker
Medially: to ~ mid-wrist (or “edge” of ulnar styloid process)

## Slide 18: Positioning – 150 PA Axial Scaphoid
Set a field size (just large enough for a “clear” anatomical marker to fit into each square of light)
Center the anatomy on the IR
Ensure the elbow and wrist are aligned, and on the same horizontal plane
Have the patient apply ulnar deviation
Place an anatomical marker (using Anderson Marker Rules), & adjust collimation as needed
Note: CR must be angled “towards the elbow”
Remember to change cassettes

## Slide 19: Positioning – 150 PA Axial Scaphoid: Notes
Move the patients body, so the tube is only aiming towards the elbow

## Slide 20: Positioning – 150 PA Axial Scaphoid
CR is over the scaphoid
(aka. halfway between the ulnar styloid process and base of 1st metacarpal)
Marker on lateral side
Wrist ulnar deviated
(until 1st metacarpal aligned with distal radius)
Light-field extends:
Distally: to ~½ of 1st metacarpal
Proximally: to ~ level of ulnar styloid process
Light-field extends:
Laterally: to include entire marker
Medially: to ~ mid-wrist (or “edge” of ulnar styloid process)

## Slide 21: Guidelines/Considerations - Notes
Identify required anatomy
  Joints proximal (elbow) and distal (wrist) to long bones MUST be included in the radiograph
2. Select appropriate equipment/technical factors
  Largest cassette is more commonly used for an adult forearm
*Forearm technique = 65→75 kVp
For Forearm imaging, follow all the same guidelines/considerations outlined earlier, making note of these differences:
Forearm radiographs require the proximal row of carpal bones, AND ½ inch proximal to the humeral epicondyles (to ensure olecranon process is included)

## Slide 22: Forearm Protocol
Routine:
AP
Lateral

## Slide 23: Positioning – AP Forearm
Center the anatomy on the IR
Align the length of anatomy with the length of IR
Position the entire upper limb on the same horizontal plane
Supinate the hand
Ensure humeral epicondyles are parallel to IR
Use external landmarks to set an appropriate field size
Place an anatomical marker (using Anderson Marker Rules), & adjust collimation as needed

## Slide 24: Positioning – AP Forearm
CR is ~mid forearm
Marker on lateral side
Hand supinated
Light-field extends:
Distally: to base of metacarpals
Proximally: to ~ level of humeral epicondyles (aka. ~ ½ inch proximal to the elbow joint/”crease”)
Light-field extends “side-side” to include @ least ½ inch beyond soft-tissue margins
Humeral epicondyles parallel to IR
Entire upper limb on same horizontal level

## Slide 25: Positioning – Lateral Forearm
Center the anatomy on the IR
Align the length of anatomy with the length of IR
Position the entire upper limb on the same horizontal plane
Flex the elbow 900
Ensure styloid processes (of radius/ulna) & humeral epicondyles are perpendicular to IR
Use external landmarks to set an appropriate field size
Place an anatomical marker (using Anderson Marker Rules), & adjust collimation as needed
Remember to change cassettes

## Slide 26: Positioning – Lateral Forearm
CR is ~mid forearm
Marker on anterior side
Styloid processes of radius & ulna perpendicular to IR
Light-field extends:
Distally: to base of metacarpals
Proximally: to ~ ¼ distal humerus
Light-field extends “side-side” to include @ least ½ inch beyond soft-tissue margins
Humeral epicondyles perpendicular to IR
Entire upper limb on same horizontal level, with elbow flexed 900