## Slide 1: MRAD 204: Radiographic Technique 1
Outcome 1-5:
Image Critique – Elbow & Humerus

## Slide 2: Affiliated Readings
Bontrager
Pgs: 164→170
Pgs: 187 → 188
Emphasis on the “pink box” Evaluation Criteria

## Slide 3: Overview
Elbow – image critique
Humerus – image critique
Tips & Tricks

## Slide 4: Image Critique – Routine Elbow Projections
Anatomy
Ideally, ALL elbow radiographs should display:
Note: hanging protocol
1/3rd of the proximal radius and ulna (to include radial tuberosity)
Soft-tissue
Elbow joint
~¼ Distal humerus
R
R

## Slide 5: Image Critique – Routine Elbow Projections
Optimal density and contrast:
  no motion (i.e. blur)
  soft tissue margins visible
  clear bony trabecular markings
ALL routine elbow radiographs should display:
kVp range of 65→75
Exposure & Technique
R
R

## Slide 6: Image Critique – Routine Elbow Projections
Marker Placement &/or artifacts
No removable artifacts are visible
Marker placement; not obscuring anatomy of interest
AP, & AP Oblique’s (with Internal & External Rotation)
  Lateral side
Lateral
  Anterior side
R
R

## Slide 7: Image Critique – AP Elbow
Slight superimposition of radial head, neck & tuberosity, over the proximal ulna
Humeral epicondyles in profile
Open elbow joint
Olecranon process within the olecranon fossa
Anatomy aligned parallel to IR
R
Position
@ 65 kVp

## Slide 8: Image Critique – AP Elbow
Four sided collimation centered to mid-elbow joint
CR & Collimation
R

## Slide 9: Image Critique – AP Elbow: Internal Rotation
Coronoid process in profile & free of superimposition
Radial head & neck centered over posterior portion of proximal ulna
Medial epicondyle and trochlea elongated and in partial profile
Olecranon process within the olecranon fossa
Anatomy aligned parallel to IR
R
Position
@ 65 kVp

## Slide 10: Image Critique – AP Elbow: Internal Rotation
CR & Collimation
Four sided collimation centered to mid-elbow joint

## Slide 11: Image Critique – AP Elbow: External Rotation
Lateral epicondyle & capitulum in partial profile and elongated
Radial head, neck, and tuberosity free of superimposition by the ulna
Olecranon process within the olecranon fossa
Anatomy aligned parallel to IR
R
Position
@ 65 kVp

## Slide 12: Image Critique – AP Elbow: External Rotation
CR & Collimation
Four sided collimation centered to mid-elbow joint

## Slide 13: Image Critique – Lateral Elbow
Position
@ 65 kVp
Superimposed humeral epicondyles
Radial tuberosity superimposed over radial shaft
½ of radial head superimposing the coronoid process
Olecranon process seen in profile
900 Elbow flexion

## Slide 14: Image Critique – Lateral Elbow
CR & Collimation
Four sided collimation centered to mid-elbow joint

## Slide 15: Image Critique – Routine Humerus Projections
Elbow joint
Anatomy
Ideally, both projections should include:
SAIT MRT Image Critique Handbook
150
L
Bontrager pg. 188 Fig. 5.33
Shoulder joint
Soft tissue
Entire humerus

## Slide 16: Image Critique – Routine Humerus Projections
Optimal density and contrast:
  no motion (i.e. blur)
  soft tissue margins
  bony trabeculae
Both routine humerus radiographs should display:
kVp range of 70→85
R
Exposure & Technique

## Slide 17: Image Critique – Routine Humerus Projections
Four sided collimation centered to mid-humerus
R
CR & Collimation

## Slide 18: Image Critique – Routine Humerus Projections
No removable artifacts are visible
SAIT MRT Image Critique Handbook
150
L
Bontrager pg. 188 Fig. 5.33
Marker Placement &/or artifacts
Marker placement; not obscuring anatomy of interest
AP = Lateral side
Lateral = Posterior side

## Slide 19: Image Critique – AP Humerus
Position
@ 70 kVp
Epicondyles in profile
Greater tuberosity and humeral head in profile
Minimal superimposition of glenoid cavity and humeral head
Collimation “tilt” parallel to length of anatomy

## Slide 20: Image Critique – Lateral Humerus
Position
@ 70 kVp
Superimposed epicondyles
Lesser tuberosity shown in profile medially
Collimation “tilt” parallel to length of anatomy

## Slide 21: Tips & Tricks
Lateral elbow critiques #1:
Capitulum articulates with the proximal radius (head of radius)
Trochlea of the humerus articulates with the proximal ulna
  Superimposition = no articulation = no joint space
SAIT imaging library
Bontrager pg. 131 Fig. 4.16
SAIT imaging library

## Slide 22: Tips & Tricks
Lateral Elbow critiques #2:
Recall position of the capitulum = lateral side
Trochlea = medial side
VS
SAIT imaging library
Shoulder
SAIT imaging library
Wrist
Superior/Inferior position of the capitulum in relation to the trochlea = shoulder elevated/depressed. Shoulder elevated on this image.
Capitulum projected inferior to trochlea = shoulder was elevated above elbow
Anterior/Posterior position of the capitulum in relation to the trochlea = wrist elevated/depressed. Wrist is depressed on this image.
Capitulum projected anterior to trochlea = wrist was depressed below elbow

## Slide 23: Tips & Tricks
Proximal Humerus critiques #1:
Greater tubercle/tuberosity is superior to the lesser tubercle
Lesser tubercle/tuberosity is always closest to the coracoid process
Bontrager pg. 178 Fig. 5.2
https://sketchfab.com/3d-models/bony-elements-of-the-glenohumeral-joint-577fc05f069046d6a5759633587d5119
AP
Lateromedial
Superoinferior
https://www.earthslab.com/wp-content/uploads/2017/07/Scapula-intro-front.jpg

## Slide 24: Tips & Tricks - Humerus
Greater tubercle anterior = A (neutral rotation, palm facing femur, side of body)
Lesser tubercle medial = B
Bontrager pg. 183 Fig 5.16, 5.18 & 5.20
Greater tubercle lateral = A (external rotation, palm facing forward, anatomical)
Lesser tubercle medial = B
Greater tubercle superimposing humeral head = A (internal rotation, back of hand to femur)
Lesser tubercle in profile medially = B
Greatest amount of glenoid fossa superimposition
Notes: Lesser tubercle is always medial – but in profile medially with internal rotation
Greater tubercle is in profile laterally on external rotation
Note: obvious “bump” when greater tubercle is in profile laterally with external rotation
With neutral rotation the humeral head looks fairly rounded, with a general greater tubercle superimposition on the anterior side
With internal rotation their becomes a more obvious “lump” on the media side

## Slide 25: Tips & Tricks – Which is Which?
Proximal Humerus critiques #2:
Remember anatomical relationships
https://quizlet.com/241427979/ap-shoulder-neutral-rotation-diagram/
Sait Imaging Library
Sait Imaging Library
Note appearance of greater and lesser tubercles as the humerus is rotated