## Slide 1: MRAD 256 Radiographic Technique 2
Positioning of the mandible and TMJ’s

## Slide 2: Routine Mandible Protocol
Regular routine:
PA (w/ OML┴ to IR)
35˚ axial Towne (for rami and condyles)
Bilateral - 25˚ Axiolateral Oblique projections (0° rotation)
Alternative for those who can’t hold the Townes
25˚ PA axial (as per CAMRT competency guide)

## Slide 3: PA Projection – Page 430
Place OML perpendicular to IR
Align MSP to long axis of the IR
CR to exit at lips
Check for rotation and tilt
Collimate to include entire mandible
Suspend respiration

## Slide 4: PA Mandible
Bontrager 11-160
Merrill’s 11-132

## Slide 5: Evaluation Criteria
  Mandibular rami and lateral portion of body are seen free of superimposition
  Anterior body and mentum is seen superimposed over cervical spine
  No rotation or tilt

## Slide 6: 35˚Axial Townes – pg. 431
  Place OML perpendicular to the IR
  Use a 35°angle to ensure the mandibular condyles are thrown inferior to the mastoid tips.
  Collimate to include rami (EAM to gonion)
Bontrager 11-163

## Slide 7: 25º PA axial
If the Townes image is not possible due to patient condition, this image is taken in lieu
Bontrager 11-116

## Slide 8: Evaluation Criteria
  Mandibular rami (condyles to gonions) are shown
  No rotation or tilt
Bontrager 11-162

## Slide 9: Axiolateral Oblique Bontrager Version
15° head tilt + 10° cephalad tube angle OR 25° cephalad angle on tube with no head tilt.
Place head in true lateral, with the side of interest at the IR
Have patient close mouth, with teeth together
Rotate head to place the anatomy of interest parallel with the IR AS REQUIRED: 1) ramus 0º
Body 30º 3) Mentum 45º
With no head tilt, CR to exit at level of required anatomy
With head tilt, CR to enter at level of 5cm below the upside mandibular angle, to exit in middle of required anatomy
Move gonion off of cervical spine
Collimate to include the anatomy closest to the IR, which is the side of interest

## Slide 10: Axiolateral Oblique – pg. 429
Posterior obliques are easier for most people than anterior obliques
Bontrager (8th ed.) 11-152,153
TMJ
Mentus

## Slide 11: Axiolateral Oblique
CR @ 25° cephalad

## Slide 12: Evaluation criteria
Anatomy of the side closest to IR is visualized: ramus, condylar process, coronoid process, body and mentum
No superimposition of side farthest from IR
No superimposition of c-spine over mandible
Anatomy of interest demonstrated in profile, with minimal foreshortening
Bontrager 11-152,155

## Slide 13
Case courtesy of Mr. Dom LeGros, Radiopaedia.org, rID: 40540

## Slide 15: Routine protocol for TMJ’s
AP modified Towne (35˚)- pg. 434
Bilateral axiolateral (Schullers)
- open and closed mouth- pg. 436
Panoramic Tomography (site dependent)- pg. 433

## Slide 16: 35˚Axial Townes – pg. 434
  Place OML perpendicular to the IR
  Use a 35° angle to ensure the manibular condyles are thrown inferior to the mastoid tips.
  Collimate to temporomandibular joints only
Bontrager 11-175

## Slide 17: Axiolateral TMJ (Schuller method)
Angle 30˚ caudad
Place patient in true lateral, side of interest on the IR
Adjust CR to enter 1-1.5 cm anterior, and 5 cm superior to the upside EAM
CR will exit at downside level of downside TMJ / EAM
Collimate to include downside TMJ
Place an anatomical and “closed” marker in light field
Change markers, and take a second image with patient’s mouth open
Bontrager 11-181,182,183,184

## Slide 18: Evaluation Criteria
Closed mouth
Posterior teeth must be in contact. In normal patient the condyle will be visualized in the temporomandibular fossa
Open mouth
Mouth should be open as wide as possible, but without the mandible jutting forward. In normal patient the condyle will be visualized anterior and inferior to the temporomandibular fossa

## Slide 19: Evaluation criteria
Open
Closed
Bontrager 11-181,182,183,184

## Slide 20: Orthopantomography
Bontrager 11-169, 11-170

## Slide 21: Panorex Read page 433 Bontrager
Condyles perpendicular to the bottom edge of the IR and equidistant from the coronoid process
Right and left structures will be symmetrical
Bontrager 11-174