## Slide 1: RADP 215: Radiation Protection
Radiation Protection Concepts

## Slide 2: Risk vs. Benefit
Benefit
  Advantage or good result arising from a specific activity
Risk
  Probability of injury, ailment or death resulting from an activity
Effective communication of the benefits compared to risk of the procedure is very important
  Exposure should always be kept at the lowest possible level for the public

## Slide 3: Risk vs. Benefit (cont’d)
Decision about whether the x-ray is taken is the patient’s
Patient that understands the procedure is more likely to consent and cooperate
When someone is injured a decision must be made: is the risk worth the diagnostic data gained?

## Slide 4: Risk vs. Benefit (cont’d)
Exposure to the radiation must be considered as a benefit and risk
Technique must be as low as possible but still enough to obtain a diagnostic image
Be mindful of techniques to keep a balance between the possible damage to tissue and value of the diagnostic data collected

## Slide 5: Risk vs. Benefit (cont’d)
With digital post-processing capabilities, “dose creep” can occur
Every manufacturer has specifications for the range of the exposure index
Phillips – Exposure Index (EI) is 100–300 and 450 for chest
  Above Range – overexposure
  Below Range – underexposure

## Slide 6: Risk vs. Benefit (cont’d)
Patients should be the only person exposed to the primary beam.
Primary radiation worker (Tech) should never be exposed to a primary beam while working.
Technologists are predominantly exposed to secondary radiation (scatter and leakage).

## Slide 7: Risk vs. Benefit (cont’d)
Chronic low doses of radiation could have damaging effects if radiation protection principles are not applied by a primary radiation worker.
Radiation workers are exposed to low dose scatter every day.
Must be aware of the risk and benefits of the decisions that are made while working in the radiation environment.
  E.g., holding or restraining patients

## Slide 8: Three Cardinal Rules of Protection
Time
Distance
Shielding

## Slide 9: Time
Reduce the amount of time in the area of radiation
Double the time, double the exposure
We may have to stay with our patients, but try to limit this
Do not routinely hold patients
Fluoroscopy is the largest contributor to chronic low-dose exposure for a technologist

## Slide 10: Time (cont’d)
Fluoroscopy can go on for several minutes up to several hours
Technologist caring for the patient must be in the room—be aware of the “beam on time”
Ensure that all the protective equipment is worn and utilized
Stay behind protective barriers as much as possible and limit amount of time spent near beam

## Slide 11: Distance
Distance is the most effective means of reducing radiation exposure
Patient is the source of most of the exposure to technologists
Exposure switch must not be located in the room so the tech can remain behind the barrier
Increase the distance between you and the beam wherever possible
  I.e., while using mobiles, OR and fluoroscopy

## Slide 12: Distance (cont’d)
Inverse Square Law (ISL)
  Intensity of radiation at a given distance from a point source is inversely proportional to the square of the distance.
I1
I2
(d1)²
(d2)²
=

## Slide 13: Inverse Square Law
If the distance between you and the beam is increased, what is the reduction in exposure?
  Exposure is 9 mGy at 1 metre
  What is it at 2 metres?
9 mGy
I2
(1 m)²
(2 m)²
=
= 2.25 mGy @ 2 metres

## Slide 14: Inverse Square Law (cont’d)
What is it at 3 metres?
Reduced by a factor of (3)2 or by 9
You would get one ninth of the original scatter
2.25 mGy
I2
(2 m)²
(3 m)²
=
= 1 mGy @ 3 metres

## Slide 15: Why is the Formula Important?
Cardinal rule for distance as a radiation protection tool
If distance between an individual and the x-ray source or scatter is cut in half, the intensity will increase by a factor of four
For every metre that the technologist stands closer to the patient or source of radiation, their exposure increases 4 times

## Slide 16: Distance
Intensity of an x-ray beam decreases as the individual moves further away from it
There are the same rules for the number of photons in the scatter, but they are more spread out over a larger area
If the distance between you and scatter is doubled, intensity of the scatter photon will have less energy

## Slide 17: Shielding
Use when time and distance are not an option
Any material will attenuate the beam
How much depends on atomic #, density and thickness of the material
There are several types of shielding:
  Primary or secondary (permanent)
  Fixed or mobile shields, in the room or worn

## Slide 18: Shielding (cont’d)
Radiation protection barriers
Who designs them?
  A diagnostic radiological physicist
Why?
  To protect staff and the public

## Slide 19: Structural Barriers
Structural barriers need to be classified as
  Primary
    Can be struck directly by the beam
      Wall behind the detector
        Needs 1/16th” of lead and 7’ from the floor
  Secondary
    Scattered and leakage radiation
      Wall 1/32nd” of lead

## Slide 20: What are the requirements?
Type of equipment, layout of the room, occupancy of adjacent rooms and other factors such as kVp
Protective barrier must be material that reduces radiation intensity—can be estimated by ½ value or 1/10th value layers
HVL/TVL is thickness of absorber that reduces intensity of ½ or 1/10th its original value

## Slide 21: Shielding
Permanent structures are the radiation protection barriers built into the department
Structural barriers
  Lead sheet – 1/16th, 1/32nd
  Concrete – 7.4 cm
  Lead glass – 1.5 mm
  Steel
  Lead-infused Acrylic – 30% less weight

## Slide 22: Shielding (cont’d)
Mobile shields like lead-equivalent aprons and gloves are used by individuals
Mobile barriers
  Aprons – 0.25, 0.5 or 1.0 mm
  Gloves – 0.25–0.5 mm
  Thyroid collars – 0.5 mm
  Lead glasses – .35 mm
  Lead walls mounted on wheels

## Slide 23: Lead is a Balance
It is standard to wear 0.5 mm of lead equivalent for a 100 kVp beam
Slightly higher for some wraparound aprons
Increase lead, increase protection
Increase lead, increase weight
Remember, we may be wearing lead for hours so wear it properly!

## Slide 24: Protective Devices
Ensure that protective devices are worn by all personnel.
  Nurses, physicians, aides in the vicinity of the beam or scatter
Be aware of who is in the room, coming in or leaving.
Everyone in the vicinity should be aware of an exposure.
    Call a warning: “x-ray”

## Slide 25: Reducing Dose in Other Ways
Correct Collimation
  Gonads, breast tissue and thyroid avoided if possible
Minimize exposure to children and adolescents
  Benefit must outweigh risk

## Slide 26: Reducing Dose in Other Ways (cont’d)
Appropriate technique selection
  Higher kVp and lower mA when possible
Maintain sensitivity of imaging system
  Higher sensitivity equipment decreases dose
Correct positioning of anatomy
  Reduce the repeats

## Slide 27: International Agencies
International Commission on Radiological Protection (ICRP)
  Authority on the safe use of ionizing radiation
National Council on Radiation Protection and Measurements (NCRP)
  Incorporates ICRP recommendations

## Slide 28: International Agencies (cont’d)
United Nations Scientific Committee on the Effects of Atomic Radiation (UNSCEAR)
  Formulates radiation guidelines
National Academy of Sciences/National Research Council on Biological Effects of Ionizing Radiation (NAS/NRC-BEIR)
  Reviews studies of biological effects

## Slide 29: International Agencies (cont’d)
Responsible for evaluating relationship between radiation and biological effects
Concept of radiation exposure and associated risk of malignancies is the basis of the effective-dose limiting system
Organizations serve as a resource for revised recommendations

## Slide 30: Safety Code and Personnel Radiation Safety
Safety Code 35 is issued by Health Canada.
Replaces the Safety Code 20A and 31
Sets out the requirements for the safe use of radiation
Contains personnel requirements, safety procedures, equipment and facility guidelines

## Slide 31: Safety Code and Personnel Radiation Safety (cont’d)
For any person concerned with equipment performance, image quality and radiation safety in a facility
Primary for instructions and guidance for radiation personnel employed in a facility
SC 35 regulations and publications are followed within Canada above all others

## Slide 32: Safety Code and Personnel Radiation Safety (cont’d)
SC 35 does not cover radiation protection for dental or mammography
Each have their own safety code
  SC 30 – Radiation Protection in Dentistry
  SC 33 – Radiation Protection in Mammography

## Slide 33: Radiation Emitting Devices (RED) Act
Standards for information, labelling, construction and performance of equipment with respect to radiation safety
All new, used and refurbished medical x-ray equipment and accessories in Canada must meet the RED act regulations

## Slide 34: Diagnostic Reference Levels (DRL)
Dose guidelines for typical exams based on standardized patients and phantoms
Promotes better control of patient exposures
Facilities should strive to meet these levels, but may not always be possible
Normally reviewed annually

## Slide 35: Diagnostic Reference Levels (cont’d)
Beneficial in large dose examinations where large reductions are possible
  CT
May lead to large reductions in the collective dose in exams done frequently or for young patients
  Chest x-rays
  Pediatrics