## Slide 1: RADP 215: Radiation Protection
Evaluate Patient Radiation Dose

## Slide 2: Radiation Terms Review
Absorbed Dose (D): Radiation energy absorbed per unit mass. J/kg or Gy
Equivalent Dose (EqD): Dose quantity that takes into account the type of radiation used. Provides an indication of the potential for biological effects. Used for risk comparisons between different types of radiation. Sv
Radiation weighting factor (W(R))
EqD = D x W(R)
Effective Dose (EfD): Provides a measure of overall risk to humans from ionizing radiation. Takes into account the part of the body that is irradiated. Sv or mSv
Tissue weighting factor (W(T))
EfD = D x W(R) x W(T)

## Slide 3: Estimating Patient Dose
Patient exposure or dose can be established in three ways:
  Entrance Skin Dose (ESD) also known as Entrance Skin Exposure (ESE)
  Gonadal Dose
  Bone Marrow Dose
Pg. 566 Bushong, Sherer Tables pg. 33-34

## Slide 4: Entrance Skin Dose/Exposure
ESE/ESD is widely used in assessing patient dose
Personal Dosimeters determine skin dose
When actual patient measurements are not available, estimate measurements can still be easy to obtain
.
  Nomogram
  Output Intensity Charts

## Slide 5: Gonadal Dose
Genetically Significant Dose (GSD) is used to assess the impact of the gonadal dose on the population
GSD is the equivalent dose (EqD) that can bring about genetic injury
Bushong p. 569 (Table 37-1) shows the gonadal dose for specific exams

## Slide 6: Effects of Radiation on Gonads
Gonads are critically important target organs—very radiosensitive
Medical x-rays exposures are the major contributor of gonadal dose
Ovaries and testes both produce germ cells
Male and female gonads are affected differently by radiation
  This is due to differences in progression from stem cell to mature cell

## Slide 7: Testes
Testes contain both mature and immature cells
  Mature germ cells are non-dividing and less sensitive
  Immature cells are unspecialized and still dividing—extremely radiosensitive
Irradiation can lead to damage and reduction in number
Doses higher than 0.1 Gy may deplete mature sperm (maturation depletion)

## Slide 8: Testes
Temporary sterility can occur and last as long as 12 months with a dose of 2 Gy
  Sterility is temporary, but it may cause genetic mutations (chromosomal abnormalities) in future generations
Direct exposure may cause genetic effects
Recommended to refrain from family planning for 2–4 months after irradiation exceeding 100 mGy
Permanent sterility is most likely occur with a dose of 5–6 Gy

## Slide 9: Ovaries
Radiosensitivity of the ovaries varies throughout the stages of maturity
In the fetal stage and in childhood, the ovaries are very radiosensitive
Contain large number of stem and immature cells
Irradiation early in life can cause:
  Ovarian atrophy (ovaries reduce in size)
  Cell death

## Slide 10: Ovaries
Irradiation doses as low as 100 mGy may cause suppression and/or delay of menstruation
Radiosensitivity
  Increased in fetal stage and childhood
  Declines between 20–30 years
  Increases again at approximately 30 years and continues until menopause
Single dose of 2 Gy to the ovaries can cause temporary sterility
Permanent sterility is most likely to occur with a dose of 5–6 Gy

## Slide 11: RECAP
Doses in diagnostic imaging are low and chance of sterility is nil
High doses of radiation can cause atrophy
Radiation of the gonads could cause chromosomal abnormalities that are passed on to future generations
Best practices state, is the ALARA principle

## Slide 12: Bone Marrow Dose
Also called Mean Marrow Dose
Defined as the average radiation dose to all active marrow
Substantial exposure of ionizing radiation can deplete or destroy stem and blood cells
Dose to bone marrow may be responsible for radiation-induced leukemia
Cannot be measured directly, can only be estimated
Bushong p. 569 (Table 37-1)

## Slide 13: Diagnostic Reference Levels (DRL)
Dose guidelines for typical exams based on standardized patients and phantoms
Recommendations can be found in the SC 35 (Section A 3.5)
Promotes better control of patient exposures
Facilities should strive to meet these levels, but may not always be possible
Normally reviewed annually

## Slide 14: Diagnostic Reference Levels (cont’d)
Beneficial in large dose examinations where large reductions are possible
  CT
May lead to large reductions in the collective dose in exams done frequently or for young patients
  Chest x-rays
  Pediatrics

## Slide 15: Protection Standards
Four major organizations that are responsible for evaluating radiation doses risks and biologic effects:
  International Commission on Radiological Protection (ICRP)
  National Council on Radiation Protection and Measurements (NCRP)
  United Nations Scientific Committee on the Effects of Atomic Radiation (UNSCEAR)
  National Academy of Sciences/National Research Council Committee on the Biological Effects of Ionizing Radiation (NAS/NRC-BEIR)

## Slide 16: Purpose of the Groups
These groups help to form recommendations for:
  Effective Dose (EfD)
  Equivalent Dose (EqD) limits
Limits on radiation exposure are developed based on research and information from these groups.

## Slide 17: ICRP, International Commission on Radiological Protection
Considered the international authority regarding the safe use of ionizing radiation.
Evaluates information on biologic effects of radiation.
Provides radiation protection guidance through general recommendations on dose limits.

## Slide 18: NCRP, National Council on Radiation Protection and Measurements
US corporation
Non-governmental organization
Determines how ICRP recommendations are incorporated into US radiation protection criteria

## Slide 19: UNSCEAR, United Nations Scientific Committee on the Effects of Atomic Radiation
Helps form radiation protection guidelines.
Evaluates human and environmental ionizing radiation exposures.
Derives risk assessments from epidemiologic data and provides information to the other organizations for evaluation.
Takes the information from radiation and nuclear accidents and conducts follow-up studies to derive radiation risk assessments for cancer and genetic effects.

## Slide 20: NAS/NRC-BEIR, National Academy of Sciences/National Research Council Committee on the Biological Effects of Ionizing Radiation
Advisory group that reviews studies of biologic effects of ionizing radiation and risk assessment.
Studies groups such as early radiation workers, atomic bomb survivors and nuclear accident survivors.
Provides information to other organizations for evaluation.

## Slide 21: Reducing Patient Dose
Many methods can be used to reduce patient dose:
  Technical factors
  Collimation
  Filtration
  Equipment (e.g., grids, immobilization devices)
  Quality Control
  Communication
  Best Practice
  ALARA