## Slide 1: MRAD 204: Radiographic Technique 1
Outcome 1-5:
Image Critique – Pelvis & Hip

## Slide 2: Affiliated Readings
Bontrager
Pgs: 281, 283→286
Pgs: 288→290
Emphasis on the “pink box” Evaluation Criteria

## Slide 3: Overview
Image Critique – Pelvis
Image Critique – Hip
Tips & Tricks

## Slide 4: Image Critique – AP Pelvis
Anatomy
Ideally, routine AP Pelvic radiographs should display:
Entire Pelvis
Proximal femurs
R
R

## Slide 5: Image Critique – AP Pelvis
Routine AP Pelvic radiographs should display:
kVp range of 80→90
Optimal density and contrast:
  no motion (i.e. blur)
  soft tissue margins visible
  clear bony trabecular markings
Exposure & Technique
R
R
McQuillen Martensen 5th Ed. Pg.430 Fig. 7.4

## Slide 6: Image Critique – AP Pelvis
Marker Placement &/or artifacts
No removable artifacts are visible
Marker placement: lateral side between ASIS and greater trochanter; not obscuring bony anatomy
R
McQuillen Martensen 5th Ed. Pg.430 Fig. 7.4

## Slide 7: Image Critique – AP Pelvis
R
CR & Collimation
Four sided collimation centered to MSP & close to level of ASIS
SAIT Campus 2021

## Slide 8: Image Critique – AP Pelvis
Femoral necks in profile
Greater trochanters in profile
Lesser trochanters not visible (or barely seen) on the medial side
No rotation = symmetric iliac alae, ischial spines, and obturator foramina
Position
@ 80 kVp

## Slide 9: Image Critique – Routine Hip
Anatomy
Ideally, both routine Hip radiographs should display:
1/3rd of proximal femur
Body of ilium
R
McQuillen Martensen 5th Ed. Pg.430 Fig. 7.4
Upper Body of ischium
Body of pubis
Entire ORIF (if present)
Note: field size will need to be extended if patient has a long hip pin
*Note: AP Hip radiographs also require symphysis pubis

## Slide 10: Image Critique –Routine Hip
ALL routine hip radiographs should display:
kVp range of 80→85
Optimal density and contrast:
  no motion (i.e. blur)
  soft tissue margins visible
  clear bony trabecular markings
Exposure & Technique

## Slide 11: Image Critique –Routine Hip
Marker Placement &/or artifacts
No removable artifacts are visible
Marker placement: lateral inferior corner of light-field not obscuring bony anatomy
Bontrager 8th Ed. Fig. 7.73

## Slide 12: Image Critique –Routine Hip
CR & Collimation
Four sided collimation centered to femoral neck
*unless long ORIF device present
VS.

## Slide 13: Image Critique – AP Hip
Femoral neck in profile
Greater trochanter in profile
Lesser trochanters barely seen (or not seen at all) on the medial side
Bontrager pg. 288 Fig. 7.67
Femoral head seen through acetabulum
Position
@ 80 kVp

## Slide 14: Image Critique – Lateral Hip
Head of femur in acetabulum
Femoral neck foreshortened and superimposed by the greater trochanter
Acetabulum and Femoral head well demonstrated
Position
@ 80 kVp
Bontrager 8th Ed. Fig. 7.73

## Slide 15: Tips & Tricks – Pelvis Projections
AP Pelvis, Axial Inlet, and Judet Projections should demonstrate entire pelvis & proximal femurs
Look at overall appearance to determine projection:
AP Pelvis
Good overall radiographic appearance
Note: Symphsis pubis and ischium
Note: Illiac wing or ala & obturator foramen
Axial Inlet
Judet Projection
Bontrager pg. 284 & 286 Fig. 7.53 & 7.62

## Slide 16: Tips & Tricks – Axial Outlet Projection
The only pelvis projection that does not require demonstration of iliac crests & greater trochanters
Bontrager pg. 283 & 284 Fig. 7.50 & 7.53
VS.
Symmetric obturator foramina
Anterior pubic bones superimposed over sacrum & coccyx
Superimposed obturator foramina

## Slide 17: Tips & Tricks – Pelvis Rotation vs. Judet
AP pelvis with rotation will demonstrate asymmetrical obturator foramina
Judet projections will demonstrate one obturator foramina with complete superimposition
Look at overall appearance to determine if it was a Judet projection or mal-positioned AP Pelvis:
VS.
Bontrager pg. 284 Fig. 7.61
McQuillen Martensen 5th Ed. Fig. 7.5

## Slide 18: Tips & Tricks: Identifying Rotation
Look at the general shape/size of the obturator foramen & the alae (alae is plural for ala):
McQuillen Martensen 5th Ed. Fig. 7.5
“Smaller” obturator foramen
=
side of rotation
“Larger” ala = side of rotation
VS.

## Slide 19: Tips & Tricks – Pelvis/Hip: Review
Bontrager pg. 274 Fig. 7.26, 7.28, & 7.30
Look at the general shape/size of the lesser trochanter and femoral neck
Internal rotation = ↓ femoral neck superimposition

## Slide 20: Tips & Tricks – Lateral Hip Projections
Look at the size/shape of the pelvis to determine the projection:
AP Hip
*Note: “Open” obturator foramen
*Note: Acetabulum size & foreshortened obturator foramen
*Note: superimposed obturator foramen
Lateral Hip
Axiolateral (x-table)
SAIT Imaging Library
Bontrager pg. 288 Fig. 7.67
Bontrager 8th Ed. Fig. 7.73

## Slide 21: Tips & Tricks – Lateral Hip Projections
McQuillen Martensen 5th Ed. pg. 442, 444 & 445 Fig. 7.36, 7.43 & 7.46
Frog leg (modified cleaves): 45° abduction from vertical: femoral neck partially foreshortened & lesser trochanter in profile medially
Lauenstein-Hickey: 90° abduction from vertical (aka. femur parallel to IR: Femoral neck foreshortened, acetabulum and femoral head well demonstrated
20° abduction from vertical: femoral neck in profile, foreshortening of body of proximal femur