## Slide 1: APPH 226: Exposure Factor Selection and Technique Charts
Objectives: 11.1-11.4

## Slide 2: Purpose
Why do we need a technique chart?
  To provide a level of consistency among images and radiographers
  Standardizes selection of exposure factors to help the technologist produce quality radiographs and keep patient dose to a minimum

## Slide 3: Technique Charts
Designed for the average patient and do not account for unusual circumstances
Technologist still needs to assess the patient
  require patient assessment and appropriate adjustments – body habitus, pathology, condition
  Certain conditions may require an increase/decrease in technique
Helps ensure that there is consistent image quality throughout the entire dept, also decrease the number of repeats (reduce patient exposures)

## Slide 4: Digital Systems
Just as important for digital systems as well as conventional
Wide dynamic range
System compensates for poor exposure factor selection
  Could be over exposing patient without knowing
  Important to check EI numbers
  Images may still appear diagnostic regardless of over/under exposure

## Slide 5: Conditions
Separate technique chart should be established for each x-ray tube
  Even if they share the same generator
Every portable must also have its own technique chart
Standardization of positioning techniques throughout department
  Positioning, accessory equipment, IR type, grid ratio
  Decreases number of variables from case to case
    Collimation, filtration, SID, IR speed/type
    Positions, grid usage

## Slide 6: Conditions
For technique charts to be effective:
Equipment must be calibrated
  Accuracy of factors is important
  Quality control program in place will ensure consistency of equipment performance
Image processing must be consistent through the department

## Slide 7: Main Types - Variable kVp/ fixed mAs
Variable kVp/ fixed mAs
  Based on the concept that kVp can be increased as anatomic part size increases
  Basic characteristic of this chart is an inherently short scale of contrast
    Typical exposures will be higher contrast due to the use of lower kVp
  +2 kVp for every additional cm of part thickness
  Accurate measurement of part is critical for this type of technique chart
    calipers

## Slide 8: Main Types - Variable kVp/ fixed mAs
Variable kVp/ fixed mAs
  Changing kVp values for variations in part thickness may be ineffective throughout the entire range of radiography exams
    Only effective for pediatrics or small extremities – small changes in kVp more effective at low kVp levels than changing the mAs
    Cons:
      less latitude for error, adequate penetration of large parts is not always assured, increased patient dose

## Slide 9: Main Types - Fixed kVp/variable mAs
Fixed kVp/variable mAs
  Uses concept of selecting optimal kVp for exam, and adjusting mAs for variations in part thickness
  Most common type of chart
  Optimal kVp: high enough to penetrate the body part
  For each part, there is an optimum kVp and mAs is adjusted for part thickness

## Slide 10: Theoretically
X-rays are attenuated exponentially, meaning…
  For every 4-5 cm change in part thickness, the mAs should be adjusted by a factor of 2
  E.g. if a knee measures 10cm, and the technique is 70 kVp @ 6 mAs, and another knee measures 14 cm, the new technique will be 70 kVp @12 mAs
  Thickness groups of 4-5 cm can be made, instead of thickness changes in increments of 1 cm
  mAs can be adjusted by 30% or factors of 2 (1/2 or doubling) – depends on site criteria

## Slide 11: Stages of Development
Set appropriate kVp for the anatomical part
Using a phantom, determine the mAs that produces desired radiographic density and exposure index
Using a calculator, extrapolate the techniques for changes in part thickness (small, large)

## Slide 12: Comparative Anatomy
What if there is no technique for the part you are imaging? What if it isn’t on the list?
  Then you choose another anatomical part that has similar thickness/composition
  E.g. knee and shoulder

## Slide 13: High kVp technique chart
This is another type of technique chart using kVp settings greater than 100
  Ideal for barium exams to ensure adequate penetration of the barium
  Also can be used for chest imaging
Preparation of this type of chart is basically the same as preparing for the fixed kVp technique chart
All exposures for a specific anatomical part will use the same kVp
Using a phantom, determine the mAs that produces the desired radiographic density

## Slide 14: Readings
Radiologic Science for Technologists 11th Ed
  Pg 252-256 (Radiographic Technique Charts, stop before Automatic Exposure Techniques)