## Slide 1: APPH 226: Repeat and Reject Analysis
Objectives: 10.1, 10.3, 10.4

## Slide 2: Ideally….
An x-ray exam will result in:
  Creating diagnostic image
  Correct diagnosis by physician
  Satisfaction of all customers (internal and external)
    Patient, referring physician

## Slide 3: Outcomes Assessment
Includes:
  Repeat analysis
    To avoid future repeats
  Artifact analysis
    Identify cause of the repeat
  Accuracy, sensitivity and specificity analysis
    Analysis of the combination of image quality and correct diagnosis

## Slide 4: Repeat Analysis
Process where rejected images are catalogued and classified with reasons for repeat
Provides information regarding equipment performance, department procedures and staff skill levels
Helps to develop solutions to decrease the number of repeats
Can document effectiveness of QC and QA procedures

## Slide 5: Advantages of Analysis
Three main advantages of repeat/reject analysis
  Improved department efficiency
    With decreased repeats, amount of time that patients spend in the department is reduced.
    Increase patient satisfaction, decrease wait times, more patients can be x-rayed
  Lower costs
    Equipment usage costs
    Decreased wear on equipment (tube, IR)
  Lower patient doses
    Less exposure if images only need to be done once

## Slide 6: Analysis
Needs to include:
  Procedures in department
  Possible causes
When analysis is done, should determine the:
  Causal repeat rate
  Total repeat rate

## Slide 7: Causal Repeat Rate
With QC program in place, most repeats are due to positioning errors
Recommended for repeat analysis to be performed by the same person to ensure maximum consistency
  Commonly done with worksheets
  Need large sample for reliability
    Usually at least 250 patients

## Slide 8: Causal Repeat Rate
Is the percentage of repeats from a specific cause (positioning)
= # of repeats from a specific cause X 100
total # of repeats

## Slide 9: Total Repeat Rate
= # of repeats X 100
total # of views

## Slide 10: Repeat Rate
Affected by:
  Quality of equipment
  Staff skill level
  Patient type
  Data collection method
  Radiologist

## Slide 11: Repeat Rates
General X-ray
  Should be less than 4-6 %
Mammography
  Should be less than 5%
If the repeat rate is greater than 10-12%, it needs to be investigated

## Slide 12: Repeat vs Reject
What is a reject exposure?
  An exposure that did not require a repeat exposure on a patient
    Test images
    QC

## Slide 13: What if the Repeat Rate is 0%?
Possible that it is the most amazing department ever!
More likely:
  Low rate of technologist cooperation
  Do not have right information
  Very lenient radiologist
  **Any repeat rate less than 2%, should be skeptical (not accurate).

## Slide 14: Results
Never single out a radiographer
Constructive feedback should be given to the entire department
  Work together to improve the rate
    Inservices, equipment maintenance, support
      Depends on the reason for the repeats, which is why that information is so critical
        Without knowing why repeats are happening, cannot improve
Reflects upon entire department, not just radiographers
  QC, Management, radiologists
Remember: without technologist compliance, the results will be inaccurate

## Slide 15: Readings
Radiologic Science for Technologists 11th Ed
  Pg 396
  Pg 590 (Repeat examinations)