## Slide 1: APPH 226: Density - Part II
Objectives: 3.1-3.4, 4.3, 5.2, 5.4

## Slide 2: Latent Image
Occurs immediately after exposure, but before processing
Invisible
This happens to all images, regardless of how it is acquired
  Film
  Digital (DR)
  CR

## Slide 3: Image Formation
How do we get it?
  Result of differential absorption of the x-ray beam
Differential absorption is:
  Process where some of the beam is absorbed and some is transmitted
  It’s called differential because the beam is not absorbed to the same degree over the entire area exposed

## Slide 4: Differential Absorption
Creates an image that represents the structures of anatomy
  Results from the variation between absorption and transmission
When an image is created this way, several processes are required
  Occurs in beam _________________

## Slide 5: Beam Attenuation
When the primary x-ray beam passes through tissue and loses some of its energy
  This reduction is known as attenuation
Attenuation consists of
  Absorption
  Scattering
  Photon Transmission

## Slide 6: Absorption
Interaction called:
  _____________________________
    Complete absorption of x-ray photon
    Inner shell electron ejected
      Photoelectron
    Outer shell electron drops to fill the spot
    Characteristic radiation emitted
      Low energy – usually remains in the body
    Atom is ionized

## Slide 7: Absorption
Probability of PE interactions increases if:
  Energy levels are __________ together
    Binding energy of inner shell electron and energy of incoming x-ray photon
    the closer they are, the higher the odds of PE occurring
    Complete absorption of the x-ray photon
What other interactions are classified as absorption?
  Pair Production and Photodisintegration

## Slide 8: Scattering
What interaction would this be?
_______________
  Incoming x-ray photon is not absorbed
  Ejects outer shell electron
    Compton electron, secondary electron
  X-ray photon loses energy, changes direction
    Can go onto interact with IR
    Can leave body

## Slide 9: Scattering
What else would be in this category?
__________________
  Not significant
  Occurs with very low energy x-rays
  Can interact with IR, but very minimally
  In diagnostic ranges, very little contribution is from coherent scatter

## Slide 10: Scattered Photons
Why is this an issue?
If they reach the IR:
  Degrade image
  Contribute nothing useful to the image
  Also known as image fog

## Slide 11: kVp and Image Fog
When kVp is increased, there are:
  Fewer interactions in total
  Increased amount of x-rays transmitted
  Increased Compton scattering
Scatter radiation creates unwanted exposure on the image called fog
  Does not offer any useful information

## Slide 12: Scatter and Image Fog
Therefore… when kVp is increased, the amount of fog is increased
  How is density affected?
    Increased fog will increase overall image density
  How is contrast affected?
    Increased fog leads to a decrease in contrast

## Slide 13: Scattered Photons
If they are absorbed:
  Contribute to the patient’s radiation exposure and increases their dose
If they leave the body and don’t reach the IR:
  Contribute to the dose of anyone near the patient

## Slide 14: Transmission
Defined as: the x-ray photon passes through to the image receptor
  Direct transmission
  Indirect transmission

## Slide 15: Exit Radiation
= transmitted and scattered radiation
= (direct and indirect transmission)
Amounts of absorption and transmission are varied
  Differential absorption

## Slide 16: On the Image…
White
  Areas of Absorption
  Photoelectric Interactions
Black
  Transmission
  High radiographic density
Grey
  Mix of both absorption and transmission

## Slide 17: Exponential Absorption
As x-rays pass through tissue, there is no fixed range to describe how far they go
Attenuated exponentially
For every increment of thickness, the x-rays are decreased in number, by a certain percentage
Never reaches zero

## Slide 18: Factors
In order to select an optimal radiographic technique, three groups of factors must be considered:
  Image Quality factors
  Exposure Technique factors
  Patient factors

## Slide 19: Distance and Density
SID
  Source to Image Distance
  Aka FFD (Focus to film distance)
  Intensity changes with distance
    Inverse Square Law

## Slide 20: Inverse Square Law
=

## Slide 21: SID
As the distance between the focal spot and the image receptor changes – the intensity of the radiation will change also
  You’ll notice as the distance is increased, the light covers a larger area

## Slide 22: SID
What happens to the number of photons as the area is increased?
  The same number of photons
  Larger area means:
    Same number of photons covering a larger area, so less density

## Slide 23: SID
What happens to the image?
  Because it is receiving less radiation, there will be less radiographic density
What if we have a very short SID?
  The reverse is true
  More photons in a smaller area – increased intensity
  More radiographic density

## Slide 24: Density Maintenance Formula
Derived from the Inverse Square Law
  Reversed to make a “Square Law”
=

## Slide 25: Density Maintenance Formula
When do we use it?
  Portables (especially chests)
  To fit larger parts to a receptor
  Patient condition

## Slide 26: Density Maintenance Formula
The original exposure is with 20 mAs at a distance of 40 inches. The new exposure will be taken at a distance of 72 inches. What will the new mAs be?

## Slide 27: OID
Object to Image Distance
Increased OID allows less scatter to reach the IR
How would less scatter affect radiographic density?
  It would ________________ it
So then we can draw the conclusion,
  Increased OID, results in decreased radiographic density

## Slide 28: Patient Factors
Most difficult
Huge influence on radiographic technique
Requires __________ call, experience and training on the part of the technologist

## Slide 29: Body Habitus
Used to classify patients when discussing patient factors
Descriptors:
  Aesthenic
  Hyposthenic
  Sthenic
  Hypersthenic

## Slide 30: Thickness
Calipers
With increased thickness, how should exposure factors be adjusted?
Must increase factors
  Can change mAs or kVp
  In most situations, would choose to adjust mAs

## Slide 31: Composition
What does the area consist of?
  Bone?
  Fluid?
  Fat?
Additional judgment required
  Tissue thickness not linear because of many variables
  Atomic number and density of part
Chest vs. abdomen

## Slide 32: General Rule of Technical Factors
Chest
  High kVp
Soft tissue
  Low kVp, high mAs
Bony extremities
  Low kVp

## Slide 33: Pathology
Another patient factor to be considered
Radiographic technique needs to be adjusted in cases with known pathology
Destructive
  Increases _______________ of tissue
Constructive
  Increases _______________of tissue

## Slide 34: Filtration
Three types:
  Inherent
  Added
  Compensating

## Slide 35: Inherent Filtration
Glass or metal envelope
Collimator usually provides some additional filtration
Technologist has no control of this
Built into the unit
Designated amount by SC 35

## Slide 36: Added Filtration
Can be adjusted or selected
Aluminum is the material most commonly used
Technique charts are based on units using the lowest allowable added filtration
  Set by the SC 35
When filtration is added, the technique must be adjusted to compensate
  Usually increase filtration for areas with high subject contrast
  Can decrease dose

## Slide 37: Emission Spectrum - Filtration
When filtration is added, low energy photons are removed
If photons are removed, what happens to the emission spectrum?
  The amplitude will decrease (amplitude = quantity)
If the low energy photons are removed, what happens to the average energy of the photons?
  The average energy will increase
If the average energy is affected, what will the emission spectrum look like?
  The peak will move to the right

## Slide 38: Compensating Filters
Sole purpose is to balance the intensity of the x-ray beam to deliver a more uniform exposure to the IR
Can be aluminum and attached by collimator
Can be placed on the patient, to even out the density.

## Slide 39: Filtration
Why do we use it?
  Increased x-ray beam quality
  Increased penetrability
    Due to losing lower energy photons
What is the result on our image?
  More scatter
  Decreased image contrast
  Compensating – more uniform density

## Slide 40: More to keep in mind….
Grids
Collimation
Generators

## Slide 41: Grids
Device placed between patient and image receptor
Purpose
  Absorb scatter exiting the patient
Why do we use it?
  Improve image __________
  High ratio grid can absorb 80-90% of scatter

## Slide 42: Grids and Density
How will a grid affect radiographic density?
  It will decrease the amount of density on the image
So then…
  mAs must be adjusted when adding, removing or changing a grid.
  This is to maintain appropriate density.
  Grid conversion formula.
    Grid factors – we will discuss this in more detail later.

## Slide 43: Beam Restriction
Collimation
  Adjusted by the technologist
What does this affect?
  The amount of tissue being irradiated
  The amount of scatter reaching the image receptor
What does this mean for density?
  Less scatter reaching the image receptor results in decreased radiographic density

## Slide 44: Generators and Density
Exposure techniques that we use are developed based on the type of generator in the room.
Generator Factors
If the output is more efficient
  ________ technique settings
If the output is less efficient
  _________ technique settings

## Slide 45: Emission Spectrum - Voltage
If the generator output is more efficient, what happens to the quantity of x-ray photons?
  It ________________, there will be more x-ray photons
With increased generator output, what will happen to the average energy of the photons?
  It will also __________, the average energy will be higher
How will the emission spectrum be affected by increased efficiency of the generator output?
  The amplitude will ____________
    Increased quantity
  The peak will move to the ____________
    Increased average energy

## Slide 46: Readings
Bushong: Radiologic Science for Technologists, 11th ed.
  Pg 54-55 (Inverse Square Law)
  Pg 131 (Effect of added filtration)
  Pg 132 (Effect of voltage waveform)
  Pg 136-143 (don’t worry about HVL)
  Chapter 9
  Pg 187-195 (up until Grids)
  Pg 240-246