## Slide 1: APPH 226: Digital Imaging
Objectives: 6.1, 6.2, 6.5

## Slide 2: Digital Imaging
Defined as:
  Any imaging acquisition process that produces an electronic image that can be viewed and manipulated on a computer
  These digital images can be sent through a computer network to various locations as needed

## Slide 3: Computer
Used throughout the department for a number of purposes – front desk, technologist work area to the radiologists’ reading room
Computer setup chosen to fulfill purpose
  File room clerk vs radiologist
Basically consists of :
  Input devices
  Output devices
  Processing devices
    Done in the central processing unit

## Slide 4: Input and Output Devices
Input Devices
Keyboards
Mouse
Microphones
Barcode readers
Touch screens
Image scanners
Output Devices
Monitors
Printers
  Paper
  Laser film
Speakers

## Slide 5: Monitors
Two main types
  CRT
    Cathode Ray Tube
  LCD
    Liquid Crystal Display
Third type in development
  OLED
    Organic Light – Emitting Diode

## Slide 6: Monitors
CRT
  Refresh Rate
  How fast the monitor rewrites the screen or
  The number of times the image is redrawn on the display/second
  Controls the ‘flicker’ seen by user
  Higher refresh rate = less flicker
LCD
  Response Rate
    The amount of time for crystal to go from off state to on and vice versa
    Slower response time will cause blurring during viewing of dynamic images

## Slide 7: Aspect Ratio
Aspect Ratio is:
  Ratio of the width of the monitor to the height of the monitor
  CRT usually 4:3
  LCD usually 16:9

## Slide 8: CRT
Used in first generation of PCs, still used today
Consists of a cathode and anode in a vacuum tube
Works like an x-ray tube
  Electrons sent to the monitors anode which is a sheet of glass coated with phosphors
Electrons strike phosphors causing glass to emit a color determined by the intensity of the interaction and area with which electrons interacted

## Slide 9: CRT
Electron beam starts in the upper left corner and scans across the glass from side to side, top to bottom
After reaching the bottom, it starts again at the top left
On average, most monitors have 350 lines to be scanned
Typical refresh rates are 60-75 Hz, meaning that 350 lines are being scanned 60-75 times per second

## Slide 10: LCD
Light passes through the first layer, and when a current is applied to the crystal layer, it aligns and allows light in varying intensities through to the next layer
  Color filters in that layer of glass form the colors and images seen on the display
Images are produced by shining or reflecting light through a layer of liquid crystal and a series of color filters
Made of two pieces of polarized glass with a liquid crystal layer in between the two

## Slide 11: Examples of Workstations
Administration
Technologist X-ray room
PACS workstation
CR reader workstation
Radiologist workstation
Archives workstation

## Slide 12: Digital Imaging
A digital image is one that has been converted into numerical values for transmission or processing
Requires a means to acquire the image information (DR, CR)
Information gathered by scanning an area using array detection
Array processing is when information is received from an entire area at once

## Slide 13: Array Processors
Special computer that functions as a peripheral device
Uses its own memory to perform simultaneous mathematical operations at extremely high speeds
  Compiles all the image information
Allows us to see the image instantaneously

## Slide 14: Digital Imaging
Factors that remain unchanged….
  Patient positioning
  Projections
  Collimation

## Slide 15: Digital is better because…
Wider range of exposure
Linear response
Greater range of densities
Easily manipulated with computer
Post processing

## Slide 16: Characteristics of a Digital Image
Digital image begins as an analog signal
Critical characteristics of a digital image are:
  Spatial resolution
  Contrast resolution
  Noise
  Dose efficiency (of the IR)

## Slide 17: Pixel
Pixel aka picture element
Smallest element in a digital image
  Magnify a digital picture to the point that the image will appear as small squares of color – that is visualization of the pixels

## Slide 18: Pixel Size
Pixel size – size of the pixel is directly related to the amount of spatial resolution or detail in the image
The smaller the pixel, the greater the detail
Can be affected by matrix size

## Slide 19: Pixel Bit Depth
Each pixel contains bits of information
Is the # of bits within a pixel
E.g. bit depth = 8 means 28
  meaning 256 shades of gray can be produced by that pixel
Some digital systems have bit depths of 10 – 16 meaning each pixel can have a gray level between 0 and 65 536 (for a 16 bit system)
Higher the bit depth, the more gray levels can be displayed by the pixel
  More shades of gray gives more accurate representation of the image

## Slide 20: Bit Systems
  8 bit system is 28 = 256 shades of gray
    2x2x2x2x2x2x2x2 = 256
  10 bit system is 210= 1024 shades of gray
    2x2x2x2x2x2x2x2x2x2= 1,024
  12 bit system is 212 = 4096 shades of gray
    2x2x2x2x2x2x2x2x2x2x2x2= 4,096
  14 bit system is 214 =16,384 shades of gray
    2x2x2x2x2x2x2x2x2x2x2x2x2x2 = 16,384
Notes:   For an 8 bit system is 28 = 256 grays
  2x2x2x2x2x2x2x2 = 256
  10 bit system is 210= 256 grays 2x2x2x2x2x2x2x2 x2x2= 1024
  12 bit system is 212 = 4096 grays 2x2x2x2x2x2x2x2x2x2x2x2= 4096
  14 bit system is 214 =16,384 grays 2x2x2x2x2x2x2x2x2x2x2x2x2x2= 16,384

## Slide 21: Matrix
Image is recorded as a matrix
Described in numerical values – dimensions of pixel quantity
Divided into many small cubes/boxes…
  Each square region is a pixel
  Assigned one binary value that is equal to the radiation exposure received
    Binary value = shade of gray

## Slide 22: Pixels
Each pixel in the matrix displays a numerical value, as well as a density level (shade of gray), proportional to the degree of the incoming signal
1
150
256
50
50
200
50
256
1
256
200
100
1
50
1
200

## Slide 23: Matrix
Matrix size = resolution
  1024 x 1024 vs 2048 x 2048
Larger the matrix = smaller the pixels
  If the detector is the same size
    i.e 1024 x 1024 matrix on a 10x12 CR cassette vs 1024 x 1024 matrix on a 35 x 43 CR cassette
      Which CR will have smaller pixels?
Matrix size is not the same as screen size
**Pixel size controls resolution

## Slide 24: Size of Detector
Cost of detector can range from $70-100K
Can be used in static or portable units
  Corded or cordless
Pixel size varies with the size of the detector
  512 x 512 matrix on a 24 x 30 cm CR cassette will have smaller pixels than a 512 x 512 matrix on a 35 x 43 cm CR cassette

## Slide 25: Dynamic Range
The ability to respond to varying levels of exposure
  More densities can be visualized on the image
  Can accurately detect very high and very low intensities
    Dynamic range wider for digital vs film/screen
The range of gray values that can be displayed
  Controlled by the detector
Human eye can differentiate about 30 shades of gray

## Slide 26: Dynamic Range
Dynamic range of digital imaging systems is identified by the bit capacity of each pixel
Although the response of a digital system can produce a huge range of greys (e.g. 16 bit = 65 536 shades of grey), limited by the human visual system
  Can only see about 30 of them
So through the use of window and level, any region/range of greys can be rendered into the 30 shades of grey that the human eye can see

## Slide 27: Dynamic Range
WINDOW LEVEL
P I XELS D I SPLAYED
Density
Pixel Values (Raw data)
WINDOW
WI
DTH
Exam algorithm applied
The biggest difference between digital and film lies in the ability to manipulate the digitized pixel values by ‘windowing’, resulting in greater exposure latitude

## Slide 28: Gray Scale
Different sources will assign 1 as either dark or white. For our purposes, we will refer to Bushong, which designates white as 1
1
1
256
256
#
of
grays
#
of
grays

## Slide 29: Pixel Depth
8 bit
256
1
10 bit
1,024
1
14 bit
16,384
1
#
of
grays
#
of
grays
#
of
grays
Black
Black
Black
White
White
White

## Slide 30: Windowing
Allows us to see only a portion of the entire dynamic range
Raw data image will show the full dynamic range
  Appears very low contrast, as there are so many shades of grey being displayed

## Slide 31: Window Level
Density (Brightness) Enhancement
Window level controls image brightness
Brightness is controlled by varying the numerical value of each pixel
Direct relationship:
  window level = image brightness
Window Level (or center) sets the midpoint of the range of brightness visible in the image.

## Slide 32: Altering Image Brightness
Increasing the brightness of the image:
  All pixels are adjusted by the same factor
Decreasing the brightness of the image:
  All pixels are adjusted by the same factor

## Slide 33: Increasing Brightness
To brighten an image all pixels are raised to a higher value by the same factor
Ex: Increase the intensity of the brightness of each pixel by 100
To decrease the brightness of the image all pixels are decreased in value by the same factor
Ex: Decrease the intensity of the brightness of each pixel by 50

## Slide 34: Window Width
Contrast Enhancement
Controls image contrast
Sometimes called gray scale expansion or compression
Inverse relationship:
  Window Width = Image Contrast
  (because: WW = fewer shades of gray are used)

## Slide 35: Window Width
Varies the dynamic range (grayscale) of the densities to adjust the contrast
Narrow WW:
  the window width = in contrast
Wide WW:
  window width = in contrast
Controls the visibility of detail
Any value outside of the chosen window width is lost from diagnosis

## Slide 36: Windowing
Using window and level, any region and range of the available # of greys, can be rendered as 30 shades of gray

## Slide 37: Readings
Radiologic Science for Technologists 11th Ed
  Pg 267-281
  Pg 309 (Contrast Resolution)-312
  Pg 315 (Patient Radiation Dose Considerations) -319
  Pg 322-326
Digital Radiography and PACS 2nd Ed
  Chapter 2
  44-46