## Slide 1: MRAD 204: Radiographic Technique 1
Outcome 6-10:
Positioning – Ankle, Foot, Calcaneus & Toes

## Slide 2: Affiliated Readings
Module Reading
Bontrager
Pgs: 228→230
Pgs: 232→236
Pgs: 237→238
Pgs: 239→242

## Slide 3: Overview
Guidelines/Considerations
Protocol
Positioning

## Slide 4: Guidelines/Considerations – Ankle
Identify required anatomy
All ankle projections require visualization of 1/3rd of distal tib/fib
R
Lateral projection must also display the entire calcaneus, navicular and base of 5th metatarsal

## Slide 5: Guidelines/Considerations – Ankle
2. Select appropriate equipment/technical factors
100cm SID, measured manually
  Using cassettes or wireless digital IR
Ankle technique = 60→75 kVp
Prepare the control panel/console
  *your 1st projection
*Using the smallest field size possible

## Slide 6: Guidelines/Considerations – Ankle
Setup room before bringing the patient in
  Note: can be done at either end of table
Ensure the table IR is not directly under the IR
Tube and IR aligned using 100cm SID
Field size matches size of IR
Correct anatomical marker selected
SAIT Campus 2021

## Slide 7: Guidelines/Considerations – Ankle
3. Artifact Removal
Any clothing or objects from the knee down
Notes: when the patient is in the room:
Use external landmarks when positioning
  Correct patient position is determined by:
    Femoral epicondyles: for AP & Lateral projections
    Intermalleolar line: for Mortise projection
*i.e. shoes, socks, and any jewelry must be removed
  Marker NOT under soft-tissue anatomy shadow

## Slide 8: Protocol - Ankle
Routine:
AP
AP Mortise (15-200 medial oblique)
Lateral (Mediolateral)

## Slide 9: Positioning – AP Ankle
Knee must be positioned in true AP
  Femoral epicondyles parallel to IR
Dorsiflex foot 90o
  (if patient condition allows)
Place an anatomical marker (using Anderson Marker Rules), and make final adjustments
Bontrager pg. 239 Fig. 6.78 & SAIT Campus 2021
Note: ankle joint is not ½ between all the required anatomy
If positioned with the calcaneus over inferior edge of the IR; the light field will extend beyond the active surface
If ankle joint is centered over the IR; the light field will include the entire foot (i.e. phalanges and metatarsals)

## Slide 10: Positioning – AP Ankle
Bontrager pg. 239 Fig. 6.78
CR should be over ankle joint
“Top” of light field on pt. to include 1/3rd of distal tib/fib
Lengthwise crosshair centered ½ between malleoli
Foot dorsiflexed 900
Toes not superimposing ankle joint
Inferior light field will include entire foot, and may extend beyond the active surface of the IR
Lateral-medial collimation: @ least ½ inch beyond soft-tissue
Marker on lateral side, not under anatomy shadow

## Slide 11: Positioning – AP Mortise Ankle
Place malleoli parallel to IR
  15-20o medial rotation
Dorsiflex foot 90o
  (if patient condition allows)
Place an anatomical marker (using Anderson Marker Rules), and make final adjustments
Bontrager pg. 240 Fig. 6.81

## Slide 12: Positioning – AP Mortise Ankle
CR should be located over ankle joint
“Top” of light field on pt. to include 1/3rd of distal tib/fib
Lengthwise crosshair centered between malleoli
Marker on lateral side, not under anatomy shadow
Lateral-medial collimation: @ least ½ inch beyond soft-tissue
Inferior light field will include entire foot, and may extend beyond the active surface of the IR
Foot dorsiflexed 900
Toes not superimposing ankle joint

## Slide 13: Positioning – Lateral Ankle
Femoral epicondyles perpendicular to IR
Dorsiflex foot 90o
Entire lateral surface of foot in contact with IR
Place an anatomical marker (using Anderson Marker Rules), and make final adjustments

## Slide 14: Positioning – Lateral Ankle
Collimate anteriorly to include navicular & base of 5th metatarsal
Lengthwise crosshair to pass thru medial malleolus
“Top” of light field on pt. to include 1/3rd of distal tib/fib
“Bottom” of light field on IR @ least ½ inch beyond soft-tissue of calcaneus
CR should be located over ankle joint
Foot dorsiflexed 900
Collimate posteriorly to include @ least ½ inch beyond soft-tissue of calcaneus
Marker anterior, not under anatomy shadow
Lateral surface of foot “flat” against IR

## Slide 15: Guidelines/Considerations – Calcaneus
1, 2 & 3. Same as Ankle EXCEPT:
All calcaneus projections require visualization of entire calcaneus, base of 5th metatarsal & the talocalcaneal joint
R
Lateral projection must also display ~1 inch of distal tib/fib & all soft-tissues
Calcaneus technique = *60→75 kVp (*Axial = 65-75)

## Slide 16: Protocol – Calcaneus (aka. os calsis)
Routine:
Plantodorsal Axial
Lateral (Mediolateral)

## Slide 17: Positioning – Plantodorsal Axial Calcaneus
Direct CR to base of 3rd metatarsal (superior border of “heel pad”)
  Crosshair should be distal to lateral malleolus
Dorsiflex foot 90o
  (if patient condition allows)
Place an anatomical marker (using Anderson Marker Rules), and make final adjustments
Tube Angle & ankle flexion should always = 130o
400

## Slide 18: Positioning – Plantodorsal Axial Calcaneus
Bontrager pg. 237 Fig. 6.72
Tube Angle and ankle flexion should always = 130o
CR ~5th metatarsal base (aka. diverging crosswise crosshair should be inferior/distal to lateral malleolus)
Foot dorsiflexed 900
Lengthwise crosshair centered between malleoli
Collimate distally to include @ least ½ inch beyond soft-tissue shadow of calcaneus
Marker on lateral side, not under anatomy shadow
Lateral-medial collimation: @ least ½ inch beyond soft-tissue
Superior light field inferior to phalanges

## Slide 19: Positioning – Lateral Calcaneus
Same positioning as lateral ankle:
Dorsiflex foot 90o
  (if patient condition allows)
Lateral surface of foot in contact with IR
Place an anatomical marker (using Anderson Marker Rules), and make final adjustments
Center ~1 inch (2.5cm) distal to medial malleolus

## Slide 20: Positioning – Lateral Calcaneus
Collimate anteriorly to include navicular & base of 5th metatarsal
Lengthwise crosshair to pass thru medial malleolus
“Top” of light field on pt. to include 1 inch of distal tib/fib
“Bottom” of light field on IR @ least ½ inch beyond soft-tissue of calcaneus
CR ~1 inch distal to medial malleolus
Foot dorsiflexed 900
Collimate posteriorly to include @ least ½ inch beyond soft-tissue of calcaneus
Marker anterior, not under anatomy shadow
Lateral surface of foot “flat” against IR

## Slide 21: Guidelines/Considerations – Foot
1, 2 & 3. Same as Ankle EXCEPT:
Oblique & Lateral Foot projections should demonstrate entire foot, including entire calcaneus and soft-tissues
Foot technique = *55→70 kVp (*AP = 55-65 & Obl. & Lat. = 60-70)
Correct patient position is determined by:
  Plantar surface of foot: for AP (axial) projection
  Transverse arch: for Oblique projection
  Metatarsal heads: for Lateral projection
AP (axial) projection is only required to display all anatomy anterior to the talus
Lateral projection must also display ~1 inch of distal tib/fib

## Slide 22: Protocol - Foot
Routine:
AP (10o Axial – Dorsoplantar)
AP Oblique (with medial rotation)
Lateral (Mediolateral)
Non-Routine Views:
Weight-bearing AP (10o Axial)
Weight-bearing Lateral (Mediolateral)

## Slide 23: Positioning – AP (Axial) Foot
Entire plantar surface flat on IR
Ensure entire foot is parallel to long edge of IR
Knee and tib/fib should be aligned with foot
Place an anatomical marker (using Anderson Marker Rules), and make final adjustments

## Slide 24: Positioning – AP (Axial) Foot
Posterior light field on pt. to exclude ~½ inch of calcaneus
Lengthwise crosshair centered ~2nd and 3rd phalanx
Entire plantar surface flat on IR
Lateral-medial collimation: @ least ½ inch beyond soft-tissue
Marker on lateral side, not under anatomy shadow
100 Cephalad CR angle
Knee & ankle aligned with foot (i.e. parallel to long edge of IR)
Distal light field @ least ~½ inch beyond digits

## Slide 25: Positioning – AP Oblique Foot
Rotate foot medially until transverse arch is parallel to IR
  ~30-40o rotation
Ensure entire foot is parallel to long edge of IR
Knee and tib/fib should be aligned with foot
SAIT Campus 2021
Place an anatomical marker (using Anderson Marker Rules), and make final adjustments
Note: 3cm OID under lateral side of foot = adequate rotation for most people

## Slide 26: Positioning – AP Oblique Foot
Posterior light field on IR to @ least ~½ inch beyond calcaneus
Lengthwise crosshair centered ~2nd and 3rd phalanx
Marker on lateral side, not under anatomy shadow
Lateral-medial collimation: @ least ½ inch beyond soft-tissue *ensure shadow of talus is included medially
Foot parallel to long edge of IR
Distal light field @ least ~½ inch beyond digits

## Slide 27: Positioning – Lateral Foot
Dorsiflex foot 90o
Ensure plantar surface is perpendicular to IR
  i.e. Metatarsal heads perpendicular to IR
Place an anatomical marker (using Anderson Marker Rules), and make final adjustments
Flex patient’s knee and place lateral side of foot on IR

## Slide 28: Positioning – Lateral Foot
Collimate anteriorly to include @ least ½ inch beyond shadow of digits
“Top” of light field on pt. to include 1 inch of distal tib/fib
“Bottom” of light field on IR @ least ½ inch beyond soft-tissue of the foots plantar surface
Foot dorsiflexed 900
Collimate posteriorly to include @ least ½ inch beyond soft-tissue of calcaneus
Marker anterior, not under anatomy shadow
Metatarsal heads perpendicular to IR

## Slide 29: Positioning: AP (Axial) Weight-bearing Feet
Entire plantar surface of both feet flat on IR
  Weight evenly distributed
Ensure feet are parallel to long edge of IR
Angle CR 10o→15o posteriorly
Place anatomical markers (using Anderson Marker Rules), and make final adjustments
  i.e. Weight-bearing, and R & L markers required
Bontrager 9th Ed. pg. 235 Fig. 6.68
L
R
Wt. bearing
Bontrager pg. 235 Fig. 6.67

## Slide 30: Positioning – Lateral Weight-bearing Feet
Evaluates longitudinal arch when body weight is applied
Bontrager pg. 236 Fig. 6.69
L
R
Wt. bearing
Fig 6-55 and 6-56 Frank, E.D., Long, Bruce W., Smith Barbara J. 2012 Merrill’s atlas of Radiographic Positioning and Procedures (12 ed.) St. Louis. pg. 263
Requires weight bearing and anatomical markers

## Slide 31: Positioning – Toes
Bontrager pg. 228-230 Fig. 6.39, 6.42, 6.43, 6.44, 6.46, 6.47, 6.49 & 6.51
Oblique in direction which removes superimposition and minimizes OID
AP = axial projections