## Slide 1
MRAD 251: CT
Theory 1
Summarize the use of contrast media and intravenous injections in computed tomography (CT)

## Slide 2: Objectives
1. Compare the different types of contrast media available
2. Describe indications and of contrast media
contraindications for the use
7.5 Outline the factors that determine the route of the contrast media and equipment selection

## Slide 3: Introduction to Contrast Media
Contrast Media is used in CT, because:
Structures may be difficult to differentiate without the use of contrast media.
Objects with similar densities will resemble one another visually (on a radiograph)
Windowing cannot always improve visualization of tissues that possess nearly identical attenuation properties
  HU values of objects may be too similar (tissues must differ by at least 10HU to visualize distinctly)

## Slide 4: Introduction Continued
Considerations:
The use of contrast material in any given study is determined by evaluating a variety of factors:
Radiographic appearance, required for diagnosis
Protocol
  Equipment limitations
  Type of contrast agent
Patient
  Contraindications
  Condition
Administration Route
  Example: Barium is only safe for use with GI tract imaging

## Slide 5: Introduction Continued
Technologist Responsibilities:
Sites/departments can vary greatly in their use of contrast media (protocols are not universal).
The type and dose of contrast media recommended for use is subjective
  Supply is also a factor
Regardless of protocol differences, technologists should consistently perform:
Patient assessment
Preparation
Administration of contrast media
Precautions

## Slide 6: Introduction Continued
What is Contrast Media?
A material that temporarily enhances differences between anatomical structures.
The use of contrast media affects:
  Viewing – tissues will display with very different shades, increasing
their visibility
  Localization – can determine the precise location of structures within tissues
  Differentiation – tissues contained within a structure will have different
HU values
(example: kidneys: renal cortex enhances differently than the medulla)

## Slide 7: Objective 7.1
Types of contrast media
Main forms:
Liquid
Gas
Paste/Powder
Classifications:
  Dependant on attenuation value of the enhanced structure
    Negative - ↓attenuation
    Positive - ↑attenuation

## Slide 8: Classifications
Negative contrast appears darker than the surrounding structure
  Example: Air & Gases
Positive contrast appears lighter than the surrounding structure
  Example: Iodinated Solutions & some Barium Sulfate Solutions
Double contrast studies can use a combination of contrast agents to help distinguish between structures on a CT scan

## Slide 9: Types of Contrast Media used in CT
Air
*Carbon Dioxide
  Preferred over air
Water
  Barium Sulfate Solutions
    Formulated for CT usage
Iodinated water-soluble Solutions
  *Most commonly used contrast agent in CT imaging

## Slide 10: Objective 7.2
Air & Gases:
Are non-toxic
Provide unobstructed visualization of anatomical structures
Distends GI tract (colon & stomach) for improved pathology detection
•
Advantage of Carbon Dioxide:
Insufflation/distention
Absorption
Patient comfort

## Slide 11: Why Water is used in CT
Water:
Patients will not present with allergies
Cost effective
Easily accessible
Water’s low density will not impede 3D reformatting
Cons:
Poor bowel distention
Rapid transit time

## Slide 12: Why Barium Sulfate is Used in CT
Barium Sulfate Solutions:
Specially formulated radiopaque agents use a 1→3% concentration for CT usage
2 Forms can be used to improve anatomic visualization:
  Liquid –
for esophageal studies
Paste –
Can “cling” to bowel walls
Cons:
Can cause streaks
Needs to be diluted
“Allergies” can occur
Poor mucosal evaluation
Complications
  Example: impaction
Contraindications
  Suspected bowel perforation

## Slide 13: VoLumen
“Unique” CT Barium Sulfate solution:
Low HU
  Classification can vary (i.e. neutral or negative)
0.1% Barium Sulfate Concentration
Resembles water
Advantages over water:
Better bowel distention
Slower transit time
Improved bowel wall & mucosa visualization

## Slide 14: Why Iodinated Media is Used in CT
Iodinated water-soluble solutions:
Provide differential enhancement, increasing visualization of a variety of structures
There are many non-ionic forms that can be used
  Osmolality & Viscosity is variable
Not metabolized
Cons:
Differential enhancement
Allergic-like reactions
Poor mucosal coating
Diarrhea
Contraindications
  Example: Renal Failure

## Slide 15: Objective 7.5
Contrast materials can be introduced into the body in the following ways:
Rectal
  Via specialized catheters
Injection
  Intra-articular or Intrathecal
Oral
  By mouth or nasogastric tube
IV
  Veins & Arteries
Each method has benefits and drawbacks

## Slide 16: Rectal Administration
On some occasions, rectal contrast is required for CT scans.
Procedure:
  Contrast is administered through an enema tip that is attached to a specialized catheter
Purpose:
  Large bowel visualization
Types of contrast media used:
  Typically all contrast media except water will be administered rectally
Preferred contrast media: C02
  Barium sulfate/Iodinated only demonstrates recto-sigmoid

## Slide 17: Injection Administration
Useful for post-arthrogram & intrathecal imaging.
Procedure:
Contrast is administered of the CT Department, typically using fluoroscopic guidance
  Intraarticular – a needle is advanced directly into a joint space, and contrast is injected
  Intrathecal - a needle is advanced to the spinal canal (or subarachnoid space) and contrast is injected

## Slide 18: Injection Administration
Purpose:
  Intraarticular - simultaneous visualization of bone and soft-tissue
  Intrathecal –spinal cord assessment
Types of contrast media used:
  Intraarticular – Air, gas, and iodinated
  Intrathecal – Only specifically manufactured iodinated contrast media can be safely used
Preferred contrast media: Iodinated
  Contrast media that is safe for intrathecal administration is specially labelled as
“for myelography or intrathecal use”
  Barium and water can not be administered

## Slide 19: Oral Administration
Oral contrast media is commonly used for CT scans of the abdomen and pelvis.
Procedure:
  Contrast media is diluted with water and administered by mouth (PO) or nasogastric tube
Purpose:
  Investigates GI tract pathology
Types of contrast media used:
  Any type of contrast media
Preferred contrast media: Iodinated
  Barium sulfate & iodinated contrast media must be diluted with water prior to
administration

## Slide 20: Oral Contrast Media Considerations
Patient’s should be NPO (~2hrs) for these exams.
Diabetic patients should be monitored closely
Administration start times should be recorded on the patients requisition:
Patients drink the oral contrast in intervals over a period of time:
  Enables the contrast to fill the entire GI tract
Length of time patients are required to ingest contrast is department dependent:
  Scan acquisition could be desired immediately following administration
or 45→120 minutes afterwards

## Slide 21: Considerations Continued
For improved visualization of the pancreas:
Scan acquisition should occur immediately after oral administration of
(~1-2 cups) water
For most routine abdominal CT scans:
Scan acquisition should occur ~2hrs following the onset of oral
administration of an iodinated water-soluble contrast agent diluted in water
  Ex. Patients can be expected to drink ~1500ml of water mixed with ~22.5ml of Telebrix at intervals over a 2 hour period (i.e. 1 cup of the solution every 30 minutes)
Note: most abdominal studies typically require the use of two contrast agents (via IV & Oral administration)

## Slide 22: Considerations Continued
Most common Iodinated oral contrast agents:
Telebrix
Lactulose
Gastrografin
Normal responses can include the onset of diarrhea either immediately while ingesting the oral contrast or post-procedure
As a result of dilution, concentrations of oral contrast used may vary.
Note: Barium is preferred when only small amounts of contrast can be consumed.

## Slide 23: IV Administration
.
Procedure:
Contrast media is administered through an pre-existing IV access site, or an IV line that is established in the CT department
  Considerations:
    Aseptic techniques must be applied
    Angiocaths vs. butterfly needles
    Location of the venous access site
    Equipment compatibility

## Slide 24: IV Administration
Purpose:
IV contrast is used when imaging the arterial or venous circulation system as well as the solid organs of the chest abdomen or pelvis
Types of contrast media used:
Only Iodinated (LOCM or IOCM)
  Preferred contrast media: Iodinated
Optiray, Visipaque, or Omnipaque will most commonly be used for IV & Injection administration methods

## Slide 25: Usage & Administration Summary
Air & gases can be used for the following exams:
•
GI studies
Arthrograms
Myelograms
Air & gases can be administered:
Via injection
Orally
Rectally

## Slide 26: Usage & Administration Summary
Water can be used for the following exams:
Evaluation of the pancreas
GI studies
Gastric Neoplasms
Water is typically administered:
•

## Slide 27: Usage & Administration Summary
Barium Sulfate Solutions can be used for:
•
Barium Solutions are typically administered:
•
More common
Rectally

## Slide 28: Usage & Administration Summary
Iodinated contrast media can be used for:
GI studies
Arthrograms
Postmyelograms
Vascular & Arterial Studies
Solid organ contrast enhancement
Iodinated agents can be administered:
Orally
Rectally
Via injection
•

## Slide 29: Things to Take Away
Purpose of contrast media
Classifications
Types of contrast media used in CT
  How the different types can be used (aka. administration methods)
  What the different types are used for
  Why the different types are used