## Slide 1: MRAD 204: Radiographic Technique 1
Outcome 6-10:
Positioning – Femur & Knee

## Slide 2: Affiliated Readings
Module Reading
Bontrager
Pgs: 246→250
Pgs: 278→280

## Slide 3: Overview
Guidelines/Considerations
Protocol
Positioning

## Slide 4: Guidelines/Considerations - Femur
Identify required anatomy
Femur radiographs require the entire femur, entire hip & knee joint AND at least 1-inch of proximal tibia/fibula
SAIT Image Library
R
https://radiopaedia.org/cases/normal-femur-radiographs-1?lang=us

## Slide 5: Guidelines/Considerations - Femur
2. Select appropriate equipment/technical factors
*Must prove overlap using anatomical marker
110cm SID, measured electronically using détentes (i.e. blue lock must be engaged)
Femur technique = 75→85 kVp
On the console, select:
  “Table IR”
  *1st image should be over site of injury

## Slide 6: Guidelines/Considerations - Femur
Setup room before bringing the patient in
Tube and IR aligned @ 110cm SID
  lock: centers tube to IR laterally/medially
  Laser light: centers tube to IR superiorly/inferiorly
Correct anatomical marker selected
Patient drape/patient sheet ready for use
Ensure IR is covered completely prior to patient mount/dismount
For table imaging: All locks must be “on” except yellow & green
*lock engaged

## Slide 7: Guidelines/Considerations - Femur
3. Artifact Removal
Any clothing or objects between the waist to the ankles
  Marker placed under soft-tissue anatomy shadow
Notes: when the patient is in the room:
Use external landmarks when positioning
  Proximal AP Femur projections: must palpate Bilateral ASIS
  Proximal Lateral Femur projections: same positioning requirements as Hip projections EXCEPT cannot twist/tilt collimator
  Distal Femur projections: must palpate Femoral epicondyles

## Slide 8: Guidelines/Considerations
For Femur Projections:
Must prove overlap between two images taken for the same projection
Include remaining anatomy in second “smaller” image
Try to include site of injury in one image
If present, demonstrate entire ORIF in one image (if possible) ORIF is Open Reduction Internal Fixation
*Remember: Joint above & joint below must be included in all long bone x-rays
Should be the image that contains the most anatomy (i.e. the “largest” image)

## Slide 9: Femur Protocol
Routine:
AP – (2 images: 1 proximal & 1 distal)
Lateral – (2 images: 1 proximal & 1 distal)

## Slide 10: Positioning – AP Distal Femur
SAIT Campus 2021
Ensure the patient is lying straight on the table (hips, shoulders, & femur parallel to long edge of table)
Use patient draping
ASIS’s should be level
Knee must be positioned in true AP
Femoral epicondyles parallel to IR
Place an anatomical marker,
at the top lateral edge of the light field
(to prove overlap), and make final adjustments
Note: the longer field size should include site of injury, and the marker is used to prove overlap (as seen in the next slide)
Follow ALARA when proving overlap

## Slide 11: Positioning – AP Distal Femur
Note: Check for Diverging rays!
Light-fields on patient’s are smaller than they appear radiographically.
Femoral Epicondyles parallel to IR
“Bottom” of light field on the IR @ least 1-inch below knee joint
*Knee joint is ½ inch below apex of patella
Lengthwise crosshair ½ between femoral epicondyles
Marker over superior lateral corner – to prove overlap
Lateral-medial collimation: @ least ½ inch beyond femoral epicondyles
Femur parallel to longitudinal edge of IR

## Slide 12: Positioning – AP Proximal Femur
Ensure affected leg is parallel to long edge of table
ASIS’s should be level
Hip must be positioned in true AP
  Internally rotate leg 15-20o
Place an anatomical marker
at the bottom lateral edge of the light field
(to prove overlap), and make final adjustments
*AP proximal femur positioning is the same as AP hip positioning (as per Bontrager page 288)
Note: Collimation should start at (and include) location of marker from distal femur image (to prove overlap), and extend to include hip joint superiorly

## Slide 13: Positioning – AP Proximal Femur
Lengthwise crosshair around middle of knee
Marker in same location should now be over inferior lateral corner – to prove overlap
Lateral-medial collimation: should “clip” symphysis pubis
Femur parallel to longitudinal edge of IR
*AP proximal femur positioning is the same as AP hip positioning (as per Bontrager page 288)
“Top” of light-field on patient at ASIS

## Slide 14: Positioning – Lateral Distal Femur
http://www.radtechonduty.com/2012/11/lateral-view-femur.html
Collimator head can NOT be tilted
Ensure affected leg is parallel to long edge of table
Knee must be positioned in true lateral
Femoral epicondyles perpendicular to IR
Flex knee with patient on affected side
A lateral limb will display a “level” light field
Note: the longer field size should include site of injury, and the marker is used to prove overlap (as seen in the next slide)
Two different positions can be used to ensure the unaffected leg will not obscure the image
Follow ALARA when proving overlap
Bontrager pg. 279 Fig. 7.38

## Slide 15: Positioning – Lateral Distal Femur
Collimation: ½ inch anterior to patella & ½ inch posterior to the femoral condyle
Femur parallel to longitudinal edge of IR
Bontrager pg. 279 Fig. 7.38
Two positioning options
Collimator head can NOT be twisted
Lengthwise crosshair around medial femoral epicondyle
“Bottom” of light field on the IR @ least 1-inch below knee joint
Marker over superior anterior corner – to prove overlap
Femoral Epicondyles perpendicular to IR
Knee flexed (˂450)

## Slide 16: Positioning – Lateral Proximal Femur
Ensure femur on side of interest is parallel to long edge of table
Ensure unaffected leg does not obscure (superimpose region of interest/ROI)
Place an anatomical marker, at the bottom anterior edge of the light field (to prove overlap), and make final adjustments
Note: Collimation should start at (and include) location of marker from distal femur image (to prove overlap), and extend to include hip joint superiorly
L
Follow ALARA when proving overlap

## Slide 17: Positioning – Lateral Proximal Femur
Lengthwise crosshair around middle of knee
Marker in same location should now be over inferior anterior corner – to prove overlap
Anterior-posterior collimation: should be the same size as the distal image (i.e. width of the bony anatomy of the knee)
Femur parallel to longitudinal edge of IR
“Top” of light-field on patient around upside ASIS
Collimator head can NOT be twisted

## Slide 18: Guidelines/Considerations - Knee
Identify required anatomy
Knee radiographs require 1/4 of proximal tibia/fibula, the distal femur, and the entire patella

## Slide 19: Guidelines/Considerations - Knee
2. Select appropriate equipment/technical factors
*Using the smallest field size possible - collimation
110cm SID, measured electronically using détentes
*Knee technique = *65→80 kVp
On the console, select:
  “Table IR”
  the projection you will begin positioning
    *remember: AP & Lateral knee require a 50 cephalad tube angle
Table IR

## Slide 20: Guidelines/Considerations - Knee
3. Artifact Removal
Any clothing or objects between the mid-femur to the “mid-calf”
Notes: when the patient is in the room:
Use external landmarks when positioning
  Femoral epicondyles determine correct patient position for all knee projections
  Apex of patella is used to determine location of the knee joint
Ensure the marker is NOT placed under “anatomy shadow”
*can be easier to ask your patient to remove their pants and provide them with a gown & housecoat

## Slide 21: Knee Protocol
Routine:
AP or PA
AP or PA 45o internal oblique
AP or PA 45o external oblique
Lateral
Special Request:
AP weight-bearing

## Slide 22: Positioning – AP/PA Knee
Ensure femur is parallel to long edge of table
Rotate femoral epicondyles until parallel to IR
Place an anatomical marker, and make final adjustments
Bontrager pg. 246 Fig. 6.100
http://www.radtechonduty.com/2012/10/pa-projection-patella.html
Angle CR 5° cephalad
Angle CR 5° caudad
Collimator head can NOT be tilted
Remember: knee joint is ½ inch below apex of patella
R

## Slide 23: Positioning – AP Knee
Marker on lateral side NOT under anatomy shadow
Collimate “side-side” to include ½ inch beyond soft-tissue
Lengthwise crosshair around middle of knee
Angle CR 5° cephalad
Femur parallel to edge of light field
“Top” of light field must include @ least ½ inch proximal to the base of patella
CR should be located over knee joint
“Bottom” of light-field to include 1/4th of proximal tibia

## Slide 24: Positioning – AP/PA 45o internal oblique
Ensure femur is parallel to long edge of table
Rotate entire leg (and body) medially, until femoral epicondyles are 45o to IR
Place an anatomical marker, and make final adjustments
Collimator head can NOT be tilted
Remember: knee joint is ½ inch below apex of patella
https://ce4rt.com/positioning/radiographic-positioning-of-the-knee-pa-views/
PA
“Straight” ray
Bontrager pg. 247 Fig. 6.103

## Slide 25: Positioning – AP 45o internal oblique
Marker on lateral side NOT under anatomy shadow
Collimate “side-side” to include ½ inch beyond soft-tissue
Lengthwise crosshair around middle of knee
Femur parallel to edge of light field
“Top” of light field must include @ least ½ inch proximal to the base of patella
CR should be located over knee joint
“Bottom” of light-field to include 1/4th of proximal tibia
NO tube angle

## Slide 26: Positioning – AP/PA 45o external oblique
Ensure femur is parallel to long edge of table
Rotate entire leg (and body) laterally, until femoral epicondyles are 45o to IR
Place an anatomical marker, and make final adjustments
Bontrager pg. 248 Fig. 6.106
Collimator head can NOT be tilted
Remember: knee joint is ½ inch below apex of patella
https://ce4rt.com/positioning/radiographic-positioning-of-the-knee-patella-views/
PA
45o
medial
lateral
“Straight” ray

## Slide 27: Positioning – AP 45o external oblique
Marker on lateral side NOT under anatomy shadow
Collimate “side-side” to include ½ inch beyond soft-tissue
Lengthwise crosshair around middle of knee
Femur parallel to edge of light field
“Top” of light field must include @ least ½ inch proximal to the base of patella
CR should be located over knee joint
“Bottom” of light-field to include 1/4th of proximal tibia
NO tube angle

## Slide 28: Positioning – Lateral Knee
Ensure femur is parallel to long edge of table
Rotate femoral epicondyles until perpendicular to IR
Flex knee 20-30o
Place an anatomical marker, and make final adjustments
Bontrager pg. 249 Fig. 6.109
Angle CR 5° caudad
Note: lateromedial projection usually taken x-table “as-is” for trauma
Angle CR 5° cephalad
Collimator head can NOT be tilted
Remember: knee joint is ½ inch below apex of patella
90o
L

## Slide 29: Positioning – Lateral Knee
Marker on anterior side NOT under anatomy shadow
Collimate “side-side” to include ½ inch beyond soft-tissue
Lengthwise crosshair around middle of knee
Femur parallel to edge of light field
CR ~1-inch distal to medial epicondyle
Knee flexed 20-300
“Bottom” of light-field to include 1/4th of proximal tibia

## Slide 30: Special Request: AP Weight-bearing Knees
Bontrager pg. 250 Fig. 6.112-6.113
Taken for:
evaluation of medial & lateral deformities
osteoarthritis
Check for narrowing of joint space
Check for alignment of bones