## Slide 1: MRAD 204: Radiographic Technique 1
Outcome 1-5:
Image Critique – Wrist, Scaphoid, & Forearm

## Slide 2: Affiliated Readings
Bontrager
Pgs: 153→156
Pgs: 162-163
Emphasis on the “pink box” Evaluation Criteria in readings.

## Slide 3: Overview
Determining Diagnostic Quality - Review
Wrist – image critique
Scaphoid – image critique
Forearm – image critique
Review

## Slide 4: Determining Diagnostic Quality - Review
For MRAD 204, an image is considered diagnostic unless:
Anatomy is clipped
Positioning appears more similar to a different projection
    Example: radiograph labelled as a PA projection, but the radiographic anatomy appears more similar to an oblique projection
Radiograph was labelled as underexposed
*reference your “Image Critique” Handout

## Slide 5: Image Critique – PA Wrist
#1. Anatomy
Ideally, you should visualize:
  Proximal ½ of metacarpals
  All 8 carpals
  2 inches of distal forearm
  Soft-tissue
@ 55 kVp

## Slide 6: Image Critique – PA Wrist
#2. Position
Long axis of wrist aligned with long axis of the IR
A true PA projection is evidenced by:
Equal concavity on metacarpal shafts
Near-equal distances between the metacarpals
Minimal superimposition of the distal radioulnar joint

## Slide 7: Image Critique – PA Wrist
Optimal density and contrast:
  no motion (i.e. blur)
  soft tissue margins visible
  clear bony trabecular markings
#3. Exposure & Technique
kVp range of 55-65
  *Notes: Ideal for the patient = 55

## Slide 8: Image Critique – PA Wrist
Four sided collimation centered to midcarpal area
#4. CR & Collimation

## Slide 9: Image Critique – PA Wrist
No removable artifacts are visible
#5. Marker Placement &/or artifacts
Marker placement is on the lateral side, not obscuring anatomy of interest

## Slide 10: Image Critique – PA Oblique Wrist
#1. Anatomy
Ideally, you should visualize:
  Proximal ½ of metacarpals
  All 8 carpals
  2 inches of distal forearm
  Soft-tissue
@ 60 kVp

## Slide 11: Image Critique – PA Oblique Wrist
#2. Position
Long axis of wrist aligned with long axis of the IR
A true 450 Oblique of the wrist is evidenced by:
Ulnar head partially superimposed by distal radius
3rd→5th metacarpal bases mostly superimposed

## Slide 12: Image Critique – PA Oblique Wrist
Optimal density and contrast:
  no motion (i.e. blur)
  soft tissue margins visible
  clear bony trabecular markings
#3. Exposure & Technique
kVp range of 60-70
  *Notes: Ideal for the patient = 60

## Slide 13: Image Critique – PA Oblique Wrist
Four sided collimation centered to midcarpal area
#4. CR & Collimation

## Slide 14: Image Critique – PA Oblique Wrist
No removable artifacts are visible
#5. Marker Placement &/or artifacts
Marker placement is on the lateral side, not obscuring anatomy of interest

## Slide 15: Image Critique – Lateral Wrist
#1. Anatomy
Ideally, you should visualize:
  Proximal ½ of metacarpals
  All 8 carpals
  2 inches of distal forearm
  Soft-tissue
SAIT MRT Image Critique Handbook
@ 60 kVp

## Slide 16: Image Critique – Lateral Wrist
#2. Position
Long axis of wrist aligned with long axis of the IR
A true Lateral position is evidenced by:
Ulnar head completely superimposed by distal radius
Proximal ½ of the 2nd→5th metacarpals superimposed
Lunate has a cup or “half-moon” shape

## Slide 17: Image Critique – Lateral Wrist
Optimal density and contrast:
  no motion (i.e. blur)
  soft tissue margins visible
  clear bony trabecular markings
#3. Exposure & Technique
kVp range of 60-70
  *Notes: Ideal for the patient = 60

## Slide 18: Image Critique – Lateral Wrist
Four sided collimation centered to midcarpal area
#4. CR & Collimation
SAIT MRT Image Critique Handbook

## Slide 19: Image Critique – Lateral Wrist
No removable artifacts are visible
#5. Marker Placement &/or artifacts
Marker placement is on the anterior side, not obscuring anatomy of interest

## Slide 20: Image Critique – Scaphoid
#1. Anatomy
Ideally, both projections should include:
  Base of 1st→3rd metacarpals
  Small amount of distal radius
  Scaphoid without foreshortening
  All joint spaces surrounding the scaphoid
Both @ 55 kVp
150
L
L

## Slide 21: Image Critique – Scaphoid PA
#2. Position
1st metacarpal aligned with radius
A true PA position, with ulnar deviation is evidenced by:
If included: minimal superimposition of the distal radioulnar joint
Wrist parallel to IR
Radio-scaphoid joint superimposition
@ 55 kVp

## Slide 22: Image Critique – Scaphoid 150 PA Axial
#2. Position
1st metacarpal aligned with radius
A true 150 Axial projection, with ulnar deviation is evidenced by:
If included: minimal superimposition of the distal radioulnar joint
Wrist parallel to IR
Radio-scaphoid joint free of superimposition
@ 55 kVp
Elongated scaphoid

## Slide 23: Image Critique – Scaphoid
Optimal density and contrast:
  no motion (i.e. blur)
  soft tissue margins visible
  clear bony trabecular markings
#3. Exposure & Technique
kVp range of 55-65
@ 55 kVp
@ 55 kVp
150
L

## Slide 24: Image Critique – Scaphoid
Four sided collimation centered to scaphoid
#4. CR & Collimation

## Slide 25: Image Critique – Lateral Wrist
No removable artifacts are visible
#5. Marker Placement &/or artifacts
Marker placement is on the lateral side, not obscuring anatomy of interest

## Slide 26: Image Critique – Forearm
#1. Anatomy
Ideally, both projections should include:
Proximal row of carpals
½ inch proximal to humeral epicondyles
Entire radius & ulna
Elbow joint
Soft-tissue
Both @ 65 kVp
150
L
L

## Slide 27: Image Critique – AP Forearm
#2. Position
Slight superimposition of radial head, neck, & tuberosity, over the proximal ulna
A true AP position, is evidenced by:
Forearm parallel to length of IR
No distortion of humeral epicondyles
Partially open wrist & elbow joint spaces

## Slide 28: Image Critique – Lateral Forearm
#2. Position
A true lateral position, is evidenced by:
Forearm parallel to length of IR
Superimposition of the distal radius & ulna
Superimposition of the radial head and coronoid process
Superimposed humeral epicondyles
900 Elbow flexion
Radial tuberosity facing anteriorly

## Slide 29: Image Critique – Forearm
@ 65 kVp
Optimal density and contrast:
  no motion (i.e. blur)
  soft tissue margins visible
  clear bony trabecular markings
#3. Exposure & Technique
kVp range of 65-75
@ 65 kVp

## Slide 30: Image Critique – Forearm
Four sided collimation centered to mid-forearm
#4. CR & Collimation

## Slide 31: Image Critique – Forearm
No removable artifacts are visible
#5. Marker Placement &/or artifacts
Marker placement is not obscuring anatomy of interest
  Lateral side for AP projection
  Anterior for Lateral projection

## Slide 32: Review
AP/PA projections: should demonstrate the most symmetry
  Bones should appear the same size/shape
  Soft-tissue margins should be even
Oblique projections: usually demonstrate some superimposition or remove superimposition
  Small portions of bones may superimpose one another or the patient rotation will eliminate the superimposition
Lateral projections: usually demonstrate the most superimposition
  Bony edges should be superimposed, making displacements easier to identify

## Slide 33: Review
When evaluating Anatomy:
Radiographically, if it isn’t clearly visualized in it’s entirety, it is considered clipped
When evaluating Exposure & Technique:
Use your chart to determine if it was acceptable, underexposed, or overexposed
  Remember underexposures render an image undiagnostic
Motion causes image blur, which obscures bony details
When evaluating Marker placement & Artifacts:
Memorize Anderson's marker rules
  Note orientation as well as location
Identify if the artifact can or cannot be removed
  Note if it is over anatomy of interest

## Slide 34: Review
When evaluating CR and Collimation:
Determine if the collimation/field size used, is appropriate
  if centered properly would all the required anatomy be included, or would you still clip/include too much?
  Remember collimation may be acceptable when CR centering isn’t
When evaluating Positioning:
Recall the ideal radiographic appearance, to use as a comparison (i.e. if you know what the size/shape of “normal” anatomy should be, it is easier to identify when a positioning error has occurred, and how to correct it)
  Example: A PA Oblique hand appears to have superimposition of the 3rd→5th metacarpal bodies, which demonstrates more superimposition than expected. This suggests the patient was over-rotated in the lateral/external direction.