## Slide 1: MRAD 204: Radiographic Technique 1
Outcome 1-5:
Image Critique – Shoulder & Clavicle

## Slide 2: Affiliated Readings
Bontrager
Pgs: 183, 191→193, 196, 199 & 201
Pg: 204
Emphasis on the “pink box” Evaluation Criteria

## Slide 3: Overview
Image Critique – Clavicle
Image Critique – Shoulder
Tips & Tricks

## Slide 4: Protocol
Routine:
AP shoulder with external rotation
AP Oblique for glenoid cavity
PA Scapular Y (lateral)
Superoinferior axial

## Slide 5: Image Critique – Routine Clavicle Projections
Anatomy
Ideally, BOTH clavicle radiographs should display:
Entire Clavicle
AC joint
SC joint
Acromion
R
R
Bontrager 9th Ed. pg. 204 Fig. 5.87A & B

## Slide 6: Image Critique – Routine Clavicle Projections
BOTH routine clavicle radiographs should display:
kVp range of 70→85
Optimal density and contrast:
  no motion (i.e. blur)
  soft tissue margins visible
  clear bony trabecular markings
Exposure & Technique
R
R
Bontrager 9th Ed. pg. 204 Fig. 5.87A & B

## Slide 7: Image Critique – Routine Clavicle Projections
Marker Placement &/or artifacts
No removable artifacts are visible
Marker placement: lateral side; not obscuring anatomy of interest
Note: Axial projection requires an “up” arrow
R
Bontrager 9th Ed. pg. 204 Fig. 5.87A & B

## Slide 8: Image Critique – Routine Clavicle Projections
R
CR & Collimation
Four sided collimation centered to mid-clavicle
Bontrager 9th Ed. pg. 204 Fig. 5.87A & B
SAIT Campus 2021

## Slide 9: Image Critique – AP Clavicle
Clavicle demonstrated without foreshortening
Midclavicle superimposed on the superior scapular angle
Position
@ 70 kVp
Bontrager 9th Ed. pg. 204 Fig. 5.87A

## Slide 10: Image Critique – AP Clavicle
Only the medial portion of the clavicle is superimposed by the first and second ribs
*Note: Clavicle appears more “horizontal” in shape
Position
@ 70 kVp

## Slide 11: Image Critique – Routine Shoulder Projections
Optimal density and contrast:
  no motion (i.e. blur)
  soft tissue margins visible
  clear bony trabecular markings
ALL routine shoulder radiographs should display:
kVp range of 70→85
Exposure & Technique

## Slide 12: Image Critique – Routine Shoulder Projections
Marker Placement &/or artifacts
No removable artifacts are visible
Marker placement; not obscuring anatomy of interest
AP, Glenoid, & Scap Y
  Lateral side
Superoinferior Axial
  Anterior side “walking along the humerus”
R
R

## Slide 13: Image Critique – AP Shoulder (external rotation)
Entire Scapula
Anatomy
R
R
Entire clavicle
Proximal humerus
½ sternum (crosswise)

## Slide 14: Image Critique – AP Shoulder (external rotation)
CR & Collimation
Four sided cross-wise collimation; centered to ~mid clavicle (side-side) & ~2 inches inferior

## Slide 15: Image Critique – AP Shoulder (external rotation)
Position
@ 70 kVp
Greater tubercle in full profile laterally
Lesser tubercle superimposed over humeral head
Minimal superimposition of glenoid cavity and humeral head

## Slide 16: Image Critique – AP Oblique Shoulder (Glenoid)
Anatomy
R
R
Glenoid cavity in profile without superimposition of humeral head
Acromion
Coracoid process

## Slide 17: Image Critique – AP Oblique Shoulder (Glenoid)
CR & Collimation
Four sided collimation centered to ~mid scapulohumeral joint

## Slide 18: Image Critique – AP Oblique Shoulder (Glenoid)
Position
@ 70 kVp
Open scapulohumeral joint space
Superimposed anterior & posterior rims of glenoid cavity

## Slide 19: Image Critique –PA Oblique (Scap Y Lateral)
Anatomy
R
R
Entire scapula
Scapulohumeral joint
Proximal humerus

## Slide 20: Image Critique –PA Oblique (Scap Y Lateral)
CR & Collimation
Four sided collimation, parallel to medial border of scapula; centered to mid-scapula
Bontrager pg. 201 Fig. 5.75

## Slide 21: Image Critique –PA Oblique (Scap Y Lateral)
Position
@ 70 kVp
Scapula in true lateral with superimposed lateral & medial borders
No superimposition of scapular body & thorax (i.e. ribs)
Acromion & coracoid nearly symmetrical “upper limbs of the Y”
Humeral head superimposing the base of the “Y” (on ‘normal’ shoulders)

## Slide 22: Image Critique –PA Oblique (Scap Y Lateral)
Used to demonstrate dislocations
https://litfl.com/posterior-shoulder-dislocation/#jp-carousel-175094
Bontrager pg. 201 Fig. 5.77
Vs.
Anterior: humeral head beneath coracoid process
Posterior: humeral head beneath acromion
https://www.sportsinjuryclinic.net/sport-injuries/shoulder-pain/acute-shoulder-injuries/dislocated-shoulder

## Slide 23: Image Critique – Superoinferior (0-15o) Axial
Anatomy
R
R
Scapulohumeral joint
Coracoid process
Proximal humerus
Soft tissue
Acromion
Lateral end of clavicle

## Slide 24: Image Critique – Superoinferior (0-15o) Axial
CR & Collimation
Four sided collimation centered to scapulohumeral joint
Note: cannot center anatomy on IR

## Slide 25: Image Critique – Superoinferior (0-15o) Axial
Position
@ 70 kVp
Open scapulohumeral joint (not open on patients with limited flexibility)
Coracoid process in profile, projected anterior to the clavicle
Lesser tubercle in profile
AC joint superimposed by humeral head
Body of humerus parallel to IR (i.e. “straight”)

## Slide 26: Shoulder
The position of the clavicle is on the anterior aspect of anatomy.
Anatomical Relationship
https://sketchfab.com/3d-models/bony-elements-of-the-glenohumeral-joint-577fc05f069046d6a5759633587d5119
“birds eye view”
Anterior
Anterior
Posterior
Posterior
Medial
Lateral
Superior
Inferior
Clavicle
Clavicle

## Slide 27: Tips & Tricks – Identifying Rotation
It’s all about distance between the spine & clavicle
SAIT Imaging Library
More space = more rotation
For AP projections:
More space on Rt. Side
=
Rt. Sided rotation

## Slide 28: Rotation – Shoulder: You Try
Which way was the patient rotated?
McQuillen Martensen 5th Ed. Fig. 5-3
  To the Right
  To the Left (more space on the left side)
  RPO
  LAO