## Slide 1: MRAD 256 Radiographic Technique 2
Positioning of the Facial Bones

## Slide 2: Facial Bones Routine
Lateral
Caldwell
Water’s
Towne’s
SMV (submentovertical)

## Slide 3: Water’s (Parietoacanthial)
Extend neck to place the MML perpendicular to the IR
  Red line shows MML perpendicular to IR
  White line shows OML at 37° to IR
Adjust CR to exit at level of acanthion

## Slide 4: Water’s (Parietoacanthial)
Collimate to include orbits, maxillae and zygomas

## Slide 5: Collimation for Waters…
Bontrager 11- 126 and 189
Collimate to include orbits, maxillae, zygomatic bones

## Slide 6: Evaluation criteria…
  Orbits, maxillae and zygomatic bones are seen
  Orbits are foreshortened
  Petrous ridges are projected immediately below the maxillary sinuses
  No rotation or tilt
R

## Slide 7: Reverse Waters (Acanthioparietal)
Supine position (AP projection)
TEA and corner of mouth form a line perpendicular to IR
Central ray enters near the acanthion

## Slide 8: Modified Waters Method
Sometimes called a “Shallow” Water’s:
LML is perpendicular to the IR
Demonstrates orbital floors perpendicular to the IR.
Taken for “blow-out” # of orbital floor,
Bontrager 9th ed. 11-135 and 11-136

## Slide 9: Evaluation criteria
Petrous ridges in lower half of maxillary sinuses
Demonstrates inferior displacement of the orbital floor and/or fluid in the maxillary sinus
Orbits are less foreshortened than in a routine waters.
Bontrager 11-136

## Slide 10: Compare the two

## Slide 11: Caldwell for facial bones
Bontrager 11-132
Place the OML perpendicular to the IR
Angle 15 degrees caudad to exit the nasion
Collimate to include the inferior margin of the maxilla, the lateral tables of the skull, and the entire perimeter of the cranial vault.

## Slide 12
Caldwell for facial bones
Collimation for skull…
R
Bontrager 9th ed. Fig. 11. 115
Collimation for facial bones…
Same position, different collimation

## Slide 13: Evaluation criteria
All anatomy superior to the maxillae is visualized: orbits, nasal septum, zygomatic bones, nasal bones, and the entire perimeter of the skull
No rotation or tilt
Bontrager 11-115
R
R

## Slide 14: Lateral- R or L position
Affected side against IR
CR centered on zygoma (halfway between the outer canthus and the EAM)
Collimate to include mandible, and all facial bones anterior to EAM
Bontrager 9th ed.
11-125, 11-126

## Slide 15: Evaluation criteria…
  Mandible and all facial bones anterior to the EAM are seen
  No rotation or tilt: superimposed orbital roofs, EAMS, greater wings and lesser wings of sphenoid, TMJ’s
Bontrager 9th ed. 11-127

## Slide 16: Comparison of collimation for lateral facial bones versus skull…
Bontrager 9th ed. Fig 11-27
Bontrager 7th ed. Fig 12-52

## Slide 17: Submentovertical Projection (Zygomatic Arches)
Bontrager 9th ed. 11-143, and 11-144

## Slide 18: Submentovertical Projection (Zygomatic Arches)
CR ┴ to the IOML
IOML parallel to IR if possible
Center on midsagittal plane, at the level of the gonions
60 º
18 X 24 cm cassette
60 º
Fig 21-23 Frank, Eugene D., Long, Bruce W., Smith, Barbara J., (2012). Merrills Atlas of Radiographic Positioning and Procedures Volume 2 (12th ed.). St. Louis, MO: Elsevier Mosby. pg. 338

## Slide 19: Evaluation criteria
  Symmetric zygomatic arches free of superimposition.
  No rotation or tilt.
Bontrager 9th ed. 11-144

## Slide 20: Zygomatic Arches (tangential projection)
Rotate head 15° toward the affected side
Tilt chin 15° toward affected side
Bontrager 11-146

## Slide 21: Evaluation criteria
  Zygomatic arch free of superimposition from mandible or parietal bone
Bontrager 11- 147

## Slide 22: 30˚ modified Towne projection (for mandibular rami/zygomatic arches – pg. 427)
R
Bontrager 9th ed. 11-149
R

## Slide 23: Evaluation criteria
Bilateral zygomatic arches, free of superimposition
Mandibular rami demonstrated