## Slide 1: APPH 226: Apparatus and Image Management
Introduction to Equipment Objectives: 1.2, 2.2

## Slide 2: Types of X-Ray Units
Diagnostic X-Ray imaging system
  Tube currents: 100-1200 mA
  Exposure times: very short, measured in ms
  Tube voltages: 25 – 150 kVp
Therapeutic X-Ray Unit
  Tube current: Below 20 mA
  Exposure times: 1-60 minutes
  Tube voltages: 4-40 meV (million electron volts)

## Slide 3: Principle Components
Operating Console
X-Ray Tube
High Voltage Generator

## Slide 4: Operating Console
Allows operator to select the exposure factors
Control the x-ray beam
  Tube current (mA), voltage (kVp), exposure time (ms)
  X-ray beam quality and quantity
Image receptor selection
Meters display actual exposure taken
Exposure switch is considered to be part of the console

## Slide 5: Control Panel – Example

## Slide 6: Control Panel – Example

## Slide 7: Operating Console
Operating Console includes:
  On/off switch
  Exposure switch
  Settings for kVp and mA
  Exposure time
  Focal Spot size selector
  AEC (automatic exposure control)
  APR (anatomically programmed radiography)
  Back up timer

## Slide 8: Control Panel – Example
mAs Readout
kVp Readout
APR Button
Focal Spot Selector
AEC Button
On/Off
Exposure /Rotor
Button

## Slide 9: Control Panel – Example
kVp
mAs
Focal Spot Selector
AEC Button

## Slide 10: X-ray Tube Assembly
Main functions on the tube assembly
  Digital Distance Measure
  Angulation Measure
  Locks (Longitudinal, transverse détentes)
  Light field
  Collimator Scale
  Collimator Adjustment Knob
  Manual measuring tape

## Slide 11: Tube and Tube Support
Detector Selection
Light Field/Laser
All Locks Release
Collimation Controls
Light Field Only
Locks

## Slide 12: Tube and Tube Support
Measuring Tape
SID Readout
Angulation Scale
System Button

## Slide 13: Table – Example
Notes: Center pedestal

## Slide 14: Table – Example
Notes: Off center pedestal

## Slide 15: Table – Example
Table Release
Table Up/Down
Detector Lock

## Slide 16: Table – Example
Floating Table Release
Table Up/Down

## Slide 17: Detectors
Images can be attained using cassettes or detectors
Detectors can also be called “cassette-less” systems

## Slide 18: Dual Detector Room

## Slide 19: Upright Single Detector - Example

## Slide 20: Detector Controls
Tracking
Light Field
Collimators
AEC Indicator
Moves detector position
Secondary function
All locks release

## Slide 21: High Voltage Generator

## Slide 22: Tube Supports
Tube supports are part of the external structure of the x-ray tube
  Physical support of the assembly
  Made up of rails, column, tube head, housing and tube
Other external structures include the protective housing & glass or metal envelope

## Slide 23: Tube Supports
Purpose: to support the x-ray tube and housing assembly for manipulation and immobilization as required
Types of Tube Suspension systems
  Ceiling mounted
  Floor-to-Ceiling mounted
  Floor mounted
  C-arm

## Slide 24: Ceiling Tube Mount
Likely the most common installation
Most versatility
Two perpendicular sets of rails
Telescoping column
  Angulation
  Rotation
Limited only by the range of the rails

## Slide 25: Floor to Ceiling Support system
Single column attached to two rails
  Ceiling rail and floor rail
Limited movement of the x-ray tube
  Travel along rails
  Tube attached to a telescoping arm to allow transverse movement and angulation
  Adjustable column allows for vertical movement
Less versatile than the ceiling mount

## Slide 26: Floor Mounted System
Attached to floor and table pedestal
Column allows vertical movement
Telescoping arm allows for transverse movement and angulation
  Rotation capabilities common
Movement is most restricted with this system

## Slide 27: C-arm
Can be ceiling mounted or standalone (mobile)
Commonly used:
  OR (operating rooms)
  Trauma Bay
  Interventional/Angiography suites
  Fluoroscopy suites
X-ray tube on one side, IR on the other
Some have capabilities for dynamic (fluoroscopic) imaging
S.A.I.T. Medical Radiology Program 2011

## Slide 28: C-arm
Efficient
Design allows for obtaining images without having to move the patient
  Critical for trauma and OR scenarios
  Trauma imaging often requires images at 90 degrees to each other (AP and lateral)

## Slide 29: Table Characteristics
Shape
  Flat – most common for general radiography
  Curved – angiography, CT
Uniform radiolucency
Durable
  Must stand up to wear/tear
  Able to support patient’s weight
Carbon fiber is most common
  Strong
  Minimal absorption of radiation

## Slide 30: Table Characteristics
Easy to clean
  Removal of body fluids and debris
Hard to scratch
No crevices
High weight limit
Can include a detector, or cassette holder (bucky)
  Bucky-Potter tray
  Has oscillating grid and holds cassettes
  Grid is activated and moves automatically during the exposure

## Slide 31: Fixed vs. Tilting
Majority of tables are floating table tops, some are motor driven
Tilting
  Move 90º to upright(standing) and 15-30º head down
  Fixed height
Fixed
  Can be adjustable in height for patients and technologists

## Slide 32: Readings
Radiologic Science For Technologists, Mosby 11th Ed.
  Pg. 85-87,105