## Slide 1: MRAD 204: Radiographic Technique 1
Outcome 1-5:
Image Critique – Hand & Thumb

## Slide 2: Affiliated Readings
Bontrager
Pgs: 143→145
Pgs: 148-150
Emphasis on the “pink box” Evaluation Criteria

## Slide 3: Overview
Evaluation Criteria
Image Critique – Hand
Image Critique – Thumb

## Slide 4: Evaluation Criteria
Aka. How to Evaluate/Critique any Radiograph
Anatomy
Positioning
Exposure & Technique
CR & Collimation
Marker placement & artifacts
*reference your “Image Critique” Handout

## Slide 5: Image Critique – PA Hand
Entire hand and wrist included radiographically
SAIT Image Critique Handbook
1” (2.5cm) of distal forearm
#1. Anatomy
You can visualize:
  All 8 carpals
  All 5 metacarpals
  All 14 phalanges
@ 55 kVp

## Slide 6: Image Critique – PA Hand
If a properly positioned PA Hand was exposed, how should it appear radiographically?
#2. Position
SAIT Campus 2021
SAIT Image Critique Handbook
@ 55 kVp

## Slide 7: Image Critique – PA Hand
MCP and IP joints appear open – indicates correct CR location and complete “pronation” (hand is flat on the IR)
#2. Position
SAIT Image Critique Handbook
@ 55 kVp

## Slide 8: Image Critique – PA Hand
Oblique view of the thumb
#2. Position
Bontrager 9th Ed. pg. 150 Fig. 4.68
Long axis of the wrist is aligned with the long axis of the IR
@ 55 kVp

## Slide 9: Image Critique – PA Hand
No rotation: equal concavity on both sides of metacarpal shafts 2→5, and equal soft tissue around phalanges
#2. Position
SAIT Image Critique Handbook
No soft tissue overlap
@ 55 kVp

## Slide 10: Image Critique – PA Hand
SAIT Image Critique Handbook
Optimal density and contrast:
  no motion (i.e. blur)
  soft tissue margins visible
  clear bony trabecular markings
#3. Exposure & Technique
kVp range of 55-65
  *Note: Ideal = 55
@ 55 kVp

## Slide 11: Image Critique – PA Hand
SAIT Image Critique Handbook
Four sided collimation centered to 3rd MCP joint
#4. CR & Collimation
@ 55 kVp

## Slide 12: Image Critique – PA Hand
SAIT Image Critique Handbook
No removable artifacts are visible
#5. Marker Placement &/or artifacts
Marker placement is on the lateral side, not obscuring anatomy of interest
@ 55 kVp

## Slide 13: Image Critique – PA Hand; You try…
@ 60 kVp
Is this a diagnostic radiograph?
1. Anatomy:
2. Positioning:
3. Exposure & Technique:
4. CR & Collimation:
5. Marker place./artifacts:
Bontrager 9th Ed. pg. 150 Fig. 4.68

## Slide 14: Image Critique – PA Hand; You try…
@ 60 kVp
Is this a diagnostic radiograph?
1. Anatomy:
2. Positioning:
3. Exposure & Technique:
4. CR & Collimation:
5. Marker place./artifacts:
https://medpix.nlm.nih.gov/search?allen=true&allt=true&alli=true&query=hand

## Slide 15: Image Critique – PA Oblique Hand
Entire hand and wrist included radiographically
1” (2.5cm) of distal forearm
#1. Anatomy
You can visualize:
  All 8 carpals
  All 5 metacarpals
  All 14 phalanges
@ 55 kVp
Bontrager pg. 149 Fig. 4.72
R

## Slide 16: Image Critique – PA Oblique Hand
How would you achieve this radiograph of the digits and metacarpals?
Position the fingers perpendicular to the IR
Position the fingers parallel to the IR
Have the patient make a fist
Have the patient come back when you are finished this unit
@ 55 kVp
Bontrager pg. 149 Fig. 4.72
R
#2. Position

## Slide 17: Image Critique – PA Oblique Hand
@ 55 kVp
Bontrager pg. 149 Fig. 4.72
R
#2. Position
Are the bodies of the metacarpals “free of overlap”?
Do the heads of the 3rd, 4th, & 5th metacarpals overlap slightly?
Is there separation of the 2nd & 3rd metacarpal heads?

## Slide 18: Image Critique – PA Oblique Hand
@ 55 kVp
Bontrager pg. 149 Fig. 4.72
R
#3. Exposure & Technique
Was the kVp within the acceptable range?
Is there optimal density and contrast?
  Is there motion?
  Are soft tissue margins visible?
  Are there clear bony trabecular markings?

## Slide 19: Image Critique – PA Oblique Hand
@ 55 kVp
Bontrager pg. 149 Fig. 4.72
R
Is there four sided collimation centered around the 3rd MCP joint?
#4. CR & Collimation

## Slide 20: Image Critique – PA Oblique Hand
Are there any removable artifacts visible?
@ 55 kVp
Bontrager pg. 149 Fig. 4.72
R
Does the marker comply with Anderson marker rules?
#5. Marker Placement &/or artifacts

## Slide 21: Image Critique – PA Oblique Hand; You try…
@ 60 kVp
Is this a diagnostic radiograph?
1. Anatomy:
2. Positioning:
3. Exposure & Technique:
4. CR & Collimation:
5. Marker place./artifacts:
Bontrager pg. 151 Fig. 4.72
@ 65 kVp

## Slide 22: Image Critique – PA Oblique Hand; You try…
© 2021, Southern Alberta Institute of Technology
@ 60 kVp
Is this a diagnostic radiograph?
1. Anatomy:
2. Positioning:
3. Exposure & Technique:
4. CR & Collimation:
5. Marker place./artifacts:
@ 50 kVp

## Slide 23: Image Critique – Fan Lateral Hand
Entire hand and wrist included radiographically
1” (2.5cm) of distal forearm
#1. Anatomy
You can visualize:
  All 8 carpals
  All 5 metacarpals
  All 14 phalanges
SAIT Imaging Library
@ 60 kVp

## Slide 24: Image Critique – Fan Lateral Hand
IP joints appear open – indicates digits were parallel to the IR
SAIT Imaging Library
@ 60 kVp
#2. Position
Long axis of the wrist is aligned with the long axis of the IR
Slight oblique view of the thumb
Digits separated equally (with minimal soft tissue superimposition)
True lateral evidenced by: superimposed metacarpals & distal radius and ulna

## Slide 25: Image Critique – Fan Lateral Hand
SAIT Imaging Library
@ 60 kVp
#3. Exposure & Technique
Was the kVp within the acceptable range?
Is there optimal density and contrast?
  Is there motion?
  Are soft tissue margins visible?
  Are there clear bony trabecular markings?

## Slide 26: Image Critique – Fan Lateral Hand
SAIT Imaging Library
@ 60 kVp
#4. CR & Collimation
Is there four sided collimation centered around the 3rd MCP joint?

## Slide 27: Image Critique – Fan Lateral Hand
Are there any removable artifacts visible?
SAIT Imaging Library
@ 60 kVp
#5. Marker Placement &/or artifacts
Does the marker comply with Anderson marker rules?

## Slide 28: Image Critique – Fan Lateral Hand; You try…
@ 60 kVp
Is this a diagnostic radiograph?
1. Anatomy:
2. Positioning:
3. Exposure & Technique:
4. CR & Collimation:
5. Marker place./artifacts:
@ 50 kVp
Bontrager pg. 150 Fig 4.76
@ 70 kVp

## Slide 29: Image Critique – AP Thumb
Entire thumb included radiographically
#1. Anatomy
You can visualize:
  Both phalanges
  Entire 1st metacarpal
@ 55 kVp
Entire Trapezium visualized
  *includes joint spaces around the trapezium
@ 55 kVp

## Slide 30: Image Critique – AP Thumb
Entire thumb appears parallel to long axis of IR
@ 55 kVp
#2. Position
No rotation evidenced by: equal concavity & amounts of soft tissue along sides of phalanges
Open IP & MCP joint – indicating thumb was fully extended & correct CR location used

## Slide 31: Image Critique – AP Thumb
@ 55 kVp
#3. Exposure & Technique
Was the kVp within the acceptable range?
Is there optimal density and contrast?
  Is there motion?
  Are soft tissue margins visible?
  Are there clear bony trabecular markings?

## Slide 32: Image Critique – AP Thumb
Are there any removable artifacts visible?
@ 55 kVp
#4. CR & Collimation
#5. Marker Placement &/or artifacts
Is there four sided collimation centered around the 1st MCP joint?
Does the marker comply with Anderson marker rules?

## Slide 33: Image Critique – PA Oblique Thumb
Entire thumb included radiographically
#1. Anatomy
You can visualize:
  Both phalanges
  Entire 1st metacarpal
Entire Trapezium visualized
  *includes joint spaces around the trapezium
@ 55 kVp
@ 55 kVp
@ 55 kVp

## Slide 34: Image Critique – PA Oblique Thumb
Entire thumb appears parallel to long axis of IR
@ 55 kVp
@ 55 kVp
@ 55 kVp
#2. Position
Proper obliquity evidenced by: uneven concavity of metacarpal and phalangeal bodies (lateral edge will appear “straighter”)
Open IP & MCP joint – indicating thumb was fully extended & correct CR location used

## Slide 35: Image Critique – PA Oblique Thumb
@ 55 kVp
@ 55 kVp
@ 55 kVp
Was the kVp within the acceptable range?
Is there optimal density and contrast?
  Is there motion?
  Are soft tissue margins visible?
  Are there clear bony trabecular markings?
#3. Exposure & Technique

## Slide 36: Image Critique – PA Oblique Thumb
Are there any removable artifacts visible?
@ 55 kVp
@ 55 kVp
@ 55 kVp
#4. CR & Collimation
#5. Marker Placement &/or artifacts
Is there four sided collimation centered around the 1st MCP joint?
Does the marker comply with Anderson marker rules?

## Slide 37: Image Critique – Lateral Thumb
Entire thumb included radiographically
#1. Anatomy
You can visualize:
  Both phalanges
  Entire 1st metacarpal
Entire Trapezium visualized
  *includes joint spaces around the trapezium
SAIT Image Critique Handbook
@ 55 kVp

## Slide 38: Image Critique – Lateral Thumb
Entire thumb appears parallel to long axis of IR
#2. Position
SAIT Image Critique Handbook
@ 55 kVp
True lateral evidenced by: concave anterior surface & straight posterior surface of the metacarpal proximal phalanx bodies, with rounded heads
Open IP & MCP joint – indicating thumb was fully extended & correct CR location used

## Slide 39: Image Critique – Lateral Thumb
#3. Exposure & Technique
Was the kVp within the acceptable range?
Is there optimal density and contrast?
  Is there motion?
  Are soft tissue margins visible?
  Are there clear bony trabecular markings?
SAIT Image Critique Handbook
@ 55 kVp

## Slide 40: Image Critique – Lateral Thumb
Are there any removable artifacts visible?
Does the marker comply with Anderson marker rules?
Is there four sided collimation centered around the 1st MCP joint?
#5. Marker Placement &/or artifacts
#4. CR & Collimation
SAIT Image Critique Handbook
@ 55 kVp

## Slide 41: Which Projection is Which?
Bontrager pg. 145-147 Fig. 4.53, 4.56 & 4.59

## Slide 42: Which Projection is Which?
Notes: Now try this one