## Slide 1: MRAD 204: Radiographic Technique 1
Outcome 6-10:
Image Critique – Patella, IC Fossa, and Tib/fib

## Slide 2: Affiliated Readings
Bontrager Reading
Pgs: 244→245
Pgs: 253→255
Pgs: 256→261
Emphasis on the “pink box” Evaluation Criteria

## Slide 3: Overview
Image Critique – Patella
Image Critique – IC Fossa
Image Critique – Tibia & Fibula

## Slide 4: Image Critique – Patella
Anatomy
Ideally, “skyline” patella radiographs should display:
Entire patella
Femoral condyles
Intercondylar sulcus
R
R
Patellofemoral joint space

## Slide 5: Image Critique – Patella
Tangential patella radiographs should display:
kVp range of 70→80
Optimal density and contrast:
  no motion (i.e. blur)
  soft tissue margins visible
  clear bony trabecular markings
Exposure & Technique
R
R

## Slide 6: Image Critique – Patella
Marker Placement &/or artifacts
Marker placement: in the superior lateral corner of the light field, not obscuring soft-tissue anatomy
R
No removable artifacts are visible
Note: A radiograph may demonstrate a surgical implant (i.e. internal fixation device)

## Slide 7: Image Critique – Patella
CR & Collimation
Four sided collimation with lengthwise crosshair centered over the patellofemoral joint space
Bontrager pg. 260 Fig. 6.137
Note: crosshair will appear distorted in the 90/20 Settegast & Hughston Methods

## Slide 8: Image Critique – Patella
Position
@ 70 kVp
Patella and intercondylar sulcus in profile
Open patellofemoral joint space
Note: a “true” Seated Settegast (with 900 flexion) will demonstrate femoral condyles at the same height
Note: a 450 flexion will demonstrate the lateral femoral condyle superior to the medial
McQuillen Martensen 5th Ed. pg. 409 Fig. 6.242

## Slide 9: Image Critique – IC Fossa
Anatomy
Ideally, IC Fossa radiographs should display:
IC Fossa
Femoral epicondyles
R
L
McQuillen Martensen 5th Ed. pg. 391 Fig. 6.200
Femorotibial joint space
Fibular head
Articular facets
Apex of patella

## Slide 10: Image Critique – IC Fossa
Tangential patella radiographs should display:
kVp range of 70→80
Optimal density and contrast:
  no motion (i.e. blur)
  soft tissue margins visible
  clear bony trabecular markings
Exposure & Technique
R
R

## Slide 11: Image Critique – IC Fossa
Marker Placement &/or artifacts
Marker placement: on the lateral side, not obscuring bony anatomy
R
No removable artifacts are visible

## Slide 12: Image Critique – IC Fossa
CR & Collimation
Four sided collimation with lengthwise crosshair centered over the femorotibial joint space
Note: degree of flexion will cause the crosshair to appear distorted in both methods

## Slide 13: Image Critique – IC Fossa
Position
@ 70 kVp
~½ of fibular head superimposed by tibia
Intercondylar eminence in center of IC fossa
IC fossa in profile
  No superimposition of patella
Open tibiofemoral joint space

## Slide 14: Image Critique – Tib/Fib
Anatomy
Ideally, all routine Tibia & Fibula radiographs should display:
Knee & Ankle joint
R
Entire Tibia & Fibula
Femoral condyles
All soft-tissue of lower leg

## Slide 15: Image Critique – Tib/Fib
ALL routine hip radiographs should display:
kVp range of 70→80
Optimal density and contrast:
  no motion (i.e. blur)
  soft tissue margins visible
  clear bony trabecular markings
Exposure & Technique

## Slide 16: Image Critique – Tib/Fib
Marker Placement &/or artifacts
No removable artifacts are visible
Marker placement, not obscuring soft-tissue:
AP projection: lateral edge of light-field
Lateral projection: anterior edge of light field

## Slide 17: Image Critique – Tib/Fib
CR & Collimation
Four sided collimation centered to mid-knee joint

## Slide 18: Image Critique – AP Tib/Fib
Femoral and tibial condyles in profile
Intercondylar eminence centered within intercondylar fossa
Head of fibula partly superimposed by tibia
Distal tibia and talus partially superimposing fibula
Position
@ 70 kVp
R

## Slide 19: Image Critique – Lateral Tib/Fib
Tibial tuberosity in profile
Head of fibula partly superimposed by tibia
Distal fibula superimposed by the posterior ½ of tibia
Posterior borders of femoral condyles superimposed
Position
@ 70 kVp
R