## Slide 1: MRAD 251: CT Theory 1
Outcome 5 (Part 1):
Summarize radiation safety in computed tomography
(CT)

## Slide 2: Objectives
Describe basic CT radiation protection procedures
Describe factors affecting patient dose
Outline radiation protection considerations specific to CT
Outline dose modulation used in CT imaging
Distinguish radiation effects to organs and their tissues
Outline best practices for radiation safety

## Slide 3: CT Exposures - Generalization
CT imaging produces higher doses vs. other imaging modality procedures, partly because:
Quantum Mottle compromises image quality
  Low-contrast resolution
  Small objects are harder to image
  Thinner slices require more photons
The decision to perform a CT must be calculated using the Risk vs. Benefit model.
  (aka. Benefit must outweigh risk)
Patient’s must be aware of the risk(s)

## Slide 4: Objective 5.1
Technologists must always follow ALARA principles (As Low As Reasonably Achievable) when imaging CT patients.
This means diagnostic quality images should be obtained with the lowest dose possible for the patient
  (Aka. Balancing patient dose with image quality)
There are of radiation protection that apply to
everyone in CT:
Time – exposure to ionizing radiation should be limited
Distance – from ionizing source of radiation should be maximized
Shielding – absorbs ionizing radiation, preventing the radiation from exposing unwanted areas or persons

## Slide 5: Objective 5.2
Factors are directly controlled by the technologist, or inherently built into the scanner.
Designed to balance Image Quality & Dose
Factors you should understand:
Technique (kVp, mAs)
Collimation
Pitch
Centering
Over-ranging
Beam Geometry
Repeat Scans
Filtration
Detector Efficiency
Scan Field Diameter
Localizers
Slice Width & Spacing
Patient size & part thickness

## Slide 6: Patient Dose Considerations
Dose Distribution
In CT, the 3600 acquisition, causes patient dose to be distributed more uniformly.
Dose distribution becomes less uniform as patient thickness (and SFOV) increases
  Note: Entrance skin dose is higher than dose at the center of a patient
  Caused by: Partial Shielding

## Slide 7: Objective 5.3
ATCM: “Automatic Exposure Control” for CT scanners
Optimizes the dose to the patient while maintaining image quality regardless of patient size or tissue attenuation
Automatically adapts the mAs in both the “z” and “x-y” axis
Uses information from the scout image(s) to determine the appropriate mAs during the scan
A predefined level of image quality is established by the vendor and protocolled by the users

## Slide 8: Continued Dose Concerns
Advancements such as ATCM have reduced doses to patients, however:
New technology has also increased the number of CT clinical applications
  CT Screening procedures
  CT guided procedures
  Pediatric imaging
    Due to scan speed
These advancements have resulted in:
  More CT exams
  Increased patient doses

## Slide 9: Objective 5.4
How the 3 Cardinal Rules apply in CT:
Time:
Limit the number of scans
Adjust Pitch
Distance:
From the source of radiation (for patients)
From the patient (for technologists)
  Dose is inversely proportional to the square of the distance
Overall amount of scatter radiation in CT is low, and the distance it travels is short

## Slide 10: Shielding Considerations in CT
Patient Shielding:
Less beneficial in CT due to the amount of scatter
  Most scatter is internal & is unaffected by surface shielding
Bismuth shielding Used for anterior dose- reduction
In-plane shielding
Causes problems with ATCM
Must be outside SFOV during Scout acquisition
Lead alternative
Lead shielding
Used to enhance perception of safety
Out-of-plane shielding
Must not be in the SFOV
No effect on image quality
Must be 3600 around the patient

## Slide 11: Shielding Considerations Cont’d
Shielding the Public & Personnel:
As per the SC35:
Secondary shielding is required
  Room walls (to protect the public)
  Based on equipment not workload values
Lead shielding is required for any person who must remain in the room during scan acquisitions
  Areas of greatest radiation exposure are near the gantry aperture
  0.35mm of lead required for kVp’s of 100→150

## Slide 12: Objective 5.6
Relevant Doses
Exposure: the amount of radiation the patient is exposed to
Absorbed Dose: the amount of radiation that is absorbed by the patient
Effective Dose: used to measure the risk of partial body exposure from the equivalent whole-body dose
  Effective dose takes into account the type of radiation and the exposed tissues

## Slide 13: Important Doses to Consider
Absorbed dose is used to determine the threshold for which a deterministic effect will occur
  Measured in “Grays” (Gy)
Effective dose (Sv) is used when considering the probability
that a stochastic effect may occur
  Measured in “Sieverts” (Sv)

## Slide 14: Stochastic Effects
These effects occur by chance
The probability of an adverse effect increases with an increase in dose
There is no dose threshold
The severity of the adverse effect is not dependent on the dose (adverse effects can still happen at low doses)
Usually appear years after exposure
Examples include cancer and genetic effects

## Slide 15: Deterministic Effects
There is a dose threshold after which an adverse effect will happen
The severity of the adverse effect is related to the dose (increases in dose increase the severity of the effect)
Because there is a dose threshold, radiation protection methods are put into place to reduce the risk to patients as well as radiation workers
Examples include skin erythema, necrosis, epilation and cataracts

## Slide 16: Objective 5.7
How can we Reduce Dose in CT?
Technologists can use the following guidelines:
Appropriate patient selection
  CT referrals are reviewed by the radiologist
Limit multiphase scans (i.e., with and without contrast)
Develop protocols based on the patient’s body habitus (i.e., small, medium, & large patients)
  Using the lowest appropriate mAs
  Adjusting the Pitch when appropriate

## Slide 17: Pediatric Considerations
The law of Bergonie and Tribondeau states that the radiosensitivity of a tissue is dependent on its metabolic state
Pediatric patients are therefore more sensitive to radiation exposure because their cells are rapidly dividing
Children have a longer life expectancy than adults
  Results in a larger window for potential adverse effects to radiation exposure

## Slide 18: How can we Reduce Pediatric Dose?
Have separate protocols for pediatric CT exams
  Customize the exam
    Education plays an important role in reducing dose to pediatric patients
Use CT only when clinically indicated
  Consider using other modalities (e.g., MRI, ultrasound)
Apply ALARA Principles
  In some cases, lower resolution scans can still be diagnostic and save patient dose
  Limit the need for multiphase scans (i.e., with and without contrast)
  Consider patient shielding

## Slide 19: Things to Take Away
Relevant doses
Effects of radiation exposure
Dose distribution
Factors affecting dose/image quality
How to reduce dose
Shielding in CT
Pediatric considerations