## Slide 1: MRAD 204: Radiographic Technique 1
Outcome 1-5:
Positioning – Elbow & Humerus

## Slide 2: Affiliated Readings
Module 4
Bontrager
Pgs: 164→170
Pgs: 187→188

## Slide 3: Overview
Guidelines/Considerations
Protocols
Positioning

## Slide 4: Guidelines/Considerations - Elbow
Identify required anatomy
McQuillen Martensen 5th Ed. 224 Fig. 4.144
Elbow radiographs require ~1/3rd of the proximal forearm (to include the radial tuberosity) AND ~1/4 of the distal humerus

## Slide 5: Guidelines/Considerations - Elbow
2. Select appropriate equipment/technical factors
100cm SID, measured manually
*Elbow technique = *65→75 kVp
On the console, select:
  “free cassette”
  the projection you will begin positioning

## Slide 6: Guidelines/Considerations - Elbow
Setup room before bringing the patient in
  Note: can be done at either end of table
Ensure the table IR is not directly under the CR cassette if applicable
Tube and IR aligned using 100cm SID
Field size matches size of IR
Correct anatomical marker selected
SAIT Campus 2021

## Slide 7: Guidelines/Considerations - Elbow
3. Artifact Removal
Any clothing or objects over the distal ½ of the humerus or proximal ½ of the forearm
  Ensure the marker is NOT placed under “anatomy shadow”
Notes: when the patient is in the room:
Use external landmarks when positioning
  *Position of the elbow is determined by the epicondyles NOT the hand
  Best practice to have patient facing you
  Do NOT let the patient's legs go under the IR/table

## Slide 8: Elbow Protocol
Routine:
AP
Lateral
AP Oblique with Medial Rotation (45o)
AP Oblique with Lateral Rotation (45o)
Non-Routine:
Partial Flexion
Acute Flexion
Lateral radial head views

## Slide 9: Positioning – AP Elbow
Anderson Marker Rules

## Slide 10: Positioning – AP Elbow
*Center elbow joint over the center of the IR, to ensure all required anatomy will be on top of the IR’s active surface
CR is over the elbow “crease” (aka. Elbow joint)
Humeral epicondyles parallel to IR
Entire upper limb “flat” against IR/table surface
*At least 1/2inch of light beyond all soft-tissue*
Radiograph must include @ least 1/3rd proximal forearm & ¼ distal humerus
Marker on lateral side *note orientation*
Humerus & Forearm parallel to length of IR
Hand supinated

## Slide 11: Positioning – AP Oblique with Medial Rotation
Position the entire upper limb on the same horizontal plane
Arm fully extended
Pronate hand
Rotate arm medially until the epicondyles form a 45o angle to the IR
*Center elbow joint over the center of the IR, to ensure all required anatomy will be on top of the IR’s active surface

## Slide 12: Positioning – AP Oblique with Medial Rotation
CR is over the elbow “crease” (aka. Elbow joint)
Humeral epicondyles 450 to IR
Entire upper limb “flat” against IR/table surface
*At least 1/2inch of light beyond all soft-tissue*
Radiograph must include @ least 1/3rd proximal forearm & ¼ distal humerus
Marker on lateral side (NOT thumb side) *note orientation*
Humerus & Forearm parallel to length of IR
Hand pronated

## Slide 13: Positioning – AP Oblique with Lateral Rotation
Position the entire upper limb on the same horizontal plane
Arm fully extended
Supinate hand
Rotate arm laterally until the epicondyles form a 45o angle to the IR
*Center elbow joint over the center of the IR, to ensure all required anatomy will be on top of the IR’s active surface
Remember to change CR cassette

## Slide 14: Positioning – AP Oblique with Lateral Rotation
CR is over the elbow “crease” (aka. Elbow joint)
Humeral epicondyles 450 to IR
Entire upper limb “flat” against IR/table surface
*At least 1/2inch of light beyond all soft-tissue*
Radiograph must include @ least 1/3rd proximal forearm & ¼ distal humerus
Marker on lateral side *note orientation*
Forearm parallel to length of IR
Hand “supinated”

## Slide 15: Positioning – Lateral Elbow
Position the entire upper limb on the same horizontal plane
Rotate hand and wrist into a true lateral
Elbow flexed 90o

## Slide 16: Positioning – Lateral Elbow
CR is ~½ inch proximal and anterior to lateral epicondyle
Humeral epicondyles perpendicular to IR
Entire upper limb “flat” against IR/table surface
Radiograph must include @ least 1/3rd proximal forearm & ¼ distal humerus
Marker on anterior side *note orientation*
Elbow flexed 900 (aka. Humerus parallel to “short” edge & Forearm parallel to “long” edge of IR)
Hand & Wrist in lateral position
SAIT Campus 2021
Light-field extends:
Distally: ½ inch beyond body of ulna
Posteriorly: ½ inch beyond olecranon process

## Slide 17: Non-Routine: Partial Flexion
Bontrager pg. 165 Fig. 4.123-4.126
When the patient is unable to fully extend their arm
Humerus parallel
Forearm parallel

## Slide 18: Non-Routine: Acute Flexion
Bontrager pg. 166 Fig. 4.127-4.128 & 4.131-4.132
When flexion is greater than 90o
For distal humerus
For proximal forearm

## Slide 19: Non-Routine: Radial Head Views
Bontrager pg. 124 Fig. 4.152 & 4.153
Four images required to determine if the radius is rotating properly around the ulna
Assists in locating “occult” (hidden) fractures of the radial head and neck
Image #1: Radial Head: maximum external rotation
(aka. supinated)
Slightly anterior

## Slide 20: Non-Routine: Radial Head View
Bontrager pg. 172 Fig. 4.154 & 4.155
Image #2: Radial Head: hand lateral
Superimposed over radial shaft

## Slide 21: Non-Routine: Radial Head View
Bontrager pg. 172 Fig. 4.156 & 4.157
Image #3: Radial Head: hand pronated
Slightly posterior

## Slide 22: Non-Routine: Radial Head View
Bontrager pg. 172 Fig. 4.158 & 4.159
Image #4: Radial Head: maximum internal rotation
Posterior

## Slide 23: Guidelines/Considerations - Humerus
Identify required anatomy
Humerus radiographs require the elbow AND shoulder joint

## Slide 24: Guidelines/Considerations - Humerus
2. Select appropriate equipment/technical factors
110cm SID, measured electronically using détentes
*Humerus technique = *70→85 kVp
On the console, select:
  “Wall IR”
  the projection you will begin positioning
Wall IR

## Slide 25: Guidelines/Considerations - Humerus
Setup room before bringing the patient in
Tube and IR aligned @ 110cm SID
  Green lock: sets SID
  Blue lock: centers tube to IR laterally/medially
  Laser light: centers tube to IR superiorly/inferiorly
  Above colours may vary - site dependant
Correct anatomical marker selected
SAIT Campus 2021
Ensure the correct détente (alignment) is used
For humerus imaging: All locks must be “on” except yellow

## Slide 26: Guidelines/Considerations - Humerus
3. Artifact Removal
“Everything from the waist up”
  Tops (i.e. shirt/sweaters), bra, necklace(s), long earrings, wet or braided hair
Ensure the marker is NOT placed under “anatomy shadow”
Notes:
Upright or seated position is best
Humeral epicondyles are used as external landmarks
  i.e. position of the elbow determines position of the humerus
Patient must be asked to suspend respiration
    *Patient must be given gowning instructions*

## Slide 27: Humerus Protocol
Routine:
AP
Lateral

## Slide 28: Positioning – AP Humerus
Abduct the patient’s arm to prevent soft tissue overlap
Align collimator light to the length of required anatomy
Center the anatomy on the IR and/or in the light field
Position entire humerus & epicondyles parallel to the IR
Place an anatomical marker (using Anderson Marker Rules), and make final adjustments
https://radiopaedia.org/articles/humerus-ap-view-3?lang=us
Note: suspend respiration

## Slide 29: Positioning – AP Humerus
CR is ~mid humerus
Marker on lateral side
Humeral epicondyles parallel to IR
SAIT Campus 2021
Entire upper limb on same horizontal level
Light-field extends:
Distally: ~ ½ inch inferior to elbow joint
Proximally: ~ ½ inch superior to AC joint
Medially: ~ ½ inch medial to scapulohumeral joint
Laterally: ~ ½ inch beyond soft-tissue margins
Arm abducted, with
collimator tilted parallel to length of humerus

## Slide 30: Positioning – Lateral Humerus (mediolateral)
Turn patient to face IR
Abduct the patient’s arm to prevent soft tissue overlap
Align collimator light to length of anatomy
Position the entire humerus parallel to the IR
Ensure epicondyles are perpendicular to the IR
Flex elbow 90o
Place an anatomical marker (using Anderson Marker Rules), and make final adjustments
Note: suspend respiration

## Slide 31: Positioning – Lateral Humerus
Humeral epicondyles perpendicular to IR
Entire upper limb on same horizontal level, with elbow flexed 900
Arm abducted, with
collimator tilted parallel to length of humerus
Light-field extends:
Distally: ~ ½ inch inferior to body of ulna
Proximally: ~ ½ inch superior to AC joint
Medially: ~ ½ inch medial to scapulohumeral joint
Laterally: ~ ½ inch beyond soft-tissue margins
Central Ray is ~mid humerus
Marker on *posterior side
Note: Collimation is NOT ½ inch beyond soft-tissue = clipped anatomy