## Slide 1: MRAD 204: Radiographic Technique 1
Outcome 1-5:
Positioning – Hand & Thumb

## Slide 2: Affiliated Readings
Module 2
Bontrager
Pgs: 143→146
Pgs: 148→151

## Slide 3: Overview
Guidelines/Considerations
Protocols
Positioning

## Slide 4: Guidelines/Considerations
Bontrager pg. 150 Fig. 4.68
R
Identify required anatomy
Hand radiographs require 1’ of distal forearm
Thumb radiographs require entire trapezium
Sait Imaging Library

## Slide 5: Guidelines/Considerations
2. Select appropriate equipment & technical factors
*Always use the smallest size cassette possible for CR
Hand imaging can be done using DR or CR cassettes
    Set 3 CR cassettes aside for the exam, using 1 per image

## Slide 6: Guidelines/Considerations
2. Select appropriate equipment & technical factors
100cm SID is required
  Must be measured manually
S = source (i.e. x-ray tube)
I = IR
D = distance
55→65 kVp
SAIT Campus 2021

## Slide 7: Guidelines/Considerations
2. Select appropriate equipment & technical factors
Setup room before bringing the patient in
  Note: can be done at either end of table
Ensure the table IR is not directly under the cassette if using CR
Tube and IR aligned using 100cm SID
Field size matches size of IR
Correct anatomical marker selected
SAIT Campus 2021

## Slide 8: Guidelines/Considerations
3. Artifact removal
SAIT Imaging Library
SAIT Campus 2021
Only anatomy of interest should appear in the light field
Ensure the marker is NOT placed under “anatomy shadow”

## Slide 9: Guidelines/Considerations
Have patient sit on the stool (be aware of the wheels)
  Ensure legs are NOT under the IR
OR
SAIT Campus 2021
VS.
Note: best practice to have patient facing you

## Slide 10: Hand Protocols
Routine:
PA
PA Oblique (45º anterior oblique)
Fan lateral
By special request:
Extension lateral
Bilateral oblique hands

## Slide 11: Positioning – PA Hand
Center the anatomy on the IR and/or in the light field
Bontrager pg. 150 Fig. 4.67
Note: the anatomy is NOT centered in the light field, or on the IR 
VS.
CR is over 3rd MCP and middle of IR
*At least ½ inch of anatomy proximal to the ulnar styloid process must be over the active surface of the IR

## Slide 12: Positioning – PA Hand
Align the length of anatomy with the length of IR
VS.
SAIT Campus 2021
Wrist should also be aligned

## Slide 13: Positioning – PA Hand
Position the hand so the bones will reflect the ideal evaluation criteria
VS.
Fingers fully extended with entire palmar surface of hand, flat against IR
SAIT Campus 2021

## Slide 14: Positioning – PA Hand
Position the hand so the bones will reflect the ideal evaluation criteria
SAIT Campus 2021
No soft-tissue overlap (i.e. fingers cannot touch)

## Slide 15: Positioning – PA Hand
Use external landmarks to set an appropriate field size
Place an anatomical marker (using Anderson Marker Rules)
*At least 1/2inch of light beyond required anatomy*
Radiograph must include entire hand & 1 inch of distal forearm

## Slide 16: Positioning – PA Oblique Hand
Switch out the exposed cassette for CR, keeping the patient in the same position as the PA Hand
Immediately remove the exposed CR cassette from the room
OR
Flip the exposed CR cassette upside down, and remove just before the next exposure
Used
New

## Slide 17: Positioning – PA Oblique Hand
Rotate entire hand laterally, until the metacarpal heads form a 45o angle with the IR
SAIT Campus 2021
VS.

## Slide 18: Positioning – PA Oblique Hand
Center the anatomy on the IR and/or in the light field
VS.
Central Ray is around 3rd MCP and middle of IR
Note: the anatomy is NOT centered in the light field, or on the IR 
Bontrager Fig. 4.71
*At least ½ inch of anatomy proximal to the ulnar styloid process must be over the active surface of the IR

## Slide 19: Positioning – PA Oblique Hand
Align the length of anatomy with the length of IR
SAIT Campus 2021
VS.
Wrist should also be aligned
Bontrager Fig. 4.71

## Slide 20: Positioning – PA Oblique Hand
Position the hand so the bones will reflect the ideal evaluation criteria
VS.
SAIT Campus 2021
Ensure the phalanges remain fully extended (i.e. fingers cannot rest against IR)

## Slide 21: Positioning – PA Oblique Hand
Position the hand so the bones will reflect the ideal evaluation criteria
VS.
SAIT Campus 2021
Avoid soft-tissue overlap (i.e. should see space between finger shadows)
Bontrager Fig. 4.42
Ensure distal phalanx is not hyperextended

## Slide 22: Positioning – PA Oblique Hand
Use external landmarks to set an appropriate field size
Place an anatomical marker (using Anderson Marker Rules)
Bontrager Fig. 4.72
*At least 1/2inch of light beyond required anatomy* Pro Tip: check anatomy “shadows”
Radiograph must include entire hand & 1 inch of distal forearm
R

## Slide 23: Positioning – Lateral Hand
Switch out the exposed cassette for CR
Immediately remove the exposed CR cassette from the room
OR
Flip the exposed cassette upside down, and remove just before the next exposure
Used
New

## Slide 24: Positioning – Fan Lateral Hand
Center the anatomy on the IR and/or in the light field
Bontrager pg. 150 Fig. 4.75
Note: the anatomy is NOT centered in the light field 
VS.
Central Ray is by the 2nd MCP and middle of IR
*At least ½ inch of anatomy proximal to the ulnar styloid process must be over the active surface of the IR

## Slide 25: Positioning – Fan Lateral Hand
Align the length of anatomy with the length of IR
VS.
SAIT Campus 2021
Metacarpal heads & wrist must be aligned

## Slide 26: Positioning – Fan Lateral Hand
Position the hand so the bones will reflect the ideal evaluation criteria
SAIT Campus 2021
Metacarpal heads and styloid processes perpendicular to IR
VS.
Bontrager pg. 149 Fig. 4.71

## Slide 27: Positioning – Fan Lateral Hand
Position the hand so the bones will reflect the ideal evaluation criteria
VS.
Digits separated and parallel to IR
Bontrager pg. 151 Fig. 4.79

## Slide 28: Positioning – Fan Lateral Hand
Use external landmarks to set an appropriate field size
Place an anatomical marker (using Anderson Marker Rules)
*At least 1/2inch of light beyond required anatomy* Pro Tip: check anatomy “shadows”
Radiograph must include entire hand & 1 inch of distal forearm
Sait Imaging Library

## Slide 29: By Special Request – Extension Lateral
For foreign object or displacement
Bontrager pg. 153 Fig. 4.78
https://en.wikipedia.org/wiki/File:X-ray_of_normal_hand_by_lateral_projection.jpg

## Slide 30: By Special Request – AP Oblique Hands
The “ball-catcher’s position” assists in detecting early radiographic changes indicative of rheumatoid arthritis
Bontrager 9th Ed. pg. 154 Fig. 4.83 & 4.84

## Slide 31: Thumb Protocol
Routine:
AP
PA Oblique (45º anterior oblique)
Lateral
Adaptive:
PA

## Slide 32: Positioning – AP Thumb
Center the anatomy on the IR and/or in the light field
SAIT Campus 2021
VS.
Central Ray is over 1st MCP and middle of IR
Align the length of anatomy with the length of IR
Wrist should be aligned and flat against IR

## Slide 33: Positioning – AP Thumb
Position the hand so the bones will reflect the ideal evaluation criteria
Ensure the head of the proximal phalanx is parallel to the IR
SAIT Image Critique Handbook
Use external landmarks to set an appropriate field size
Place an anatomical marker (using Anderson Marker Rules)
*At least 1/2inch of light beyond required anatomy*
Radiograph must include entire Thumb & trapezium
SAIT Campus 2021

## Slide 34: Positioning – PA Oblique Thumb
Center the anatomy on the IR and/or in the light field
SAIT Campus 2021
VS.
CR is over 1st MCP and middle of IR
Align the length of anatomy with the length of IR
Wrist should be aligned and flat against IR
Note: curled fingers will superimpose anatomy of interest
Remember to change cassettes

## Slide 35: Positioning – PA Oblique Thumb
Position the hand so the bones will reflect the ideal evaluation criteria
Ensure the head of the proximal phalanx is 450 to the IR
SAIT Image Critique Handbook
Use external landmarks to set an appropriate field size
Place an anatomical marker (using Anderson Marker Rules)
*At least 1/2inch of light beyond required anatomy*
Radiograph must include entire Thumb & trapezium
SAIT Campus 2021
L

## Slide 36: Positioning – Lateral Thumb
Center the anatomy on the IR and/or in the light field
SAIT Campus 2021
CR is over 1st MCP and middle of IR
Align the length of anatomy with the length of IR
Wrist should be aligned and flat against IR
Remember to change cassettes

## Slide 37: Positioning – Lateral Thumb
Position the hand so the bones will reflect the ideal evaluation criteria
Ensure the head of the proximal phalanx is perpendicular to the IR
SAIT Image Critique Handbook
Use external landmarks to set an appropriate field size
Place an anatomical marker (using Anderson Marker Rules)
*At least 1/2inch of light beyond required anatomy*
Radiograph must include entire Thumb & trapezium
L