## Slide 1: MRAD 251: CT Theory 1
Outcome 2 (Part 2):
Analyze computed tomography (CT) system design and components

## Slide 2: Objective 2.4
Describe the applications of:
CT Fluoroscopy
Dual Source CT
CT Simulation
CT in Nuclear Medicine

## Slide 3: CT Fluoroscopy
“Real-time” imaging, accomplished with:
Fast continuous scanning
  Patient does not move during continuous tube rotation
Fast image reconstruction
  Applies a different interpolation algorithm than “normal” helical scan modes
  Processes 6 images/second = “real-time” reconstruction
Continuous image display
  Images are displayed on a monitor in “cine mode” (dynamic display)
  Images are reconstructed and displayed every 1/6th of a second

## Slide 4: CT Fluoroscopy Continued
Enables interventional procedures such as biopsies and abscess drainages to be performed in a CT suite.
3D localization improves accuracy and procedure success rates
Two different fluoroscopic techniques can be used (separately, or in combination during the same procedure):
Sequential CT
CTF

## Slide 5: Sequential CT
An imaging technique used for CT-guided procedures.
Uses a similar method as axial acquisitions
  Scan acquisition is completed (for image display)
  Needle is advanced
  Scan acquisition occurs again (confirms needle movement/location)
  Repeat steps 1-3 as needed
Imaging is not viewed in “real-time”
  Prevents rapid needle adjustments
Can be used to reduce personnel dose

## Slide 6: CTF
The imaging technique that enables real-time imaging.
Requires additional software
  CTF software is not standard on CT scanners
Requires additional equipment
  Irradiation foot pedal controls
Viewing monitors in the CT room
Can use intermittent scanning to reduce patient and personnel dose

## Slide 7: CTF Advantages
No lag between acquisition and reconstruction for image display
Movement will not impede localization
  Any body region can be imaged
    Example: respiratory system
  Increases procedure success rates
  Reduces repeats

## Slide 8: Dual Source CT
Created by demand for higher temporal and spatial resolution.
Increased detector rows
  Improves spatial resolution
Two tubes, detector arrays & DAS ~900 apart
  Improves temporal resolution
Sufficient amounts of data can be acquired in 1/4th of a gantry rotation
*Minimum amount of data needed for image reconstruction = 1800
  Data from both detector arrays are coordinated for image reconstruction

## Slide 9: Dual Source CT, Continued
Additional benefits:
Improved bariatric imaging
  Higher power rating, improves image quality
Dual-energy imaging techniques
  Improves accuracy of these techniques
    Example: Emphasizing the difference between bone and contrast enhanced vasculature in CTA procedures
Performance options
  Can operate with one source or both

## Slide 10: CT Simulation
A specialized CT scanner used in radiation oncology department(s).
Assists with the radiation treatment planning process
Three primary steps:
Patient scanning
Treatment planning & CT Simulation
  CT Simulation results are used to setup the patient in the treatment machine
Treatment setup
  Patient is positioned in the treatment machine

## Slide 11: CT Simulation Equipment
Primary components are similar to general use CT scanners.
Main differences:
  Flat tabletop with immobilization devices
  Larger gantry aperture
  Registration software
    Enables image fusion
  Virtual Simulation software
Patients must be scanned in exactly the same position as they would be on the radiation treatment machine

## Slide 12: Nuclear Medicine
Relatively non-invasive method of gathering metabolic information.
Images function as opposed to anatomical information
  Aka. Physiological diagnostic information
Accomplished using radioactive tracers
  Images are formed using the radiation emitted from predicted anatomical locations
  Metabolic function is determined by radiation intensity; pathologies can be demonstrated as:
    Hot spots = areas of increased uptake
    Cold spots = areas of decreased uptake

## Slide 13: Radiopharmaceuticals
Preparation of radiopharmaceuticals occurs in a Radiopharmacy.
There are two components:
Non-radioactive drug portion
  Determines localization in the body
Radioactive isotope
  Allows for detection by the cameras

## Slide 14: Nuclear Medicine Scanners
SPECT (Single Photon Emission Computed Tomography)
Images acquired as cameras/detectors rotate around the patient
Images are reformatted via
  Back projection or iterative techniques
  Very similar to CT image reconstruction techniques

## Slide 15: Nuclear Medicine Scanners
PET (Positron Emission Tomography)
Differs from SPECT imaging:
  β+ emitters
    Annihilation photons (high energy gamma rays) are captured for data analysis
  Requires a cyclotron in close proximity
    Radiotracers have a very short half life
  Radiopharmaceuticals have biological significance (Nitrogen, Fluorine,
Oxygen and Carbon)
  FDG
    Most common radiotracer used

## Slide 16: SPECT vs. PET
Advantages of SPECT:
Less space & consumables
  No Cyclotron required
Decreased operating costs
Not limited to positron emission detection
  However does require the use of septa
Diagnostic CT scanner is not required
  CT is only for the purposes of attenuation correction

## Slide 17: CT in Nuclear Medicine
CT provides anatomical detail used to identify pathology that affects the shape of body structures.
Unable to distinguish malignant vs benign pathologies via visualization of structures
  Aka. form
Nuclear Medicine imaging enables early detection of disease, and assists in differentiating pathologies.
PET (positron emission tomography) provides metabolic detail
  Aka. function

## Slide 18: CT in Nuclear Medicine
Combining CT with SPECT & PET imaging enables image fusion.
Image fusion is more accurate when equipment is combined
  Gantry tilt is disabled when equipment is combined
Creates overlapping of anatomic detail with functional data
  Provides anatomical localization of the hot or cold spots identified on the nuclear medicine scan

## Slide 19: PET
Firstly, a CT scan is completed, then the PET scan follows.
“Head to toe” in the CT scanner
“Toe to head” through the PET scan
Benefits of the CT Scan:
Provides an anatomic image that aligns perfectly with the functional image of the PET scan
Can be transformed into an attenuation map for correcting the PET images

## Slide 20: Using CT with Nuclear Medicine
The exponential attenuation law:
  A beam of photons will be attenuated as it travels through a given medium and a given thickness
Lower detection efficiency of gamma rays
CT is one of the methods utilized to determine patient specific attenuation correction factors

## Slide 21: Localization
The increase in photon flux and decreased noise factor demonstrated by CT has led to it being the method of choice for attenuation correction
The CT transmission scan acquired is non-diagnostic
  Enables correlation of anatomical information with the functional information of the nuclear medicine scan

## Slide 22: CT in Nuc. Med. Considerations
Diagnostic efficacy can be compromised due to:
Imaging defects caused by prior scans that compromise image quality (attenuation artifacts)
  Example: barium studies (48hrs)
Inappropriate patient preparation that could affect normal metabolic processes
  Example: not fasting, and/or taking medications
Ineffectively directing patients
  Could cause motion artifacts
Insufficient patient history
  Benign pathologies can visually imitate malignancy

## Slide 23: Things to take away
The difference between:
CTF
Sequential CT
Purpose of dual source CT
How CT Simulation equipment differs from “general” CT scanners
The evaluative difference between:
  Nuclear medicine
  CT
Benefits of PET/CT (hybrid imaging)