## Slide 1: APPH 226: Line Focus Principle and The Anode Heel Effect
Objective: 1.5

## Slide 2: Line Focus Principle
States that: by angling the face of the anode target, a large actual focal spot size can be maintained, and a small effective focal spot can be created
Relationship between the actual and effective focal spot

## Slide 3: Line Focus Principle
Allows for a larger area for heating while maintaining a small focal spot
  Achieved by angling the target
Focal spot is:
  The area of the target where x-rays are emitted
  Actual x-ray source

## Slide 4: Actual Focal Spot
Area of the target that is actually bombarded with filament electrons
Size of the electron stream is determined by the filament size selected
Ideal for this area to be as large as possible for better heat distribution
  The smaller the electron stream is, the greater the heat produced in a small area
    Better to have the heat spread out over a larger area

## Slide 5: Actual and Effective Focal Spot Size
Direct relationship
The smaller the actual focal spot, the smaller the effective focal spot size
The larger the actual focal spot, the larger the effective focal spot size
Large actual focal spot will have less heat on the anode, than a small focal spot
  Same quantity of photons over a larger area vs. a smaller area

## Slide 6: Effective Focal Spot
Origin of the x-ray beam
X-ray beam area as seen from the patient’s perspective
When specifying focal spot sizes, this is the focal spot that is being identified
The smaller the area, the sharper the image will be
For the best image quality, it is desirable to keep this as small as possible

## Slide 7: Effective Focal Spot
Controlled by actual focal spot, which is controlled by:
  Filament length
  Target angle
  Charge on the focusing cup
  Depth of filament in focusing cup
  Dimensions and shape of focusing cup

## Slide 8: Limitations
Line Focus Principle achieves goal to balance heat area and effective focal spot size, but with trade offs
The target angle should be as small as possible, right?
  No….If the target angle is too small:
    X-ray beam area (field size) may be too small to effectively image all required anatomy
    Useful beam will be too narrow

## Slide 9: With the good…comes the bad…
Anode Heel Effect is
  affected by the line focus principle
  Intensity of radiation on the cathode side of the x-ray field is greater than that on the anode side

## Slide 10: Anode Heel Effect
How does this happen?
The ‘heel’ of the target is in the path of the beam
  As electrons bombard the target, x-rays are produced and emitted at angles between 45-90° in the direction of electron travel
X-rays on the anode side must first penetrate a portion of the target before exiting the tube
  Loss of x-ray photons
  Loss of energy

## Slide 11: Anode Heel Effect
Intensity of x-rays that are emitted through the ‘heel’ are reduced due to:
  Longer path to travel
  Increased absorption
This is the anode heel effect

## Slide 12: Radiation Intensity
As a result of the anode heel effect, the useful beam will have a variation of radiation intensity
Central Ray is the imaginary center most x-ray in the beam
Designated as 100% radiation intensity
Cathode side has higher intensity
Anode side has lower intensity

## Slide 13: Working with the Anode Heel Effect
When imaging areas with great differences in thickness or mass density, need to be conscientious of the Anode Heel Effect
Cathode and anode are clearly indicated on the tube housing
In general, when possible:
  Position the cathode over the thicker part of the anatomy to produce more uniform exposure on the image receptor
    E.g. Femur, Thoracic spine
  Designated ‘head end’ of the table

## Slide 14: Readings
Radiologic Science for Technologists 11th Edition
  Pg 113-116