## Slide 1: MRAD 204: Radiographic Technique 1
Outcome 6-10:
Positioning – Pelvis & Hip

## Slide 2: Affiliated Readings
Module Reading
Bontrager
Pgs: 281, 283→286
Pgs: 288→290

## Slide 3: Overview
Guidelines/Considerations
Protocols
Positioning

## Slide 4: Guidelines/Considerations - Pelvis
Identify required anatomy
Pelvic radiographs require the entire pelvis AND both trochanters of the proximal femurs
McQuillen Martensen 5th Ed. Pg.430 Fig. 7.4
R

## Slide 5: Guidelines/Considerations - Pelvis
2. Select appropriate equipment/technical factors
*Using the smallest field size possible, collimation
110cm SID, measured electronically using détentes (i.e. blue lock must be engaged)
Pelvis technique = 80→90 kVp
On the console, select:
  “Table IR”
  AP Pelvis

## Slide 6: Guidelines/Considerations - Pelvis
Setup room before bringing the patient in
Tube and IR aligned @ 110cm SID
  Lock(s): centers tube to IR laterally/medially
  Laser light: centers tube to IR superiorly/inferiorly
Correct anatomical marker selected
Patient drape/sheet cover ready for use
Ensure IR is covered completely prior to patient mount/dismount
For table imaging: All locks must be on
*Locks engaged

## Slide 7: Guidelines/Considerations - Pelvis
3. Artifact Removal
Any clothing or objects between the waist to the knees
  Marker placed under soft-tissue anatomy shadow
Notes: when the patient is in the room:
Use external landmarks when positioning
  *Bilateral ASIS must be palpated, to ensure:
    No patient tilt (i.e. midsagittal plane parallel to lateral edge of IR)
    No patient rotation (i.e. midcoronal plane parallel to anterior surface of IR)
Never rotate a leg medially, if you suspect a fracture!

## Slide 8: Guidelines/Considerations - Pelvis
For AP Pelvis Projections:
Make note of the relationship between these topographic landmarks:
Top of Crest
ASIS
Inferior edge of greater trochanter

## Slide 9: Pelvis Protocol
Routine:
AP
Non-Routine/Special Request:
AP Axial Inlet & Outlet
AP Oblique’s (for acetabulum) – aka. Judet

## Slide 10: Positioning – AP Pelvis
Ensure the patient is lying straight on the table (hips & shoulders parallel to long edge of table)
Use patient draping/sheet cover
ASIS’s should be level
Center anatomy in light-field
Lower limbs must be rotated 15-20o unless contraindicated
Place an anatomical marker (using Anderson Marker Rules), and make final adjustments
Bontrager pg. 281 (inset) Fig. 7.44
Note: Check for Diverging rays! Light-fields on patient’s are smaller than they appear radiographically.
Note: suspend respiration

## Slide 11: Positioning – AP Pelvis: Supine
Note: Check for Diverging rays!
Light-fields on patient’s are smaller than they appear radiographically.
Lengthwise crosshair over MSP
(aka. ½ between the ASIS’s)
“Top” of light-field on IR
½ inch above top of crests
“Bottom” of light field on the IR 1-inch below inferior edge of greater trochanters
CR located around ASIS
Lower Limbs internally rotated 15-200
Marker between ASIS & greater trochanter laterally

## Slide 12: Non-Routine: AP Axial Inlet
Angle CR 40° degrees caudad
Center around level of ASIS
CR parallel to body of pubis
Ischial spines demonstrated
Bontrager pg. 284 Fig. 7.52 & 7.53

## Slide 13: Non-Routine: AP Axial Outlet
Angle CR ~35° degrees cephalad
  *CR cephalad 20→350 = males & 30→450 = females
Center ~1→2inches distal to symphsis pubis
CR perpendicular to body of pubis
Pubic & Ischial bones demonstrated
Bontrager pg. 283 Fig. 7.49 & 7.50 & Bontrager 9th Ed pg. 281 Fig. 7.50

## Slide 14: Non-Routine: AP Oblique's (45o post. Obl. Judet views)
Taken to visualize acetabular rims
RPO and LPO always done together
  i.e. 2 views of each side
Bontrager pg. 285 Fig. 7.55 & 7.56

## Slide 15: Positioning – RPO (“Right” Downside Acetabulum)
anterior rim
Demonstrates:
Posterior (ilioischial) column
Illiac wing (or ala)
Aka. External Oblique
Bontrager pg. 285-286 Fig. 7.55, 7.58 & 7.62

## Slide 16: Positioning – LPO (“Right” Upside Acetabulum)
posterior rim
Demonstrates:
Anterior (ilioipubic) column
Obturator foramen
Aka. Internal Oblique
Bontrager pg. 285-286 Fig. 7.56, 7.60 & 7.61

## Slide 17: Guidelines/Considerations - Hip
Identify required anatomy
AP Hip radiographs require 1/3rd of proximal femur, symphysis pubis & body of the ilium
McQuillen Martensen 5th Ed. Pg.440 Fig. 7.34
R
Bontrager pg. 290 Fig. 7.73
L
*Note: if present, entire ORIF must be included (i.e. field size will need to be extended for patients with long hip pins)
Lateral Hip radiographs require 1/3rd of proximal femur, and surrounding pubis, ischium & ilium

## Slide 18: Guidelines/Considerations - Hip
2 & 3. Same as Pelvis except:
Hip technique = 80→85 kVp
*Axiolateral’s = 80→95kVp
Remember:
Never rotate a leg medially, if you suspect a fracture!
Bontrager pg. 274 Fig. 7.31

## Slide 19: Protocol - Hip
Routine:
AP
Lateral (Lauenstein-Hickey Method) *Note 2: Bontrager pg. 290
Non-Routine:
Frog-leg (Modified Cleaves Method)
Adaptive Projections:
Axiolateral inferosuperior/x-table (Danelius-Miller)
Modified Axiolateral (Clements-Nakayama)

## Slide 20: Positioning – AP Hip
Bontrager pg. 274 Fig. 7.27 & SAIT Campus 2021
Apply patient draping
Ensure affected leg is parallel to long edge of table
ASIS’s should be level (*i.e. ensure no patient tilt or rotation)
Leg rotated 15-20º medially unless contraindicated
Place an anatomical marker (using Anderson Marker Rules), and make final adjustments
Note: suspend respiration

## Slide 21: Positioning – AP Hip
McQuillen Martensen 5th Ed. pg. 438Fig. 7.26
Lengthwise crosshair around middle of knee
CR should be located around femoral neck
“Top” of light-field on patient at ASIS
“Bottom” of light-field around 1/3rd of proximal femur
Lower Limb internally rotated 15-200
Marker on inferior-lateral corner
Medial edge of light-field @ symphysis

## Slide 22: Positioning – Lateral Hip (Lauenstein-Hickey)
Bontrager 9th Ed. pg. 287 Fig. 7.71
Flex the knee
Twist collimator head until light-field is parallel to length of
femur
Float table to center the crosshairs over the femoral neck
Place an anatomical marker (using Anderson Marker Rules), and make final adjustments
Ensure patient is “straight”
on the table
Ask patient to move to the
edge of the table (away from
side of interest)
Roll patient towards affected
side, and place a 45o
sponge under their hips &
shoulders
Note: suspend respiration
Flexing the knee & abducting the femur until it is “flat” against the table top ensures the proximal femur will be parallel to the IR

## Slide 23: Positioning – Lateral Hip (Lauenstein-Hickey)
Lengthwise crosshair around middle of knee
CR should be located around femoral neck
“Top” of light field around upside ASIS
“Bottom” of light field around 1/3rd of proximal femur
Bontrager 9th Ed. pg. 287 Fig. 7.71
Collimate side-side to width of bony anatomy of the knee
Twist collimator to match angle of femur
Marker on inferior-lateral corner

## Slide 24: Non-Routine: Frog-leg (Modified Cleaves Method)
Bontrager 8th ED Fig. 7.48
McQuillen Martensen 5th Ed. pg. 433,434 & 442 Fig. 7.13, 7.14 & 7.36
Femoral neck only partially foreshortened & Lesser Trochanter in profile medially
Same positioning as Lauenstein-Hickey except:
No rotation onto affected side (aka. proximal femur NOT parallel to IR)

## Slide 25: Adaptive – Axiolateral (x-table) Danelius-Miller
Bontrager pg. 289 Fig. 7.69-7.71
Aka. inferosuperior
Flex unaffected leg and place on a support that will not interfere with the CR
CR perpendicular to femoral neck & IR
Place patient’s arms high above chest

## Slide 26: Adaptive – Modified Axiolateral (Clements-Nakayama)
Bontrager pg. 291 Fig. 7.75 & 7.77
Used in trauma situations when both legs are affected, or the unaffected leg cannot be moved effectively