## Slide 1: APPH 226: Screens, IR speeds, Characteristic Curves
Objectives: 4.1, 4.2, 4.3, 6.1

## Slide 2: Where it all began
Digital radiography was developed based on film-screen radiography
Primary purpose of radiographic imaging is:
  Transfer information from the x-ray beam to the eye
  After the x-ray beam passes through matter, the image-forming x-rays need to be captured and transferred to a form that can be visualized by the human eye
  Examples of appropriate mediums
    Film, fluoroscopic image intensifier, TV/flat panel monitor, laser imaging system, solid state detectors

## Slide 3: Film
Construction and characteristics of radiographic film are similar to that of photographic film
Radiographic film is manufactured with extremely high quality control, and low threshold acceptance limits
  Slightest bit of contaminant would affect the films ability to reproduce information from the x-ray beam

## Slide 4: Film Construction
  Foundation of the film
  Polyester or plastic – flexible
    Much thicker than that of photographic film
  Emulsion is fragile, need this base so that film can be handled and processed
    Allows us to handle films
  Lucent
  Blue dye/tint added to reduce strain

## Slide 5: Film Construction
  Radiation sensitive and light-sensitive layer: function
  Silver halide crystals suspended in gelatin
    silver bromide (AgBr) and silver iodide (AgI)
    ~ 90-99% AgBr and 1-10% AgI
    About half a billion crystals per cubic mm of film
X-ray film has emulsion on both sides
Some specialty films only have an emulsion on one side.
  Less sensitive to radiation but very precise
  Example: mammography film

## Slide 6: Film Construction
Adhesive Layer /Substratum
  This is between the emulsion and base layer
  Holds the layers together
  Essentially the ‘glue’ that holds the film together
Supercoat/ overcoat
  Durable protective layer – made of hard gelatin
  Purpose to protect and prevent damage to the sensitive emulsion layer beneath it
  Paper clips and staples will tear it no problem

## Slide 7: Latent Image Formation
The image that exists on the film after exposure, but before processing
Invisible change in the silver halide crystal
  Radiation activated and inactivated crystals make up the latent image
Film processing changes the latent image into a manifest image (visible image)

## Slide 8: Types of Film
Direct Exposure Film
  Aka nonscreen film
  Used in a cardboard holder, instead of a cassette
  Single emulsion – thicker than screen film, requires more development time
    Requires more exposure also
Specialty film
  Duplicating/copy film
    Already exposed to maximum OD
    Behaves opposite to normal (solarization)
    Notch in a corner

## Slide 9: Screen Film
Most widely used radiographic film
  Used with one or two intensifying screens
  More light sensitive, less sensitive to x-rays
Can be single or double emulsion
  Double
    typically used in radiographic imaging
  Single
    Single intensifying screen
    Uses – e.g. duplication, subtraction, mammography

## Slide 10: Cassettes
Container for intensifying screens and film
Must be
  Light-proof
  Portable
  Maintain good film-screen contact
  Rigid enough not to bend under patient’s weight, but allow maximum radiation to pass through to screen
    Front layer made of low x-ray absorbing material
      E.g. Bakelite, magnesium, graphite carbon
    Back layer must absorb backscatter before it exposes film
      E.g. thin sheet of lead foil

## Slide 11: Intensifying Screens
Device found in radiographic cassettes containing phosphors that convert x-rays into light
  Light then exposes the radiographic film
Phosphors are a chemical compound that emits visible light when struck by radiation

## Slide 12: Intensifying Screens
  Less mAs required to obtain exposure in comparison to non screen film
Using film alone, much higher doses required in order to achieve diagnostic images
Less than 1% of x-rays incident on film will interact and contribute to the latent image.
  Meaning large amounts of x-rays required to achieve the proper radiographic density

## Slide 13: Intensifying Screens
‘Intensifies’ the energy to which film is exposed
  Without screens, 100% of energy reaching film would have to be from x-rays
  With screens, 90-99% of energy reaching film would be light, and 1-10% would be from x-rays
Pros
  Less dose to patient
  Shorter exposure times
Cons
  Recorded detail reduced on image, increased blur

## Slide 14: Intensifying Screens
Reflective Layer
  Between phosphor and base
  Shiny substance: magnesium oxide or titanium dioxide
  Light emits isotropically from phosphor
  Redirects light towards the film to enhance efficiency
Base
  Farthest from film
  Mechanical support for the phosphor layer
  Usually made up of polyester

## Slide 15: Intensifying Screens
Protective Coating
  Closest to the film
  Helps to protect the active layer of the screen
  Allows us to handle the screen
  Transparent
Phosphor Layer
  Active layer that converts x-rays into light
  Used to be calcium tungstate, now we use rare earth elements : gadolinium, lanthanum and yttrium
    Faster , lower patient dose, smaller load on tube

## Slide 16: Phosphor Layer
Active layer of screen
Emits light when x-rays hit it
Concepts of luminescence are used in DR/CR
Important characteristics:
  DQE – Detective Quantum Efficiency
    % of x-rays absorbed by screen
    High atomic number is important
  CE – Conversion Efficiency
    Amount of light emitted for each x-ray absorbed

## Slide 17: Luminescence
A material that will emit light in response to external stimulation
  Luminescent material or phosphor
Two types
  Fluorescence
    Light is emitted only while being stimulated
  Phosphorescence
    Light continues to be emitted after stimulation

## Slide 18: Luminescence
Similar to characteristic radiation
When stimulated, outer shell electrons get excited and leave shell
When they return back to the shell, energy emitted is a light photon
Light emitted is of a characteristic color

## Slide 19: Spectral Matching
Major consideration when selecting screens and films
Film sensitivity must be properly matched to the spectrum of light emitted by the screen
e.g green sensitive film, green emitting screens
If mismatched, the “IR speed” is greatly reduced resulting in:
  increased exposure time/techniques
  increased patient dose

## Slide 20: Phosphors and the Image
Most of the screen imaging characteristics are due to the phosphor composition
  Material composition
  Thickness of layer
  Concentration
  Size
  Dye

## Slide 21: Phosphors and the Image
Material Composition
  Efficiency – calcium tungstate vs rare earth
  Calcium tungstate ~5% of x-rays into light
  Rare earth ~20% of x-rays into light
Thickness of the Layer
  The thicker the layer, increases DQE
  High speed screen has thicker layer
Concentration
  Higher crystal concentration
  Higher screen speed

## Slide 22: Phosphors and the Image
Size of Phosphor
  The larger the phosphor, the more light produced per x-ray interaction
  Higher screen speed
Dye
  Light absorbing dye is added to some phosphors
  Helps control light spread
  Reduces speed

## Slide 23: Intensification Factor (IF)
Screens are used to decrease patient dose
Magnitude of dose reduction
  How much did the dose decrease after using the screen?
Information about patient dose from intensification factor.
IF = Exposure without screen
Exposure with screen

## Slide 24: Screen Speeds
Identified by relative speed (RS) expressed numerically
Can range from 50-1200
Describes efficiency of x-ray conversion
  X-rays into light
Calcium tungstate used as basis of comparison
  Assigned value is 100
  High speed rare earth screens – up to 1200
  Detail – 50-80

## Slide 25: What affects the screen speed?
Ultimately, the speed is determined by the number of x-rays interacting with the phosphor and how efficiently x-ray energy is converted into visible light
  Some factors are controlled by tech, but many are controlled by manufacturer
  A faster screen produces more light than a slower screen

## Slide 26: Speed Factors – Uncontrolled
These are the factors we can’t control
  Phosphor composition
  Phosphor thickness
  Reflective layer
  Dye in phosphor layer
  Crystal size
  Crystal concentration

## Slide 27: Screen speed will increase with:
  Type of phosphors – rare earth
  Thicker layer
  Reflective layer
  No dye
  Larger crystal size
  More crystals (higher concentration)
  *listed in relative order of importance

## Slide 28: With high speed comes
Decreased image quality
  Image blur
    Phosphor size
    Thickness of layer
  Image noise

## Slide 29: Image Blur
When x-rays interact with phosphors, the area of the film/IR activated by the light is larger than it would be with direct x-ray exposure
  Reduced spatial resolution and increased image blur
  For the most part, conditions that increase the IF reduces spatial resolution
    Large phosphor size
    Thicker layer

## Slide 30: Quantum Mottle
Aka, noise
Appears splotchy, mottled, grainy
Occurs when:
  Very few photons required by the screens to produce an image of appropriate radiographic density
    Not enough photons producing the image
  High speed system requiring very short exposure

## Slide 31: DQE vs CE
DQE: Detective quantum efficiency
the percentage of x-rays absorbed by the screen
CE: Conversion efficiency
the quantity of light emitted for each x-ray absorbed
Increasing CE will increase image noise, but an increase in DQE will not
  With increased CE, fewer x-rays are needed

## Slide 32: Quantum Mottle
What does this mean for image quality?
  Decreases it!
  Limits diagnostic value of image
How do we reduce it?
  Need more x-ray photons to produce image
    Need to increase mAs (quantity)
    Use slower speed system
    Decrease kVp, increase mAs (use the rules for maintenance!)

## Slide 33: Speed Factors- Controllable
These are the factors that we can control
  Radiation Quality
    If kVp is high, IF will be higher due to increased probability of light producing interactions within the phosphors
  Processing
    Mostly to do with film processing and film development
  Temperature
    External environment
    Higher Intensification Factor at low temp vs high temp

## Slide 34: Digital and Speeds
Essentially the same concept
It is the efficiency of x-ray conversion
However, instead of using film, it’s the digital detector component
Same scale
  the higher the speed, the less exposure needed
  The lower the speed, the more exposure needed

## Slide 35: Screen Care
Handle with care
Scratches can produce artifacts and degrade the image
  Often fingernails, edges/corners of film
When loading cassettes, don’t slide the film in
Remove film by tipping open cassette
Do not leave cassettes open
Should only be handled when necessary
  Only cleaned as needed
With proper care, screens can last forever, phosphors do not get worn out

## Slide 36: Characteristic Curve
Sensitometry
  Two principal measurements
    Exposure to the film
    Percentage of light transmitted (OD)
The relationship between optical density (OD) and radiation exposure.
  Called a characteristic curve.
  H & D curve (Hurter and Driffield)
  Sensitometric Curve

## Slide 37: Characteristic Curve
Toe and Shoulder
  High and low exposure levels
  Large variations in exposure produce only small changes in OD
Straight line portion
  In between the toe and shoulder
  This is where a properly exposed radiograph appears
  This is the ideal density range

## Slide 38: Constructing a Curve
Need two pieces of Equipment
Densitometer
  To measure the densities
Sensitometer or Penetrometer (Step Wedge)
  This produces the range of different densities

## Slide 39: Constructing a Curve
The film is exposed to visible light with the sensitometer
Processed film is analyzed/measured with densitometer
Data is recorded and analyzed
Data is plotted, into the characteristic curve

## Slide 40: Characteristic Curve
Exposure values for a characteristic curve are presented in a logarithmic fashion
It is the change in OD over each exposure interval that is of interest
The x-axis is log relative exposure (LRE)
The y-axis is optical density

## Slide 41: Optical Density
OD is a logarithmic function
Meaning – it is a small number that actually represents a wide range of values
Remember, OD numbers correspond to clear and black
Useful range is 0.25-2.5 OD

## Slide 42: Film
Unexposed film will always have an OD
This is because of the base plus fog
  Base – color added to the film base
  Fog – any exposure during storage, contamination, processing

## Slide 43: Purpose
The characteristic curve can show the relative degree of contrast of an image receptor at a glance
Slope/steepness of the straight line portion
Characteristic curve = 1, angled at 45 degrees

## Slide 44: Contrast
Contrast = 1
  Very low contrast
Contrast = 3
  High contrast
  Subject contrast would be amplified
  Remember, one to the right, will result in a height of 3
  Very large OD differences with a small range of exposure

## Slide 45: Gradient
Slope of the tangent at any point on the characteristic curve
Toe gradient
  More important than average gradient, because many clinical ODs appear in this region
Shoulder Gradient
  Important in mammography, as most of their clinical ODs are in that region

## Slide 46: Mid Gradient
Slope of the line drawn between the points corresponding to OD 0.25-2 above base and fog densities
This is the approximate useful range of OD on most radiographs
Average gradient usually between 2.5-3.5

## Slide 47: Latitude
Refers to the range of exposures over which the image receptor responds with ODs in the diagnostically useful range
Sometimes thought of as the margin of error
Wider latitude – mAs can vary more
  Lower contrast
Narrow latitude – less variation of mAs
  Higher contrast

## Slide 48: Speed
Defined as the ability of an image receptor to respond to an x-ray exposure
Also called measure of sensitivity
Characteristic curve can be used to identify speed
Speed < 100 = detail IRs
Speed > 100 = fast/high speed IRs

## Slide 49: Changing Speeds
When you change speeds, a change in mAs settings will be necessary to maintain the same OD
  E.g. if the speed is doubled, the mAs must be halved

## Slide 50: Speeds
Image receptor speeds affects:
  Radiation sensitivity/response
  Radiographic Density
  Patient Dose

## Slide 51: Limitations of Film (Analog)
Limited dynamic range (the range of exposure intensities that an image receptor can accurately detect)
Cost
Time
Film processors – equipment and maintenance costs
  Frequent quality control procedures
Processed film is permanent, no adjustments can be made
Cannot be electronically stored or duplicated
Additional expense of storing radiographs and retrieving them
Notes:   Limited dynamic range (the range of exposure intensities that an image receptor can accurately detect)
  Dynamic range – Very sensitive to over or under exposure
  More repeats
  Restricts visibility of structures (soft tissue and bone)
-may need to take two images, one to see soft tissue, one to see bone, difficult to image both on one image

## Slide 52: Digital Radiography
Uses storage phosphors to temporarily store energy representing the image signal
Phosphor then undergoes a process to extract the latent image
DR (Direct radiography) system utilizes detectors that directly capture and read out the electronic image signal
CR (Computed radiography) uses phosphors within a cassette

## Slide 53: Readings
Radiologic Science for Technologists 11th Ed
  Pp. 163-172 (Stop before “Film processing”)
  Pg 208-213 (Stop before “Handling & Storage of Film”)
  Pg 214- 226 (Start at “Formation of the Latent Image’. Stop before “Film Processing)